JPL Publication 97-4

Chemical Kinetics and Photochemical Data

for Use in Stratospheric Modeling

Evaluation Number 12

(Part 2 of 2 Parts)

NASA Panel for Data Evaluation:

W. B. DeMore	C. J. Howard

S. P. Sander	A. R. Ravishankara

Jet Propulsion Laboratory	NOAA Environmental Research Laboratory

D. M. Golden	C. E. Kolb

SRI International	Aerodyne Research Inc.

R. F. Hampson	M. J. Molina

M. J. Kurylo	Massachusetts Institute of Technology

National Institute of Standards and Technology

January 15, 1997

NASA

National Aeronautics and

Space Administration

Jet Propulsion Laboratory

California Institute of Technology

Pasadena, California

(Continued from Part 1)

## PHOTOCHEMICAL DATA

### Discussion of Format and Error Estimates

In Table 4 we present a list of photochemical reactions considered to be of stratospheric interest.  The absorption cross sections of O2 and O3 largely determine the extent of penetration of solar radiation into the stratosphere and troposphere.  Some comments and references to these cross sections are presented in the text, but only a sample of the data is listed here.  (See, for example, WMO Report No. 11 [1]; WMO Report No. 16 [330])  The photodissociation of NO in the O2 Schumann-Runge band spectral range is another important process requiring special treatment and is not discussed in this evaluation (see, for example, Frederick and Hudson [92]; Allen and Frederick [3];  WMO Report No. 11 [1], and Minschwaner and Siskind [195]).

For some other species having highly structured spectra, such as CS2 and SO2, some comments are given in the text, but the photochemical data are not presented.  The species CH2O, NO2, NO3, ClO, BrO, and OClO also have complicated spectra, but in view of their importance for atmospheric chemistry a sample of the data is presented in the evaluation; for more detailed information on their high-resolution spectra and temperature dependence, the reader is referred to the original literature.

Table 5 gives recommended reliability factors for some of the more important photochemical reactions.  These factors represent the combined uncertainty in cross sections and quantum yields, taking into consideration the atmospherically important wavelength regions, and they refer to the total dissociation rate regardless of product identity.  The exception is O(1D) production from photolysis of O3: the reliability factor applies to the quantum yield at the indicated wavelengths.

The error estimates are not rigorous numbers resulting from a detailed error propagation analysis of statistical manipulations of the different sets of literature values; they merely represent a consensus among the panel members as to the reliability of the data for atmospheric photodissociation calculations, taking into account the difficulty of the measurements, the agreement among the results reported by various groups, etc.

The absorption cross sections are defined by the following expression of Beer's Law:

I = Ioexp(-nl),

where Io and I are the incident and transmitted light intensity, respectively;  is the absorption cross section in cm2 molecule-1; n is the concentration in molecule cm-3; and l is the pathlength in cm.  The cross sections are room temperature values at the specific wavelengths listed in the table, and the expected photodissociation quantum yields are unity, unless otherwise stated.

###### Table 4.  Photochemical Reactions

_______________________________________________________________________

&	O2 + h O + O

&	O3 + h O2 + O

*	O3 + h O2 + O(1D)

HO2 + h products

H2O + h H + OH

H2O2 + h OH + OH

NO + h N + O

&	NO2 + h NO + O

*	NO3 + h products

N2O + h N2 + O(1D)

N2O5 + h products

NH3 + h NH2 + H	(1)

HONO + h OH + NO

*	HNO3 + h OH + NO2

HO2NO2 + h products

CO + h C + O	(1)

CO2 + h CO + O	(1)

CH4 + h products	(2)

CH2O  products

&	CH3O2 + h products

&	C2H5O2 + h products

CH3OOH + h products

#	CH3C(O)O2NO2 + h products

HCN + h products

CH3CN + h products

Cl2 + h Cl + Cl

ClO + h Cl + O

ClOO + h products

&	OClO + h O + ClO

&	ClO3 + h products

&	Cl2O + h products

&	Cl2O2 + h products

*	Cl2O3 + h products

Cl2O4 + h products

Cl2O6 + h products

HCl + + h H + Cl

HF + h H + F

&	HOCl + h OH + Cl

ClNO + h Cl + NO

#	FNO + hF+ NO

ClNO2 + h products

ClONO + h products

*	ClONO2 + h products

CCl4 + h products

CCl3F + h products

CCl2F2 + h products

CF2ClCFCl2 + h products

CF2ClCF2Cl + h products

CF3CF2Cl + h products

CF4 + h products

C2F6 + h products

CCl2O + h products

CClFO + h products

CF2O + h products

#	CF3OH + h products

CH3Cl + h products

CH3CCl3 + h products

CHClF2 + h products

CH3CF2Cl + h products

CF3CHCl2 + h products

CF3CHFCl + h products

CH3CFCl2 + h products

CF3CF2CHCl2 + h products

CF2ClCF2CHFCl + h products

#	CH3OCl + h products

BrO + h products

#	HOBr + h products

*	BrONO2 + h products

#	BrCl + h Br + Cl

CH3Br + h products

CHBr3 + h products

&	CF3Br + h products

&	CF2Br2 + h products

&	CF2BrCF2Br + h products

&	CF2ClBr + h products

CF3I + h CF3 +I

SO2 + h SO + O

H2S + h HS + H	(1)

CS2+ h CS + S

OCS + h CO + S

SF6 + h products

NaOH + h Na + OH

NaCl + h Na + Cl

______________________________________________________________________

(1)	Hudson and Kieffer [132].

(2)	Turco [305].

#	New Entry.

*	Indicates a change in the recommendation from the previous evaluation.

&	Indicates a change in the note.

###### Table 5.  Combined Uncertainties for Cross Sections and Quantum Yields

| Species | Uncertainty |  |
| --- | --- | --- |
| O2 (Schumann-Runge bands) | 1.2 |  |
| O2 (Continua) | 1.2 |  |
| O3 (Cross Sections Only) | 1.1 |  |
| O3  O(1D),  >310 nm | 1.3 |  |
| O3  O(1D), 290 < < 310 nm | 1.2 |  |
| H2O2 | 1.3 |  |
| NO2 | 1.2 |  |
| NO3 | 1.5 |  |
| N2O | 1.2 |  |
| N2O5 | 2.0 |  |
| HNO3 | 1.3 |  |
| HO2NO2 | 2.0 |  |
| CH2O | 1.4 |  |
| CH3OOH | 1.5 |  |
| CH3C(O)O2NO2 | 1.3 |  < 300 nm |
| CH3C(O)O2NO2 | 2.0 |   300 nm |
| HCl | 1.1 |  |
| HOCl | 1.4 |  |
| ClOOCl | 1.5 |  < 300 nm |
| ClOOCl | 3.0 |   300 nm |
| Cl2O3 | 1.5 |  < 300 nm |
| Cl2O3 | 3.0 |   300 nm |
| ClONO2 | 1.3 |  |
| CCl4 | 1.1 |  |
| CCl3F | 1.1 |  |
| CCl2F2 | 1.1 |  |
| CH3Cl | 1.1 |  |
| CF2O | 2.0 |  |
| CF3Br | 1.3 |  |
| CF2ClBr | 2.0 |  |
| CF2Br2 | 2.0 |  |
| C2F4Br2 | 2.0 |  |
| HOBr | 2.0 |  < 350 nm |
| HOBr | 10 |   350 nm |
| BrONO2 | 1.4 |  |

### O2 + h O + O

The photodissociation of molecular oxygen in the stratosphere is due primarily to absorption of solar radiation in the 200-220 nm wavelength region, i.e., within the Herzberg continuum.  The 185-200 nm region-the O2 Schumann-Runge band spectral range-is also very important, since solar radiation penetrates efficiently into the stratosphere at those wavelengths.

Frederick and Mentall [93] Herman and Mentall [121] and Anderson and Hall [8, 9] estimated O2 absorption cross sections from balloon measurements of solar irradiance in the stratosphere.  These authors find the cross sections in the 200-210 nm range to be ~35% smaller than the smallest of the older laboratory results, which are those of Shardanand and Prasad Rao [279].  The more recent laboratory studies (Johnston et al. [144]; Cheung et al. [54, 55], Jenouvrier et al. [137]) confirm the lower values obtained from solar irradiance measurements.  The recommended absorption cross section values between 205 and 240 nm are listed in Table 6; they are taken from Yoshino et al. [334] and are based on the latter set of laboratory measurements.  Amoruso et al. [7] have also carried out cross section measurements in this wavelength range (the Herzberg continuum); their values are ~15% lower than those reported by Yoshino et al.

###### Table 6.  Absorption Cross Sections of O2 Between 205 and 240 nm

|  (nm) | 1024  (cm2) |  (nm) | 1024  (cm2) |
| --- | --- | --- | --- |

205	7.35	223	3.89

206	7.13	224	3.67

207	7.05	225	3.45

208	6.86	226	3.21

209	6.68	227	2.98

210	6.51	228	2.77

211	6.24	229	2.63

212	6.05	230	2.43

213	5.89	231	2.25

214	5.72	232	2.10

215	5.59	233	1.94

216	5.35	234	1.78

217	5.13	235	1.63

218	4.88	236	1.48

219	4.64	237	1.34

220	4.46	238	1.22

221	4.26	239	1.10

222	4.09	240	1.01

The studies of the penetration of solar radiation in the atmosphere in the Schumann-Runge wavelength region were based originally on laboratory measurements of cross sections that were affected by instrumental parameters due to insufficient spectral resolution.  Yoshino et al. [342] reported high resolution O2 cross section measurements at 300 K, between 179 and 202 nm, obtaining the first set of results which is independent of the instrument width.  Additional studies at other temperatures, wavelengths, and isotopic compositions have been carried out by Yoshino et al. [336, 338-341], Lewis et al. [158, 159], Cheung et al. [53], and Chiu et al. [56].  More recently, Yoshino et al. [335] reported cross sections of the Schumann-Runge bands in the window region between the rotational lines for wavelengths between 180 and 195 nm; these measurements supersede their earlier ones.  Minschwaner et al. [194] have fit temperature-dependent O2 cross sections between 175 and 204 nm with polynomial expressions, providing accurate means of determining the Schumann-Runge band cross sections with a model that incorporates the most recent laboratory data.  Coquart et al. [67] have reported Herzberg continuum absorption cross sections in the wavelength region 196-205 nm of the Schumann-Runge bands.

For parameterizations of the O2 absorption in the Schumann-Runge bands used in atmospheric modeling calculations, see, e.g., the review in WMO Report No. 16 [330].  More recent work by Murtagh [220], Nicolet and Kennes, [229] and Minschwaner et al. [194] incorporates results of the later laboratory measurements into efficient schemes for computing broad-band transmission and photolysis rates.  Transmission values obtained by Murtagh [220] agree well with the WMO [330] recommendations, although the high-resolution calculations of Minschwaner and Salawitch differ with the WMO values by as much as 10 - 20% at some wavelengths.

In view of the quality of the high-resolution laboratory measurements, the primary source of uncertainty in modeling O2 photolysis in the Schumann-Runge bands (other than the issue of absolute solar irradiance) has shifted to the choice of broadband parameterization.

### O3 + h O + O2

The O3 absorption cross sections and their temperature dependence have been measured by several groups.  An earlier review is presented in WMO Report No. 16 [330]; this reference should be consulted to obtain data for atmospheric modeling calculations.  Table 7 lists merely a sample of the data taken from this review, namely the 273 K cross section values averaged over the wavelength intervals commonly employed in modeling calculations, except for the wavelength range 185 to 225 nm, where the present recommendation incorporates the averaged values from the work of Molina and Molina [206]; the older values were based on the work of Inn and Tanaka [136].  More recently, Daumont et al. [79] and Brion et al. [30] reported ozone absorption cross section measurements between 195 and 345 nm, in the temperature range 200 - 300 K; and Yoshino et al. [337] measured the cross sections in the 185 to 254 nm wavelength range at 195, 228, and 295 K; the results of these studies yield values in very good agreement with those reported by Molina and Molina [206].  Cacciani et al. [46] reported measurements of the ozone cross sections in the wavelength range from 339 to 355 nm, in reasonable agreement with the present recommendation; the same group has measured also the cross sections in the 590-610 nm region, at 230 K and at 299 K (Amoruso et al. [5]).  The temperature effect on the cross sections is negligible for wavelengths shorter than ~260 nm.  Recent work by Mauersberger et al. [181, 182] yields a value of 1137 x 10-20 cm2 for the cross section at 253.7 nm, the mercury line wavelength; it is about 1% smaller than the commonly accepted value of 1147 x 10-20 cm2 reported by Hearn [119]; about 2% smaller than the value obtained by Molina and Molina [206], 1157 x 10-20 cm2; and 0.5% larger than the value obtained by Daumont et al. [79].  The reason for the small discrepancy, which appears to be beyond experimental precision, is unclear.

Malicet et al. [170] report cross section measurements in the 195-345 nm range, at temperatures between 218 and 295 K, with a spectral bandwidth of 0.01-0.02 nm.; the results are in good agreement with the recommended values.  Their data are presented in graphical form, and are also available on floppy disks.

###### Table 7.  Absorption Cross Sections of O3 at 273 K

|  (nm) | 1020 (cm2) average |  (nm) | 1020 (cm2) average |
| --- | --- | --- | --- |
| 175.439 - 176.991 | 81.1 |  | 238.095 - 240.964 | 797 |
| 176.991 - 178.571 | 79.9 |  | 240.964 - 243.902 | 900 |
| 178.571 - 180.180 | 78.6 |  | 243.902 - 246.914 | 1000 |
| 180.180 - 181.818 | 76.3 |  | 246.914 - 250.000 | 1080 |
| 181.818 - 183.486 | 72.9 |  | 250.000 - 253.165 | 1130 |
| 183.486 - 185.185 | 68.8 |  | 253.165 - 256.410 | 1150 |
| 185.185 - 186.916 | 62.2 |  | 256.410 - 259.740 | 1120 |
| 186.916 - 188.679 | 57.6 |  | 259.740 - 263.158 | 1060 |
| 188.679 - 190.476 | 52.6 |  | 263.158 - 266.667 | 965 |
| 190.476 - 192.308 | 47.6 |  | 266.667 - 270.270 | 834 |
| 192.308 - 194.175 | 42.8 |  | 270.270 - 273.973 | 692 |
| 194.175 - 196.078 | 38.3 |  | 273.973 - 277.778 | 542 |
| 196.078 - 198.020 | 34.7 |  | 277.778 - 281.690 | 402 |
| 198.020 - 200.000 | 32.3 |  | 281.690 - 285.714 | 277 |
| 200.000 - 202.020 | 31.4 |  | 285.714 - 289.855 | 179 |
| 202.020 - 204.082 | 32.6 |  | 289.855 - 294.118 | 109 |
| 204.082 - 206.186 | 36.4 |  | 294.118 - 298.507 | 62.4 |
| 206.186 - 208.333 | 43.4 |  | 298.507 - 303.030 | 34.3 |
| 208.333 - 210.526 | 54.2 |  | 303.030 - 307.692 | 18.5 |
| 210.526 - 212.766 | 69.9 |  | 307.692 - 312.5 | 9.80 |
| 212.766 - 215.054 | 92.1 |  | 312.5 - 317.5 | 5.01 |
| 215.054 - 217.391 | 119 |  | 317.5 - 322.5 | 2.49 |
| 217.391 - 219.780 | 155 |  | 322.5 - 327.5 | 1.20 |
| 219.780 - 222.222 | 199 |  | 327.5 - 332.5 | 0.617 |
| 222.222 - 224.719 | 256 |  | 332.5 - 337.5 | 0.274 |
| 224.719 - 227.273 | 323 |  | 337.5 - 342.5 | 0.117 |
| 227.273 - 229.885 | 400 |  | 342.5 - 347.5 | 0.0588 |
| 229.885 - 232.558 | 483 |  | 347.5 - 352.5 | 0.0266 |
| 232.558 - 235.294 | 579 |  | 352.5 - 357.5 | 0.0109 |
| 235.294 - 238.095 | 686 |  | 357.5 - 362.5 | 0.00549 |

The quantum yields for O(1D) production, (O1D), for wavelengths near 310 nm, i.e., the energetic threshold or fall-off region, have been measured mostly relative to quantum yields for wavelengths shorter than 300 nm, which were assumed to be unity.  There are several studies that indicate that this assumption is not correct:  Fairchild et al. [88] observed approximately 10% of the primary photolysis products in the ground state channel, that is (O3P) ~0.1, at 274 nm; Sparks et al. [289] also report (O3P) ~0.1, at 266 nm; according to Brock and Watson [32] (O1D) = 0.88 at 266 nm; Amimoto et al. [4] report (O1D) = 0.85 at 248 nm; and Wine and Ravishankara [328] measured directly (O1D) = 0.9 at 248 nm.  There are also some indications that  (O1D) decreases slightly between 304 and 275 nm (see Brock and Watson [31, 32]).  Turnipseed et al. [307] report (O1D) = 0.87±0.04 at 222 nm and 0.46±0.29 at 193 nm, and Cooper et al. [65] report values between 0.83 and 0.88 in the wavelength region 221 - 243.5 nm.  The photochemistry of ozone has been reviewed by Wayne [325] and by Steinfeld et al. [293].  The recommended (O1D) values in the fall-off range 305 to 325 nm (the Huggins bands) are presented in Table 8, which lists the parameters for  a polynomial expression that yields (O1D) as a function of temperature and wavelength.  The expression was developed by Michelsen et al. [193] on the basis of a model that accounts for absorption by vibrationally and rotationally excited ozone. The parameters have been adjusted to yield a value of 0.95 at 305 nm.

Our earlier recommendation for (O1D) in the fall-off wavelength range was to eliminate the “tail” seen in some of the laser experiments, because it was not reproduced in the monochromator experiments.  The present recommendation is to use the larger quantum yields (0.2 - 0.3) at these wavelengths- i.e., not to eliminate the tail in question, in agreement with the high resolution data of Arnold et al. [10], Brock and Watson [32], and Trolier and Wiesenfeld [304];  with the more recent work of Takahashi et al. [298], who carried out direct quantum yield measurements at room temperature; and with the work of Ball et al. [12, 13], who measured between 227 and 300 K the quantum yield for O2 (1g), which correlates with that of O(1D), assuming spin forbidden processes do not occur.  Additional experimental work is needed to establish the temperature dependency of the quantum yield in this fall-off wavelength region.

Note that the recommendation in Table 8 applies only for  > 290 nm.  For 220  280 nm the more recent quantum yield measurements yield values around 0.85-0.9; however, the contribution from these wavelengths to O(1D) production in the stratosphere and troposphere is not significant.

The uncertainty in the quantum yield values for atmospheric modeling purposes is estimated in Table 5 as 1.2 for 290 <  < 305 nm, and 1.3 for  > 305 nm.  Considering the importance of the process additional measurements should be carried out in the fall-off region (the Huggins bands) for quantum yields and their temperature dependence.

###### Table 8.  Quantum Yields, , for Production of O(1D) in the Photolysis of O3

|  (nm) | A | B (K) |
| --- | --- | --- |
| 305 | 0.96 | 5.659 |
| 306 | 0.96 | 16.56 |
| 307 | 1.00 | 47.61 |
| 308 | 1.09 | 114.2 |
| 309 | 1.32 | 230.1 |
| 310 | 1.80 | 392.1 |
| 311 | 2.78 | 586.9 |
| 312 | 4.63 | 793.3 |
| 313 | 7.80 | 981.7 |
| 314 | 12.6 | 1139 |
| 315 | 16.7 | 1225 |
| 316 | 19.4 | 1300 |
| 317 | 17.1 | 1295 |
| 318 | 20.7 | 1365 |
| 319 | 17.2 | 1282 |
| 320 | 16.3 | 1534 |
| 321 | 7.59 | 1395 |
| 322 | 10.9 | 1728 |
| 323 | 13.6 | 1701 |
| 324 | 10.2 | 1657 |
| 325 | 11.2 | 2065 |

 (,T) = A exp [-B/T]

185K < T < 320K

for 290 nm <  < 305nm, (

fornm, (

### HO2 + h OH + H

The absorption cross sections of the hydroperoxyl radical, HO2, in the 200-250 nm region have been measured at room temperature by Paukert and Johnston [242]; Hochanadel et al. [123]; Cox and Burrows [70]; McAdam et al. [186]; Kurylo et al. [153]; Moortgat et al. [217]; Dagaut and Kurylo [77]; Lightfoot and Jemi-Alade [162]; who measured the cross sections up to 777 K;  Crowley et al. [76]; and Sander et al. [269] at 227.5 nm.  There are significant discrepancies in the cross section values, particularly around 200 nm; no definitive explanation of the differences can be offered at present.

Table 9 lists the recommended cross sections, which are taken from the review by Wallington et al. [321].  Photolysis of HO2 in the stratosphere and troposphere is slow and can be neglected, but the UV absorption cross sections are important in laboratory studies of reaction kinetics.

Lee [156] has detected O(1D) as a primary photodissociation product at 193 and at 248 nm, with a quantum yield that is about 15 times larger at the longer wavelength.  The absolute quantum yield for O(1D) production has not been reported yet.

###### Table 9.  Absorption Cross Sections of HO2

| (nm) | 1020(cm2) |
| --- | --- |

190	387

200	458

210	454

220	373

230	245

240	135

250	60

### H2O + h H + OH

Water vapor has a continuum absorption spectrum at wavelengths longer than 145 nm, with a maximum around 165 nm, the cross sections falling off rapidly toward longer wavelengths; the photodissociation threshold occurs at 246 nm.  Below 69 nm the spectrum is also a continuum, and between 69 and 145 nm it consists of diffuse bands.  In the atmosphere water vapor is photodissociated mainly by the solar Lyman alpha line (121.6 nm).

The absorption cross sections and the photochemistry of water vapor have been reviewed, for example, by Hudson [130, 131], by Hudson and Kiefer [132], by Calvert and Pitts [47], and by Okabe [234].

The recommended absorption cross sections are taken from the review by Hudson and Kiefer [132] and are listed in Table 10 between 175 and 190 nm.  At these wavelengths the quantum yield for production of H and OH is unity.  At shorter wavelengths H2 and O are also formed as primary products. Stief et al. [294] report a quantum yield of 0.11 for this process between 105 and 145 nm.

###### Table 10.  Absorption Cross Sections of H2O Vapor

| (nm) | 1020(cm2) |
| --- | --- |

175.5	262.8

177.5	185.4

180.0	78.1

182.5	23.0

185.0	5.5

186.0	3.1

187.5	1.6

189.3	0.7

### H2O2 + h OH + OH

The recommended 298 K absorption cross section values, listed in Table 11, are the mean of the data of Lin et al. [164], Molina and Molina [203], Nicovich and Wine [230], and Vaghjiani and Ravishankara [310].  Molina and Molina [203] supersedes the earlier results of Molina et al. [209].  Nicovich and Wine measured the cross sections at  ± 230 relative to the values at 202.6,  = 4.32 x 10-19 cm2, and at 228.8 nm,  = 1.86 x 10-19 cm2.  The values are within 2% of the recommended value.

###### Table 11.  Absorption Cross Sections of H2O2 Vapor

| (nm) | 1020(cm2) | (nm) | 1020(cm2) |  |
| --- | --- | --- | --- | --- |
|  | 298 K | 355 K |  | 298 K | 355 K |

190	67.2		270	3.3	3.5

195	56.4		275	2.6	2.8

200	47.5		280	2.0	2.2

205	40.8		285	1.5	1.6

210	35.7		290	1.2	1.3

215	30.7		295	0.90	1.0

220	25.8		300	0.68	0.79

225	21.7		305	0.51	0.58

230	18.2	18.4	310	0.39	0.46

235	15.0	15.2	315	0.29	0.36

240	12.4	12.6	320	0.22	0.27

245	10.2	10.8	325	0.16	0.21

250	8.3	8.5	330	0.13	0.17

255	6.7	6.9	335	0.10	0.13

260	5.3	5.5	340	0.07	0.10

265	4.2	4.4	345	0.05	0.06

350	0.04	0.05

Nicovich and Wine have measured the temperature dependence of these cross sections.  They expressed the measured cross sections as the sum of two components: 1, due to absorption from H2O2, which has the O-O stretch excited; and  0, due to absorption by ground state molecules.  For atmospheric calculations the expression given in Table 12 may be used.  The photodissociation quantum yield is believed to be unity.  At and above 248 nm, the major photodissociation process is that leading to OH, i.e., the quantum yield for OH production is 2 (Vaghjiani and Ravishankara [311] and Vaghjiani et al. [312]).  At 193 nm this quantum yield decreases to about 1.5 (Vaghjiani et al. [312]; Schiffman et al. [273]), and the quantum yield for O-atom production increases to about 0.16 (Vaghjiani et al. [312]).

###### Table 12.  Mathematical Expression for Absorption Cross Sections of H2O2

as a Function of Temperature

_________________________________________________________________

1021  (,T)  =   An  n  +  (1 - )  Bn  n

Where T:  temperature K;  :  nm;   = [1 + exp (-1265/T)]-1

A0  =  6.4761 x 104	B0  =  6.8123 x 103

A1  =  -9.2170972 x 102	B1  =  -5.1351 x 101

A2  =  4.535649	B2  =  1.1522 x 10-1

A3  =  -4.4589016 x 10-3	B3  =  -3.0493 x 10-5

A4  =  -4.035101 x 10-5	B4  =  -1.0924 x 10-7

A5  =  1.6878206 x 10-7

A6  =  -2.652014 x 10-10

A7  =  1.5534675 x 10-13

_________________________________________________________________

Range 260-350 nm;  200-400 K

### NO2 + h NO + O

Earlier recommendations for the absorption cross sections of nitrogen dioxide were taken from the work of Bass et al. [18].  More recent measurements have been reported by Schneider et al. [274], at 298 K, for the wavelength range from 200 to 700 nm, and by Davidson et al. [81], from 270 to 420 nm, in the 232-397 K temperature range.  At room temperature the agreement between these three sets of measurements is good  (within 5% between 305 and 345 nm and within 10% at the longer wavelengths).  The agreement is poor below room temperature, as well as at the shorter wavelengths.  A possible cause for the discrepancies is the presence of N2O4.  The corrections needed to account for the presence of this species are largest around 200 nm, where it absorbs strongly.  The corrections are also large at the lowest temperatures, because a significant fraction of the NO2 forms N2O4.  On the other hand, there is no error apparent in the corrections carried out by Bass et al., so that the reason for the discrepancy is not clear.  Measurements of the absorption cross sections in the visible (440 to 460 nm), between 273 and 404 K, have been reported by Amoruso et al. [6], and Corcoran et al. [68] carried out high-resolution measurements at a few selected wavelength ranges between 470 and 616 nm, at 295, 573 and 673 K.  Additional high-resolution studies of the cross sections, mainly aimed at improving the accuracy of atmospheric measurements, have been reported by Harwood and Jones [115], Coquart et al. [66], Mérienne et al. [192], Frost et al. [94], and Harder et al. [113].

Table 13 lists the recommended absorption cross sections, averaged over the wavelength intervals used for atmospheric photodissociation calculations.  For the wavelength range from 200 to 274 nm the values are taken from Schneider et al. [274]; in this range the temperature effect is negligible.  For the 274 to 420 nm region the temperature-dependent values are taken from Davidson et al. [81].

###### Table 13.  Absorption Cross Sections of NO2

|  | 1020 , average at 25°C |  | 1020 , average at 0°C | 1022 a* |
| --- | --- | --- | --- | --- |
| (nm) | cm2 molecule-1 | (nm) | (cm2 molecule-1) | (cm2 molecule-1 degree-1) |

202.02 - 204.08	41.45	273.97 - 277.78	5.03	0.075

204.08 - 206.19	44.78	277.78 - 281.69	5.88	0.082

206.19 - 208.33	44.54	281.69 - 285.71	7.00	-0.053

208.33 - 210.53	46.41	285.71 - 289.85	8.15	-0.043

210.53 - 212.77	48.66	289.85 - 294.12	9.72	-0.031

212.77 - 215.06	48.18	294.12 - 298.51	11.54	-0.162

215.06 - 217.39	50.22	298.51 - 303.03	13.44	-0.284

217.39 - 219.78	44.41	303.03 - 307.69	15.89	-0.357

219.78 - 222.22	47.13	307.69 - 312.50	18.67	-0.536

222.22 - 224.72	37.72	312.5    - 317.5	21.53	-0.686

224.72 - 227.27	39.29	317.5    - 322.5	24.77	-0.786

227.27 - 229.89	27.40	322.5    - 327.5	28.07	-1.105

229.89 - 232.56	27.78	327.5    - 332.5	31.33	-1.355

232.56 - 235.29	16.89	332.5    - 337.5	34.25	-1.277

235.29 - 238.09	16.18	337.5    - 342.5	37.98	-1.612

238.09 - 240.96	8.812	342.5    - 347.5	40.65	-1.890

240.96 - 243.90	7.472	347.5    - 352.5	43.13	-1.219

243.90 - 246.91	3.909	352.5    - 357.5	47.17	-1.921

246.91 - 250.00	2.753	357.5    - 362.5	48.33	-1.095

250.00 - 253.17	2.007	362.5    - 367.5	51.66	-1.322

253.17 - 256.41	1.973	367.5    - 372.5	53.15	-1.102

256.41 - 259.74	2.111	372.5    - 377.5	55.08	-0.806

259.74 - 263.16	2.357	377.5    - 382.5	56.44	-0.867

263.16 - 266.67	2.698	382.5    - 387.5	57.57	-0.945

266.67 - 270.27	3.247	387.5    - 392.5	59.27	-0.923

270.27 - 273.97	3.785	392.5    - 397.5	58.45	-0.738

397.5    - 402.5	60.21	-0.599

402.5    - 407.5	57.81	-0.545

407.5    - 412.5	59.99	-1.129

412.5    - 417.5	56.51	0.001

417.5    - 422.5	58.12	-1.208

*	The quantity a is the temperature coefficient of  as defined in the equation

(t) = (0°) + a • t, where t is in degrees Celsius.

The earlier recommendation for quantum yields was based on the work of Harker et al. [114] and of Davenport [80] for the atmospherically important 375-470 nm region.  The work by Gardner et al. [97] yields values that are in much better agreement with the values reported earlier by Jones and Bayes [147].  The recommended quantum yield values, listed in Table 14, are in agreement with the recommendation of Gardner et al. [97]; they are based on a smooth fit to the data of Gardner et al. [97] for the wavelength range from 334 to 404 nm; Harker et al. [114] for 397-420 nm (corrected for cross sections); Davenport [80] for 400-420 nm; and Jones and Bayes [147] for 297-412 nm.  Direct measurements of the solar photodissociation rate of NO2 in the troposphere by Parrish et al. [241] and by Shetter et al. [280] agree better with theoretical estimates based on this recommendation than with the earlier one.

###### Table 14.  Quantum Yields for NO2 Photolysis

| , nm |  | , nm |  |
| --- | --- | --- | --- |

< 285	1.000	393	0.953

290	0.999	394	0.950

295	0.998	395	0.942

300	0.997	396	0.922

305	0.996	397	0.870

310	0.995	398	0.820

315	0.994	399	0.760

320	0.993	400	0.695

325	0.992	401	0.635

330	0.991	402	0.560

335	0.990	403	0.485

340	0.989	404	0.425

345	0.988	405	0.350

350	0.987	406	0.290

355	0.986	407	0.225

360	0.984	408	0.185

365	0.983	409	0.153

370	0.981	410	0.130

375	0.979	411	0.110

380	0.975	412	0.094

381	0.974	413	0.083

382	0.973	414	0.070

383	0.972	415	0.059

384	0.971	416	0.048

385	0.969	417	0.039

386	0.967	418	0.030

387	0.966	419	0.023

388	0.964	420	0.018

389	0.962	421	0.012

390	0.960	422	0.008

391	0.959	423	0.004

392	0.957	424	0.000

### NO3 + h NO + O2 (1)

### NO3 + h NO2 + O (2)

The absorption cross sections of the nitrate free radical, NO3, have been studied by (1) Johnston and Graham [142], (2) Graham and Johnston [109], (3) Mitchell et al. [198], (4) Marinelli et al. [179], (5) Ravishankara and Wine [251], (6) Cox et al. [69], (7) Burrows et al. [43], (8) Ravishankara and Mauldin [249], (9) Sander [267], (10) Cantrell et al. [51], (11) Canosa-Mas et al. [49], and (12) Yokelson et al. [333].   The 1st and 4th studies required calculation of the NO3 concentration by modeling a complex kinetic system.  The other studies are more direct, and the results in terms of integrated absorption coefficients are in good agreement.  The recommended value at 298 K and 662 nm, (2.00 ± 0.25)x10-17 cm2, is the average of the results of studies (4), (5), and (7) through (11).  The values in the wavelength range 600-670 nm, shown in Figure 2 and listed in Table 15, were calculated using the spectra measured in studies (8), (9), and (11), and with the 662 nm value normalized to the above average.  The spectra obtained in other studies are consulted for a more extended wavelength range.  The temperature dependence of the 662 nm band has been studied by Ravishankara and Mauldin, Sander, Cantrell et al., and Yokelson et al.  Except for Cantrell et al., these studies all showed that the cross section at  662 nm increases with decreasing temperature.  The reason for this discrepancy is not clear.

The quantum yields 1 and 2 have been measured by Graham and Johnston [109], and under higher resolution by Magnotta and Johnston [168], who report the product of the cross section times the quantum yield in the 400 to 630 nm range.  The total quantum yield value, 1 + 2 , computed from the results of this latter study and the cross sections of Graham and Johnston [109], is above unity for  <610 nm, which is, of course, impossible.  Hence, there is some systematic error, and it is most likely in the primary quantum yield measurements.  More recently, Orlando et al. [239] measured the photolysis quantum yields between 570 and 635 nm.

Johnston et al.[140] have recently re-analyzed the available laboratory data relevant to NO3 photolysis, including quantum yield studies, chemiluminescence,  LIF studies, and molecular beam scattering experiments. Their model reproduces the wavelength dependent quantum yield data reasonably well. The new recommendation is based on the J-values calculated by Johnston et al. for overhead sun in the stratosphere:

J1(NO + O2) = 0.0201 s-1

J2(NO2 + O) = 0.156 s-1

Wavelength-specific quantum yields over the temperature range 190-298 K may be found in the tabulation by Johnston et al.

The spectroscopy of NO3 has been reviewed by Wayne et al. [326].  The reader is referred to this work for a more detailed discussion of the cross section and quantum yield data and for estimates of the photodissociation rates as a function of zenith angle.

Figure 2.  Absorption Spectrum of NO3

###### Table 15.  Absorption Cross Sections of NO3 at 298 K

|  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |
| --- | --- | --- | --- | --- | --- |

600	258	625	796	648	60

601	263	626	703	649	51

602	302	627	715	650	49

603	351	628	702	651	52

604	413	629	672	652	55

605	415	630	638	653	61

606	322	631	470	654	76

607	225	632	344	655	93

608	170	633	194	656	131

609	153	634	142	657	172

610	192	635	128	658	222

611	171	636	159	659	356

612	202	637	191	660	658

613	241	638	193	661	1308

614	242	639	162	662	2000

615	210	640	121	663	1742

616	190	641	99	664	1110

617	189	642	91	665	752

618	208	643	93	666	463

619	229	644	92	667	254

620	292	645	85	668	163

621	450	646	72	669	113

622	941	647	69	670	85

623	1407

624	1139

### N2O + h N2 + O(1D)

The recommended values are taken from the work of Selwyn et al. [277], who measured the temperature dependence of the absorption cross sections in the atmospherically relevant wavelength region.  They have fitted their data with the expression shown in Table 16; Table 17 presents the room temperature data.  Hubrich and Stuhl [127] remeasured the N2O cross sections at 298 K and 208 K and Merienne et al. [191] in the range from 220 K to 296 K.  The results of these two sets of measurements are in very good agreement with those of Selwyn et al.  The quantum yield for photodissociation is unity, and the products are N2 and O(1D) (Zelikoff and Aschenbrand [343], Paraskevopoulos and Cvetanovic [240], Preston and Barr [244], Simonaitis et al. [285]).  The yield of N(4s) and NO(2) is less than 1% (Greenblatt and Ravishankara [112]).

###### Table 16.  Mathematical Expression for Absorption Cross Sections

of N2O as a Function of Temperature

________________________________________________________

1n (,T)  =  An  n  +  (T-300)  exp( Bn n)

Where T:  temperature K;	:  nm;

A0  =  68.21023	B0  =  123.4014

A1  =  -4.071805	B1  =  -2.116255

A2  =  4.301146 x 10-2	B2  =  1.111572 x 10-2

A3  =  -1.777846 x 10-4	B3  =  -1.881058 x 10-5

A4  =  2.520672 x 10-7

________________________________________________________

Range 173 to 240 nm;  194 to 320 K

###### Table 17.  Absorption Cross Sections of N2O at 298 K

|  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |
| --- | --- | --- | --- | --- | --- |

173	11.3	196	6.82	219	0.115

174	11.9	197	6.10	220	0.0922

175	12.6	198	5.35	221	0.0739

176	13.4	199	4.70	222	0.0588

177	14.0	200	4.09	223	0.0474

178	13.9	201	3.58	224	0.0375

179	14.4	202	3.09	225	0.0303

180	14.6	203	2.67	226	0.0239

181	14.6	204	2.30	227	0.0190

182	14.7	205	1.95	228	0.0151

183	14.6	206	1.65	229	0.0120

184	14.4	207	1.38	230	0.00955

185	14.3	208	1.16	231	0.00760

186	13.6	209	0.980	232	0.00605

187	13.1	210	0.755	233	0.00478

188	12.5	211	0.619	234	0.00360

189	11.7	212	0.518	235	0.00301

190	11.1	213	0.421	236	0.00240

191	10.4	214	0.342	237	0.00191

192	9.75	215	0.276	238	0.00152

193	8.95	216	0.223	239	0.00123

194	8.11	217	0.179	240	0.00101

195	7.57	218	0.142

### N2O5 + h Products

The absorption cross sections of dinitrogen pentoxide, N2O5 have been measured at room temperature by Jones and Wulf [146] between 285 and 380 nm, by Johnston and Graham [142] between 210 and 290 nm, by Graham [108] between 205 and 380 nm, and for temperatures in the 223 to 300 K range by Yao et al. [332], between 200 and 380 nm.  The agreement is good, particularly considering the difficulties in handling N2O5.  The recommended cross section values, listed in Table 18, are taken from Yao et al. [332]. For wavelengths shorter than 280 nm there is little or no temperature dependence, and between 285 and 380 nm the temperature effect is best computed with the expression listed at the bottom of Table 18.  Recent measurements of the cross sections and their temperature dependence by Harwood et al. [116] yield values in excellent agreement with this recommendation except at the longest wavelengths (380 nm) and lowest temperatures (233 K), where the new values are about 30% lower.  However, the contribution to solar photodissociation from these longer wavelengths is negligible, and the differences between the predicted photolysis rates from the two sets of data are smaller than 3% (Harwood et al. [116]).

There are several studies on the primary photolysis products of N2O5:  Swanson et al. [297] have measured the quantum yield for NO3 production at 249 and at 350 nm, obtaining a value close to unity, which is consistent with the observations of Burrows et al. [42] for photolysis at 254 nm.  Barker et al. [15] report a quantum yield for O(3P) production at 290 nm of less than 0.1, and near unity for NO3.  For O-atom production Margitan (private communication, 1985) measured a quantum yield value of 0.35 at 266 nm, and Ravishankara et al. [252] report values of 0.72, 0.38, 0.21 and 0.15 at 248, 266, 287, and 289 nm, respectively, with a quantum yield near unity for NO3 production at all these wavelengths.  It appears, then, that NO3 is produced with unit quantum yield while the O-atom, and hence the NO yield, increases at shorter wavelengths, with a consequent decrease in the NO2 yield.  The study of Oh et al. [233] indicates that, besides NO3, the primary photolysis products are a wavelength-dependent mixture of NO2, NO2* and NO + O, where NO2* represents one or more excited electronic states, most likely the 2B1 state.

###### Table 18.  Absorption Cross Sections of N2O5

|  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |
| --- | --- | --- | --- |

200	920	245	52

205	820	250	40

210	560	255	32

215	370	260	26

220	220	265	20

225	144	270	16.1

230	99	275	13.0

235	77	280	11.7

240	62

For 285 nm <  < 380 nm; 300 K > T > 225 K:

1020  = exp[2.735 + ((4728.5 - 17.127 )/T)]

where  is in cm2/molecule;  in nm; and T in K.

### HONO + h OH + NO

The ultraviolet spectrum of HONO between 300 and 400 nm has been studied by Stockwell and Calvert [295] by examination of its equilibrium mixtures with NO, NO2, H2O, N2O3 and N2O4; the possible interferences by these compounds were taken into account.  More recently, Vasudev [317] measured relative cross sections by monitoring the OH photodissociation product with laser-induced fluorescence; and Bongartz et al. [26] determined absolute cross section values at 0.1 nm resolution in a system containing a highly diluted mixture of NO, NO2, H2O, and HONO,  by measuring total NOx  (NO and NO2).  There are some discrepancies between these two recent sets of results in terms of relative peak heights; however, both yield essentially the same photodissociation rate provided Vasudev's relative data are normalized to match the cross section value reported by Bongartz et al. at 354 nm. At this wavelength the value reported earlier by Stockwell and Calvert is about 20% smaller.  The recommended values, listed in Table 19, are taken from Bongartz et al.

###### Table 19.  Absorption Cross Sections of HONO

|  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |
| --- | --- | --- | --- | --- | --- |

310	1.3	339	18.8	368	52.0

311	1.9	340	10.0	369	38.8

312	2.8	341	17.0	370	17.8

313	2.2	342	38.6	371	11.3

314	3.6	343	14.9	372	10.0

315	3.0	344	9.7	373	7.7

316	1.4	345	10.9	374	6.2

317	3.1	346	12.3	375	5.3

318	5.6	347	10.4	376	5.3

319	3.6	348	9.1	377	5.0

320	4.9	349	7.9	387	5.8

321	7.8	350	11.2	379	8.0

322	4.9	351	21.2	380	9.6

323	5.1	352	15.5	381	11.3

324	7.1	353	19.1	382	15.9

325	5.0	354	58.1	383	21.0

326	2.9	355	36.4	384	24.1

327	6.6	356	14.1	385	20.3

328	11.7	357	11.7	386	13.4

329	6.1	358	12.0	387	9.0

330	11.1	359	10.4	388	5.6

331	17.9	360	9.0	389	3.4

332	8.7	361	8.3	390	2.7

333	7.6	362	8.0	391	2.0

334	9.6	363	9.6	392	1.5

335	9.6	364	14.6	393	1.1

336	7.2	365	16.8	394	0.6

337	5.3	366	18.3	395	1.0

338	10.0	367	30.2	396	0.4

### HNO3 + h products

The recommended absorption cross sections and their temperature dependency, listed in Table 20, are taken from the work of Burkholder et al. [39].  The temperature effect is very important for estimates of atmospheric photodissociation; the results of Burkholder et al. agree well with those of Rattigan et al. [245, 246], except at 238 K, where these latter authors report significantly smaller values.

The new cross section values agree reasonably well at room temperature with the data of Molina and Molina [203], which provided the basis for the earlier recommendation.  These data are also in good agreement throughout the 190-330 nm range with the values reported by Biaume [21].  They are also in very good agreement with the data of Johnston and Graham [141], except towards both ends of the wavelength range.  Okabe [235] has measured the cross sections in the 110-190 nm range and his results are 20-30% lower than those of Biaume and of Johnston and Graham around 185-190 nm.

Johnston et al. [139] measured a quantum yield value of ~1 for the OH + NO2 channel in the 200-315 nm range, using end product analysis.  The quantum yield for O-atom production at 266 nm has been measured to be 0.03, and that for H-atom production less than 0.002, by Margitan and Watson [174], who looked directly for these products using atomic resonance fluorescence.  Jolly et al. [145] measured a quantum yield for OH production of 0.89 ± 0.08 at 222 nm.  Turnipseed et al. [308] have measured a quantum yield near unity for OH production at 248 and 222 nm.  However, at 193 nm they report this quantum yield to be only ~0.33, and the quantum yield for production of O-atoms to be about 0.8.  Thus, it appears that HONO is a major photolysis product at 193 nm.  These results are qualitatively in agreement with those reported by Schiffman et al. [273], namely a quantum yield for OH production of 0.47 at 193 nm, and of 0.75 at 248 nm.

###### Table 20.  Absorption Cross Sections and Temperature Coefficients of HNO3 Vapor

|  (nm) | 1020 (cm2) | 103 B (K-1) |  (nm) | 1020 (cm2) | 103 B (K-1) |  (nm) | 1020 (cm2) | 103 B (K-1) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| 190 | 1360 | 0 | 244 | 2.16 | 1.75 | 298 | 0.316 | 2.92 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 192 | 1225 | 0 | 246 | 2.06 | 1.61 | 300 | 0.263 | 3.10 |
| 194 | 1095 | 0 | 248 | 2.00 | 1.44 | 302 | 0.208 | 3.24 |
| 196 | 940 | 1.70 | 250 | 1.97 | 1.34 | 304 | 0.167 | 3.52 |
| 198 | 770 | 1.65 | 252 | 1.96 | 1.23 | 306 | 0.133 | 3.77 |
| 200 | 588 | 1.66 | 254 | 1.95 | 1.18 | 308 | 0.105 | 3.91 |
| 202 | 447 | 1.69 | 256 | 1.95 | 1.14 | 310 | 0.0814 | 4.23 |
| 204 | 328 | 1.74 | 258 | 1.93 | 1.12 | 312 | 0.0628 | 4.70 |
| 206 | 231 | 1.77 | 260 | 1.91 | 1.14 | 314 | 0.0468 | 5.15 |
| 208 | 156 | 1.85 | 262 | 1.87 | 1.14 | 316 | 0.0362 | 5.25 |
| 210 | 104 | 1.97 | 264 | 1.83 | 1.18 | 318 | 0.0271 | 5.74 |
| 212 | 67.5 | 2.08 | 266 | 1.77 | 1.22 | 320 | 0.0197 | 6.45 |
| 214 | 43.9 | 2.17 | 268 | 1.70 | 1.25 | 322 | 0.0154 | 6.70 |
| 216 | 29.2 | 2.17 | 270 | 1.62 | 1.45 | 324 | 0.0108 | 7.16 |
| 218 | 20.0 | 2.21 | 272 | 1.53 | 1.49 | 326 | 0.00820 | 7.55 |
| 220 | 14.9 | 2.15 | 274 | 1.44 | 1.56 | 328 | 0.00613 | 8.16 |
| 222 | 11.8 | 2.06 | 276 | 1.33 | 1.64 | 330 | 0.00431 | 9.75 |
| 224 | 9.61 | 1.96 | 278 | 1.23 | 1.69 | 332 | 0.00319 | 9.93 |
| 226 | 8.02 | 1.84 | 280 | 1.12 | 1.78 | 334 | 0.00243 | 9.60 |
| 228 | 6.82 | 1.78 | 282 | 1.01 | 1.87 | 336 | 0.00196 | 10.5 |
| 230 | 5.75 | 1.80 | 284 | 0.909 | 1.94 | 338 | 0.00142 | 10.8 |
| 232 | 4.87 | 1.86 | 286 | 0.807 | 2.04 | 340 | 0.00103 | 11.8 |
| 234 | 4.14 | 1.90 | 288 | 0.709 | 2.15 | 342 | 0.00086 | 11.8 |
| 236 | 3.36 | 1.97 | 290 | 0.615 | 2.27 | 344 | 0.00069 | 9.30 |
| 238 | 2.93 | 1.97 | 292 | 0.532 | 2.38 | 346 | 0.00050 | 12.1 |
| 240 | 2.58 | 1.97 | 294 | 0.453 | 2.52 | 348 | 0.00042 | 11.9 |
| 242 | 2.34 | 1.88 | 296 | 0.381 | 2.70 | 350 | 0.00042 | 9.30 |

 (, T) =  (, 298) exp [B () (T - 298)]; T in K

### HO2NO2 + h Products

There are five studies of the UV spectrum of HO2NO2 vapor:  Cox and Patrick [72], Morel et al. [219], Graham et al. [110], Molina and Molina [203], and Singer et al. [286].  The latter three studies are the only ones covering the gas phase spectrum in the critical wavelength range for atmospheric photodissociation  (290 nm).  The recommended values, listed in Table 21, are an average of the work of Molina and Molina [203] and of Singer et al. [286], which are the more direct studies.  The cross sections appear to be temperature independent between 298 and 253 K (Singer et al. [286]).  MacLeod et al. [167] report that photolysis at 248 nm yields one third OH and NO3 and two thirds HO2 + NO2.

###### Table 21.  Absorption Cross Sections of HO2NO2 Vapor

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

190	1010	260	28.5

195	816	265	23.0

200	563	270	18.1

205	367	275	13.4

210	239	280	9.3

215	161	285	6.2

220	118	290	3.9

225	93.5	295	2.4

230	79.2	300	1.4

235	68.2	305	0.9

240	58.1	310	0.5

245	48.9	315	0.3

250	41.2	320	0.2

255	35.0	325	0.1

### CH2O + h H + HCO   (1)

### CH2O + h H2 + CO   (2)

The earlier recommendation for the formaldehyde absorption cross sections was based on the work carried out by Bass et al. [17] with a resolution of 0.05 nm at 296 K and 223 K, and by Moortgat et al. [214, 216] with a resolution of 0.5 nm in the 210-360 K temperature range.  More recently, Cantrell et al. [50] measured the cross sections in the 300-360 nm range between 223 K and 293 K, and Rogers [260] measured the cross sections in the 235-365 nm range at 296 K, both groups using Fourier transform spectrometry at a resolution of up to 0.011 nm   ( cm-1).  The agreement between these two reports is very good.  The recommended values are those given by Cantrell et al. as a function of temperature; the reader is referred to the original article to obtain the high-resolution data.  Table 22 lists the low-resolution cross sections taken from that work, that are suitable for atmospheric photodissociation calculations.

The quantum yields have been reported with good agreement by Horowitz and Calvert [124], Clark et al. [60], Tang et al. [301], Moortgat and Warneck [218], and Moortgat et al. [214, 216].  The recommended values listed in Table 22 are based on the results of these investigators, as evaluated by S. Madronich (private communication, 1991).  The quantum yield for the production of H2 and CO is pressure- and temperature-dependent for wavelengths longer than about 330 nm (Moortgat et al. [216]).  Table 22 gives the values at atmospheric pressure and room temperature; the reader is referred to the Moortgat et al. publication for information on values at lower pressures and temperatures.

###### Table 22.  Absorption Cross Sections and Quantum Yields for Photolysis of CH2O

|  | 1020 (cm2) |  | T-Parameters* |  | 1 | 2 |
| --- | --- | --- | --- | --- | --- | --- |
|  (nm) | 223 K | 293 K |  | A | B |  | (H + HCO) | (H2 + CO) |

301.25	1.38	1.36	1.37	-0.21	0.749	0.251

303.75	4.67	4.33	4.43	-4.73	0.753	0.247

306.25	3.32	3.25	3.27	-1.06	0.753	0.247

308.75	2.27	2.22	2.24	-0.724	0.748	0.252

311.25	0.758	0.931	0.882	2.48	0.739	0.261

313.75	3.65	3.40	3.47	-3.64	0.724	0.276

316.25	4.05	3.89	3.94	-2.30	0.684	0.316

318.75	1.66	1.70	1.69	0.659	0.623	0.368

321.25	1.24	1.13	1.16	-1.52	0.559	0.423

323.75	0.465	0.473	0.471	0.118	0.492	0.480

326.25	5.06	4.44	4.61	-8.86	0.420	0.550

328.75	2.44	2.29	2.34	-2.15	0.343	0.634

331.25	1.39	1.28	1.31	-1.53	0.259	0.697

333.75	0.093	0.123	0.114	0.432	0.168	0.739

336.25	0.127	0.131	0.130	0.050	0.093	0.728

338.75	3.98	3.36	3.54	-8.96	0.033	0.667

341.25	0.805	0.936	0.898	1.86	0.003	0.602

343.75	1.44	1.26	1.31	-2.64	0.001	0.535

346.25	0.004	0.071	0.052	0.957	0	0.469

348.75	0.009	0.040	0.031	0.438	0	0.405

351.25	0.169	0.235	0.216	0.948	0	0.337

353.75	1.83	1.55	1.63	-4.05	0	0.265

356.25	0.035	0.125	0.099	1.27	0	0.197

Note:	The values are averaged for 2.5 nm intervals centered on the indicated wavelength.

*	Cross section for -50°C < T < 20°C calculated as (T) = A + Bx10-3 T; T in °C, and  in 10-20 cm2.

### CH3O2 + h Products

### C2H5O2 + h Products

The absorption cross sections have been reviewed by Wallington et al. [321] and by Lightfoot et al. [161].  Table 23 lists the recommended values, obtained as follows: the cross section value at 250 nm was set to 400 x 10-20 cm2, which is the value we used previously in connection with rate constant recommendations; then, the average of the recommendations of Wallington et al. and Lightfoot et al. was used to determine the shape of the CH3O2 spectrum (these two sets of values agree very well with each other); finally, the cross section values at the other wavelengths were obtained by scaling the spectrum to the 250 nm value.  The cross sections for C2H5O2 were taken from Lightfoot et al., who included in their evaluation the data of Bauer et al. [19], that was not published in time to be included in the evaluation of Wallington et al.  Recent studies of these spectra by Maricq and Wallington [177](CH3O2 and C2H5O2),  Fenter et al. [89] (C2H5O2), and Roehl et al. [258] are in excellent agreement with the recommended values.

###### Table 23.  Absorption Cross Sections of CH3O2 and C2H5O2

|  | 1020 (cm2) |
| --- | --- |
| (nm) | CH3O2 | C2H5O2 |
| 210.0 | 213 |  |
| 215.0 | 273 | 251 |
| 220.0 | 335 | 310 |
| 225.0 | 392 | 361 |
| 230.0 | 438 | 402 |
| 235.0 | 452 | 428 |
| 240.0 | 450 | 436 |
| 245.0 | 432 | 427 |
| 250.0 | 400 | 400 |
| 255.0 | 366 | 361 |
| 260.0 | 322 | 315 |
| 265.0 | 278 | 265 |
| 270.0 | 231 | 214 |
| 275.0 | 170 | 167 |
| 280.0 | 141 | 126 |
| 285.0 | 98 | 91 |
| 290.0 | 63 | 65 |
| 295.0 |  | 43 |
| 300.0 |  |  |

### CH3OOH + h Products

Vaghjiani and Ravishankara [310] measured the cross sections of CH3OOH by monitoring the CH3OOH concentration via trapping and titration.  These results are recommended and are listed in Table 24.  The earlier results of Molina and Arguello [210] are consistently 40% higher than the values shown in Table 24; this difference is believed to be due to difficulty in trapping CH3OOH and measuring its concentration.  CH3OOH dissociates upon light absorption to give CH3O with unit quantum yield (Vaghjiani and Ravishankara, [311]); these authors also observed some production of H and O atoms at shorter wavelengths (i.e., 193 nm).  Thelen et al. [302] report unit quantum yield for OH production at 248 and 193 nm, in agreement with the results of Vaghjiani and Ravishankara.

###### Table 24.  Absorption Cross Sections of CH3OOH

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

210	31.2	290	0.69

220	15.4	300	0.41

230	9.62	310	0.24

240	6.05	320	0.14

250	3.98	330	0.079

260	2.56	340	0.047

270	1.70	350	0.027

280	1.09	360	0.016

### HCN + h Products

Herzberg and Innes [122] have studied the spectroscopy of hydrogen cyanide, HCN, that starts absorbing weakly at  < 190 nm.

The solar photodissociation rate for this molecule is rather small, even in the upper stratosphere; estimates of this rate would require additional studies of the absorption cross sections and quantum yields in the 200 nm region.

### CH3CN + h Products

McElcheran et al. [187] have reported the spectrum of acetonitrile or methyl cyanide, CH3CN; the first absorption band appears at  < 220 nm.  More recently, Suto and Lee [296] and Zetzsch [344] have measured the cross sections around 200 nm; solar photodissociation is unimportant compared to reaction with OH radicals.

### CH3C(O)O2NO2 + h Products

Absorption spectra of CH3C(O)O2NO2 (PAN) have been measured by Senum et al. [278] over the range 200-300 nm, Libuda and Zabel [160] over the range 220-325 nm, and Talukdar et al. [300] over the spectral range 195-345 nm and temperature range 250-298 K. The three studies are in excellent agreement over their range of overlap, with the values of Senum et al. being slightly smaller (15-20%) beyond 250 nm. Libuda and Zabel carried out simultaneous infrared absorption studies that showed that the measured cross sections need to be corrected for impurities that are transparent in the ultraviolet but contribute to the sample pressure in the absorption cell. These corrections are on the order of 20%. The recommended cross sections (Table 25) are based on the measurements of Talukdar et al. because of the good agreement with Libuda and Zabel and the wider spectral coverage and temperature range of this study. The uncertainties in the reported cross sections are probably quite large (on the order of a factor of 2), decreasing to about 30% at shorter wavelengths.  The only PAN quantum yield studies are those of Mazely et al.[184, 185]. In these studies, PAN was photolyzed at 248 nm, with NO2 and NO3 products being observed by laser induced fluorescence at 298 K. Quantum yields of 0.830.09 were obtained for the CH3C(O)O2 + NO2 channel and 0.30.1 for the CH3C(O)O + NO3 channel.

###### Table 25.  Absorption Cross Sections of PAN

|  (nm) | 1020  (cm2) | 103B (K-1) |  |  (nm) | 1020  (cm2) | 103B (K-1) |
| --- | --- | --- | --- | --- | --- | --- |
| 196 | 430 | 2.02 |  | 274 | 2.4 | 5.55 |
| 198 | 400 | 1.73 |  | 276 | 2.1 | 5.76 |
| 200 | 360 | 1.36 |  | 278 | 1.7 | 5.98 |
| 202 | 320 | 1.07 |  | 280 | 1.5 | 6.20 |
| 204 | 290 | 0.86 |  | 282 | 1.2 | 6.43 |
| 206 | 260 | 0.75 |  | 284 | 1.0 | 6.67 |
| 208 | 230 | 0.71 |  | 286 | 0.81 | 6.90 |
| 210 | 200 | 0.75 |  | 288 | 0.65 | 7.15 |
| 212 | 170 | 0.84 |  | 290 | 0.54 | 7.39 |
| 214 | 140 | 0.97 |  | 292 | 0.45 | 7.63 |
| 216 | 120 | 1.12 |  | 294 | 0.37 | 7.86 |
| 218 | 100 | 1.29 |  | 296 | 0.30 | 8.08 |
| 220 | 90 | 1.47 |  | 298 | 0.24 | 8.27 |
| 222 | 78 | 1.64 |  | 300 | 0.19 | 8.44 |
| 224 | 68 | 1.81 |  | 302 | 0.15 | 8.61 |
| 226 | 59 | 1.98 |  | 304 | 0.12 | 8.76 |
| 228 | 52 | 2.14 |  | 306 | 0.10 | 8.87 |
| 230 | 46 | 2.30 |  | 308 | 0.082 | 9.01 |
| 232 | 40 | 2.46 |  | 310 | 0.067 | 9.13 |
| 234 | 35 | 2.63 |  | 312 | 0.054 | 9.3 |
| 236 | 31 | 2.80 |  | 314 | 0.046 | 9.46 |
| 238 | 28 | 2.96 |  | 316 | 0.036 | 9.57 |
| 240 | 24 | 3.11 |  | 318 | 0.030 | 9.75 |
| 242 | 21 | 3.25 |  | 320 | 0.025 | 10.0 |
| 244 | 19 | 3.39 |  | 322 | 0.020 | 10.2 |
| 246 | 17 | 3.52 |  | 324 | 0.017 | 10.4 |
| 248 | 15 | 3.64 |  | 326 | 0.014 | 10.6 |
| 250 | 13 | 3.76 |  | 328 | 0.012 | 10.7 |
| 252 | 11 | 3.87 |  | 330 | 0.011 | 10.9 |
| 254 | 10 | 3.98 |  | 332 | 0.0086 | 11.2 |
| 256 | 8.9 | 4.10 |  | 334 | 0.0068 | 11.5 |
| 258 | 7.8 | 4.23 |  | 336 | 0.0061 | 11.7 |
| 260 | 6.8 | 4.38 |  | 338 | 0.0053 | 11.9 |
| 262 | 6.0 | 4.53 |  | 340 | 0.0050 | 12.2 |
| 264 | 5.2 | 4.68 |  | 342 | 0.0036 | 12.4 |
| 266 | 4.5 | 4.82 |  | 344 | 0.0024 | 12.5 |
| 268 | 3.9 | 4.97 |  | 346 | 0.0023 |  |
| 270 | 3.4 | 5.14 |  | 348 | 0.0025 |  |
| 272 | 2.9 | 5.34 |  | 350 | 0.0016 |  |

Cross sections in the temperature range 250-298 K are calculated using the equation,

ln[

### Cl2 + h Cl + Cl

The recommended absorption cross sections are taken from the work of Maric et al. [175]; they can be calculated at various temperatures with the expression given at the bottom of Table 26.  For convenience, some room temperature values are also listed in the table.  Ganske et al. [96] have also measured the cross sections at room temperature, and the agreement with the recommended values is excellent.  These two sets of data also agree well with the earlier recommendation, which was based on the work of Seery and Britton [276], which is in turn in good agreement with the results reported by Gibson and Bayliss [98], Fergusson et al. [90], and Burkholder and Bair [34].  The estimated atmospheric photodissociation rate is only weakly affected by the temperature dependency of the cross sections.

###### Table 26.  Absorption Cross Sections of Cl2

|  (nm) | 1020 , 298K (cm2) |  (nm) | 1020 , 298K (cm2) |
| --- | --- | --- | --- |

260	0.20	370	8.4

270	0.82	380	5.0

280	2.6	390	2.9

290	6.2	400	1.8

300	11.9	410	1.3

310	18.5	420	0.96

320	23.7	430	0.73

330	25.5	440	0.54

340	23.5	450	0.38

350	18.8	460	0.26

360	13.2	470	0.16

= 10-20  0.5 {27.3 exp [-99.0  (ln )2] + 0.932 exp [-91.5  (ln)2]}

where = tanh (402.7/T);  in nm, and T in K; 300 K > T > 195 K.

### ClO + h Cl + O

The absorption cross sections of chlorine monoxide, ClO, have been reviewed by Watson [324].  There are more recent measurements yielding results in reasonable agreement with the earlier ones, (1) Mandelman and Nicholls [172] in the 250-310 nm region; (2) Wine et al. [329] around 283 nm; (3) Rigaud et al. [254], (4) Jourdain et al. [148], (5) Sander and Friedl [268], (6) Trolier et al. [303] in the 270-310 nm region, and (7) Simon et al. [282] between 240 and 310 nm.  The peak cross section at the top of the continuum is 5.2x10-18, based on the average of studies (4) - (7) and Johnston et al. [143].  Figure 3 shows a spectrum of ClO.  It should be noted that the cross sections on the structured part are extremely dependent on instrument resolution, and the figure is only a guide to the line positions and approximate shapes.  The cross sections of the continuum are independent of temperature (Trolier et al. [303]), while the structured part is extremely temperature dependent.  The bands sharpen and grow with a decrease in temperature.

The calculations of Coxon et al. [74] and Langhoff et al. [154] indicate that photodecomposition of ClO accounts for at most 2 to 3 percent of the total destruction rate of ClO in the stratosphere, which occurs predominantly by reaction with oxygen atoms and nitric oxide.

Figure 3.  Absorption Spectrum of ClO

### ClOO + h ClO + O

Johnston et al. [143] measured the absorption cross sections of the ClOO radical using a molecular modulation technique that required interpretation of a complex kinetic scheme.  More recently, Mauldin et al. [183] reported cross section measurements in the range from 220 to 280 nm, and Baer et al. [11] from 240 to 300 nm.  These two studies are in very good agreement, yielding cross section values that are more than twice as large as the older Johnston et al. values.  The recommended cross sections are listed in Table 27, and are taken from the work of Mauldin et al.

###### Table 27.  Absorption Cross Sections of ClOO

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

220	611	252	2630

222	670	254	2370

224	747	256	2120

226	951	258	1890

228	1100	260	1610

230	1400	262	1370

232	1650	264	1120

234	1960	266	905

236	2240	268	725

238	2520	270	596

240	2730	272	435

242	2910	274	344

244	2960	276	282

246	2980	278	210

248	2950	280	200

250	2800

### OClO + h O + ClO

The spectrum of OClO is characterized by a series of well-developed progressions of bands extending from ~280 to 480 nm.  The spectroscopy of this molecule has been studied extensively, and the quantum yield for photodissociation appears to be unity throughout the above wavelength range.  See for example, the review by Watson [324].  Birks et al. [23] have estimated a half-life against atmospheric photodissociation of OClO of a few seconds.

The recommended absorption cross section values are those reported by Wahner et al. [320], who measured the spectra with a resolution of 0.25 nm at 204, 296, and 378 K, in the wavelength range 240 to 480 nm.  Table 28 lists the cross section values at the peak of the bands [a(0) to a(26)].  Figure 4, from Wahner et al., shows the OClO spectrum at 204 K and at room temperature.  Hubinger and Nee [125] have extended the measurements of OClO cross sections over the spectral range 125-470 nm. Frost et al. [95] have studied the spectrum at very high spectral resolution (0.1 cm-1) and at low temperature (200 K) in molecular beam expansion. In both of these studies, cross sections were measured relative to values obtained by Wahner et al.

The photochemistry of OClO is extremely complex, with several electronic excited states involved in the photodissociation dynamics. Several channels have been observed at wavelengths important in the stratosphere, including O + ClO, Cl + O2 and isomerization to ClOO.  Colussi [63] measured the quantum yield for chlorine atom production to be less than 0.01, and for oxygen atom production to be unity (within experimental error), both at 308 nm.  Vaida et al. [313] and Ruhl et al. [265] reported chlorine atom production at 362 nm; and Bishenden et al. [24, 25] measured the quantum yield for this process to be 0.15 ± 0.10 around that same wavelength. In contrast, Lawrence et al. [155] report a quantum yield for Cl-atom production in the 359-368 nm region of less than 5x10-4.  This conclusion is supported by photofragment studies of Davis and Lee [82], who report Cl yields <0.2% below 370 nm, rising to a maximum of 4% near 404 nm.  The recommendation is to use a quantum yield value of unity for the production of O-atoms.  While accurate absorption cross section values are valuable for atmospheric measurements of OClO levels, the identity of the photodissociation products is only of minor importance in the context of atmospheric processes.

###### Table 28.  Absorption Cross Sections of OClO at the Band Peaks

|  | 1020 (cm2) |
| --- | --- |
| (nm) | 204 K | 296 K | 378 K |  |

475.53	-	13	-

461.15	17	17	16

446.41	94	69	57

432.81	220	166	134

420.58	393	304	250

408.83	578	479	378

397.76	821	670	547

387.37	1046	844	698

377.44	1212	992	808

368.30	1365	1136	920

359.73	1454	1219	984

351.30	1531	1275	989

343.44	1507	1230	938

336.08	1441	1139	864

329.22	1243	974	746

322.78	1009	791	628

317.21	771	618	516

311.53	542	435	390

305.99	393	312	291

300.87	256	219	216

296.42	190	160	167

291.77	138	114	130

287.80	105	86	105

283.51	089	72	90

279.64	073	60	79

275.74	059	46	-

272.93	053	33	-

Figure 4.  Absorption Spectrum of OClO

### ClO3 + h Products

The previous recommendation for absorption cross sections was based on the work of Goodeve and Richardson [107].  Lopez and Sicre [166] have shown that the spectrum reported by Goodeve and Richardson is most likely that of Cl2O6.  Thermochemical estimates by Colussi et al. [64] further corroborate this assignment.  No recommendation is given at present for the ClO3 cross sections.

Grothe and Willner (1994; 1995) have reported UV and IR spectra of ClO3 trapped in a neon matrix.  By monitoring the amount of ClO formed as a photolysis product, they estimated UV absorption cross sections of the order of 2x10-18 cm2 around 400-450 nm.

### Cl2O + h Products

The preferred absorption cross sections, listed in Table 29, are those reported by Knauth et al. [150] at 298 K.  They are in very good agreement with the cross sections measured by Lin [163] and by Molina and Molina [201]; the discrepancy is largest at the longest wavelengths.  Nee [223] has recently reported cross section measurements in the 150-200 nm wavelength region.

Sander and Friedl [268] have measured the quantum yield for production of O-atoms to be 0.25 ± 0.05, using a broadband photolysis source extending from 180 nm to beyond 400 nm.  The main photolysis products are Cl and ClO.  Using a molecular beam technique, Nelson et al. [224] found Cl + ClO to be the primary photodissociation channel at 193, 248, and 308 nm.  More recently, Nickolaisen et al. [227] reported that broadband photolysis at wavelengths beyond 300 nm results in pressure-dependent ClO quantum yields.  Furthermore, these authors detected a transient absorption spectrum, that they assigned to a metastable triplet state of Cl2O; the implication is that the photodecomposition quantum yield is less than unity at atmospherically relevant wavelengths, in spite of the continuous nature of the absorption spectrum.  Additional experimental work is needed to corroborate this interpretation.

###### Table 29.  Absorption Cross Sections of Cl2O

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

200	71.0	330	8.40

210	23.8	340	3.58

220	8.6	350	1.54

230	28.1	360	0.73

240	103	370	0.40

250	191	380	0.36

260	195	390	0.51

270	151	400	0.79

280	126	420	1.26

290	103	440	1.11

300	71.0	460	0.63

310	40.3	480	0.32

320	19.5	500	0.22

### ClOOCl + h Cl + ClOO

Recommended absorption cross sections in the wavelength range 190-450 nm for ClOOCl are listed in Table 30.  The values for the wavelength range 200 - 360 nm are the average of experimental results reported by Cox and Hayman [71], DeMore and Tschuikow-Roux [83], Permien et al.[243], and Burkholder et al. [36]. For the nm range the data are from DeMore and Tschuikow-Roux, these being the only data available in that range. Data at wavelengths greater than 360 nm were obtained from a linear extrapolation of the logarithm of the cross sections, using the expression log[1020(cm2)] = -0.01915 x (nm) + 7.589. For  > 360 nm the extrapolated data are considered to be more reliable than the experimental measurements because of the very small dimer cross sections in this region. While the results of Cox and Hayman, DeMore and Tschuikow-Roux, Permien et al., and Burkholder et al. are in good agreement at wavelengths below 250 nm, there are significant discrepancies at longer wavelengths,  which may be attributed to uncertainties in the spectral subtraction of impurities such as Cl2O, Cl2 and Cl2O3. Huder and DeMore [129] measured ClOOCl cross sections over the 190-310 nm range using a method that minimized the corrections required for impurities such as Cl2O. The cross sections from this study are significantly smaller (up to a factor of 2) than the current recommendation, particularly when extrapolated beyond 400 nm Additional measurements are needed, particularly at the longer wavelengths, to validate the results of Huder and DeMore.

These studies also indicate that only one stable species is produced in the recombination reaction of ClO with itself, and that this species is dichlorine peroxide, ClOOCl, rather than ClOClO.  Using submillimeter wave spectroscopy, Birk et al. [22] have further established the structure of the recombination product to be ClOOCl.  These observations are in agreement with the results of quantum mechanical calculations (McGrath et al. [189, 190]; Jensen and Odershede [138]; Stanton et al. [292]). The experiments of Cox and Hayman [71] indicate that the main photodissociation products at 253.7 nm are Cl and ClOO.  Molina et al. [211] measured the quantum yield for this channel to be unity at 308 nm, with no ClO detectable as a product, with an experimental uncertainty in  of about ± 25%.  These results are also supported by quantum mechanical calculations (Stanton et al. [292]; Stanton and Bartlett  [291]).  In contrast, Eberstein [85] suggested a quantum yield of unity for the production of two ClO radicals, based merely on an analogy with the photolysis of H2O2 at shorter wavelengths.  For atmospheric photodissociation calculations the recommended quantum yield value is based on the work of Molina et al. [211], i.e., a quantum yield of unity for the Cl + ClOO channel.

###### Table 30.  Absorption Cross Sections of ClOOCl at 200-250 K

| (nm) | 1020(cm2) | (nm) | 1020(cm2) | (nm) | 1020(cm2) | (nm) | 1020(cm2) |
| --- | --- | --- | --- | --- | --- | --- | --- |

| 190 | 565.0 | 256 | 505.4 | 322 | 23.4 | 388 | 1.4 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 192 | 526.0 | 258 | 463.1 | 324 | 21.4 | 390 | 1.3 |
| 194 | 489.0 | 260 | 422.0 | 326 | 19.2 | 392 | 1.2 |
| 196 | 450.0 | 262 | 381.4 | 328 | 17.8 | 394 | 1.1 |
| 198 | 413.0 | 264 | 344.6 | 330 | 16.7 | 396 | 1.0 |
| 200 | 383.5 | 266 | 311.6 | 332 | 15.6 | 398 | 0.92 |
| 202 | 352.9 | 268 | 283.3 | 334 | 14.4 | 400 | 0.85 |
| 204 | 325.3 | 270 | 258.4 | 336 | 13.3 | 402 | 0.78 |
| 206 | 298.6 | 272 | 237.3 | 338 | 13.1 | 404 | 0.71 |
| 208 | 274.6 | 274 | 218.3 | 340 | 12.1 | 406 | 0.65 |
| 210 | 251.3 | 276 | 201.6 | 342 | 11.5 | 408 | 0.60 |
| 212 | 231.7 | 278 | 186.4 | 344 | 10.9 | 410 | 0.54 |
| 214 | 217.0 | 280 | 172.5 | 346 | 10.1 | 412 | 0.50 |
| 216 | 207.6 | 282 | 159.6 | 348 | 9.0 | 414 | 0.46 |
| 218 | 206.1 | 284 | 147.3 | 350 | 8.2 | 416 | 0.42 |
| 220 | 212.1 | 286 | 136.1 | 352 | 7.9 | 418 | 0.38 |
| 222 | 227.1 | 288 | 125.2 | 354 | 6.8 | 420 | 0.35 |
| 224 | 249.4 | 290 | 114.6 | 356 | 6.1 | 422 | 0.32 |
| 226 | 280.2 | 292 | 104.6 | 358 | 5.8 | 424 | 0.29 |
| 228 | 319.5 | 294 | 95.4 | 360 | 5.5 | 426 | 0.27 |
| 230 | 365.0 | 296 | 87.1 | 362 | 4.5 | 428 | 0.25 |
| 232 | 415.4 | 298 | 79.0 | 364 | 4.1 | 430 | 0.23 |
| 234 | 467.5 | 300 | 72.2 | 366 | 3.8 | 432 | 0.21 |
| 236 | 517.5 | 302 | 65.8 | 368 | 3.5 | 434 | 0.19 |
| 238 | 563.0 | 304 | 59.9 | 370 | 3.2 | 436 | 0.17 |
| 240 | 600.3 | 306 | 54.1 | 372 | 2.9 | 438 | 0.16 |
| 242 | 625.7 | 308 | 48.6 | 374 | 2.7 | 440 | 0.15 |
| 244 | 639.4 | 310 | 43.3 | 376 | 2.4 | 442 | 0.13 |
| 246 | 642.6 | 312 | 38.5 | 378 | 2.2 | 444 | 0.12 |
| 248 | 631.5 | 314 | 34.6 | 380 | 2.1 | 446 | 0.11 |
| 250 | 609.3 | 316 | 30.7 | 382 | 1.9 | 448 | 0.10 |
| 252 | 580.1 | 318 | 28.0 | 384 | 1.7 | 450 | 0.09 |
| 254 | 544.5 | 320 | 25.6 | 386 | 1.6 |  |  |

### Cl2O3 + h Products

The absorption cross sections of Cl2O3 have been measured by Hayman and Cox [118],  Burkholder et al. [35],  and Harwood et al. [117]. The results from these studies are significantly different in the spectral regions below 240 nm and in the long-wavelength tail beyond 300 nm. Table 31 lists the recommended values.   These are derived by averaging the spectra of Burkholder et al. and Harwood et al., which are obtained by the most direct methods. Additional work is needed, particularly in the spectral region beyond 300 nm.

###### Table 31.  Absorption Cross Sections of Cl2O3

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |
| 220 | 1200 | 275 | 1470 |
| 225 | 1130 | 280 | 1240 |
| 230 | 1060 | 285 | 990 |
| 235 | 1010 | 290 | 760 |
| 240 | 1020 | 295 | 560 |
| 245 | 1120 | 300 | 400 |
| 250 | 1270 | 305 | 290 |
| 255 | 1450 | 310 | 210 |
| 260 | 1610 | 315 | 160 |
| 265 | 1680 | 320 | 140 |
| 270 | 1630 |  |  |

### Cl2O4 + h Products

The absorption cross sections of Cl2O4 have been measured by Lopez and Sicre [165]; their results are given in Table 32.

###### Table 32.  Absorption Cross Sections of Cl2O4

|  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |
| --- | --- | --- | --- |
| 200 | 161 | 255 | 42 |
| 205 | 97 | 260 | 31 |
| 210 | 72 | 265 | 22 |
| 215 | 64 | 270 | 14 |
| 220 | 71 | 275 | 8.8 |
| 225 | 75 | 280 | 5.5 |
| 230 | 95 | 285 | 4.0 |
| 235 | 95 | 290 | 2.7 |
| 240 | 87 | 295 | 2.2 |
| 245 | 72 | 300 | 1.7 |
| 250 | 56 | 305 | 1.2 |
|  |  | 310 | 0.7 |

### Cl2O6 + h Products

The absorption cross sections for Cl2O6 are listed in Table 33 and are taken from the work of Lopez and Sicre [166].  These authors show that the spectrum originally attributed to ClO3 by Goodeve and Richardson [107] was most likely that of Cl2O6.  The cross section values measured by Lopez and Sicre are several times larger than those reported by Goodeve and Richardson, but the shape of the spectrum is similar.

###### Table 33.  Absorption Cross Sections of Cl2O6

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

200	1230	300	980

210	1290	310	715

220	1230	320	450

230	1080	330	285

240	1010	340	180

250	1010	350	112

260	1290	360	59

270	1440	370	28

280	1440	380	12

290	1290

### HF + h H + F

The ultraviolet absorption spectrum of HF has been studied by Safary et al. [266].  The onset of absorption occurs at  < 170 nm, so that photodissociation of HF should be unimportant in the stratosphere.

### HCl + h H + Cl

The absorption cross sections of HCl, listed in Table 34, are taken from the work of Inn [134].

###### Table 34.  Absorption Cross Sections of HCl Vapor

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

140	211	185	31.3

145	281	190	14.5

150	345	195	6.18

155	382	200	2.56

160	332	205	0.983

165	248	210	0.395

170	163	215	0.137

175	109	220	0.048

180	58.8

### HOCl + h OH + Cl

The absorption cross sections of HOCl vapor have been measured by several groups.  Molina and Molina [201] and Knauth et al. [150] produced this species using equilibrium mixtures with Cl2O and H2O; their results provided the basis for the earlier recommendation.  More recently, Mishalanie et al. [197] and Permien et al. [243] used a dynamic source to generate the HOCl vapor.  The cross section values reported by Molina and Molina [201], Mishalanie et al. [197], and Permien et al. [243] are in reasonable agreement between 250 and 330 nm.  In this wavelength range, the values reported by Knauth et al. [150] are significantly smaller, e.g., a factor of 4 at 280 nm.  Beyond 340 nm, the cross sections of Mishalanie et al. are much smaller than those obtained by the other three groups:  at 365 nm, the discrepancy is about an order of magnitude.

The recent results by Burkholder [33] are in excellent agreement with the work of Knauth et al. [150], but in poor agreement with the more recent measurements of Mishalanie et al. [197] and Permien et al. [243]. The discrepancies can be attributed mostly to difficulties in correcting the measured absorptions for the presence of Cl2 and Cl2O.  The recommended values, taken from the work of Burkholder [33], are listed in Table 35. In this work, several control experiments were carried out in order to check the internal consistency of the data.  More recent work by Jungkamp et al. [149] yields cross section values in excellent agreement with this recommendation.

Molina et al. [212] observed production of OH radicals in the laser photolysis of HOCl around 310 nm, and Butler and Phillips [45] found no evidence for O-atom production at 308 nm, placing an upper limit of ~0.02 for the primary quantum yield for the HCl + O channel.  Vogt and Schindler [318] used broadband photolysis in the 290 - 390 nm wavelength range, determining a quantum yield for OH production of >0.95.

###### Table 35.  Absorption Cross Sections of HOCl

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- | --- | --- |

| 200 | 7.1 | 262 | 9.3 | 322 | 4.6 |
| --- | --- | --- | --- | --- | --- |
| 202 | 6.1 | 264 | 8.3 | 324 | 4.3 |
| 204 | 5.6 | 266 | 7.4 | 326 | 4.2 |
| 206 | 5.4 | 268 | 6.6 | 328 | 3.8 |
| 208 | 5.5 | 270 | 6.0 | 330 | 3.5 |
| 210 | 5.7 | 272 | 5.5 | 332 | 3.3 |
| 212 | 6.1 | 274 | 5.2 | 334 | 3.1 |
| 214 | 6.6 | 276 | 4.9 | 336 | 2.7 |
| 216 | 7.5 | 278 | 4.8 | 338 | 2.5 |
| 218 | 8.4 | 280 | 4.7 | 340 | 2.4 |
| 220 | 9.7 | 282 | 4.8 | 342 | 2.1 |
| 222 | 10.9 | 284 | 4.8 | 344 | 1.8 |
| 224 | 12.2 | 286 | 4.9 | 346 | 1.8 |
| 226 | 13.5 | 288 | 5.1 | 348 | 1.7 |
| 228 | 15.0 | 290 | 5.3 | 350 | 1.5 |
| 230 | 16.4 | 292 | 5.4 | 352 | 1.3 |
| 232 | 17.7 | 294 | 5.6 | 354 | 1.3 |
| 234 | 18.7 | 296 | 5.8 | 356 | 1.2 |
| 236 | 19.7 | 298 | 5.9 | 358 | 1.0 |
| 238 | 20.3 | 300 | 6.0 | 360 | 0.8 |
| 240 | 20.7 | 302 | 6.0 | 362 | 1.0 |
| 242 | 21.0 | 304 | 6.1 | 364 | 1.0 |
| 244 | 20.5 | 306 | 6.0 | 366 | 0.9 |
| 246 | 19.6 | 308 | 6.0 | 368 | 0.8 |
| 248 | 18.6 | 310 | 5.9 | 370 | 0.8 |
| 250 | 17.3 | 312 | 5.7 | 372 | 1.0 |
| 252 | 15.9 | 314 | 5.6 | 374 | 0.8 |
| 254 | 14.6 | 316 | 5.4 | 376 | 0.8 |
| 256 | 13.2 | 318 | 5.1 | 378 | 0.6 |
| 258 | 11.8 | 320 | 4.9 | 380 | 0.8 |
| 260 | 10.5 |  |  |  |  |

### FNO + h  F + NO

The absorption cross sections have been measured by Burley et al. [41], who report their results in graphical form as well as in tabular form in 1 nm intervals, between 180 and 350 nm.  The spectrum shows vibronic structure at wavelengths longer than 250 nm.  The cross section values are listed in Table 36 in 2 nm intervals.  The quantum yield for decomposition is expected to be unity (Brandon et al., [27]; Reid et al., [253]).

###### Table 36.  Absorption Cross Sections of FNO

|  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |  (nm) | 1020 (cm2) |
| --- | --- | --- | --- | --- | --- |
| 180 | 52.4 | 236 | 3.09 | 292 | 11.9 |
| 182 | 51.7 | 238 | 2.76 | 294 | 7.11 |
| 184 | 50.7 | 240 | 2.25 | 296 | 9.15 |
| 186 | 49.4 | 242 | 2.08 | 298 | 22.0 |
| 188 | 47.5 | 244 | 1.74 | 300 | 15.6 |
| 190 | 45.1 | 246 | 1.65 | 302 | 25.4 |
| 192 | 42.7 | 248 | 1.41 | 304 | 8.85 |
| 194 | 40.0 | 250 | 1.54 | 306 | 11.8 |
| 196 | 37.3 | 252 | 1.25 | 308 | 32.2 |
| 198 | 33.8 | 254 | 1.23 | 310 | 15.5 |
| 200 | 30.5 | 256 | 1.36 | 312 | 31.6 |
| 202 | 27.7 | 258 | 1.58 | 314 | 12.3 |
| 204 | 24.8 | 260 | 1.30 | 316 | 11.0 |
| 206 | 22.2 | 262 | 1.64 | 318 | 25.5 |
| 208 | 19.9 | 264 | 2.03 | 320 | 15.2 |
| 210 | 17.6 | 266 | 1.96 | 32.3 | 40.2 |
| 212 | 15.8 | 268 | 2.10 | 324 | 17.8 |
| 214 | 13.9 | 270 | 2.81 | 326 | 12.1 |
| 216 | 12.3 | 272 | 4.47 | 328 | 9.39 |
| 218 | 10.7 | 274 | 3.97 | 330 | 12.9 |
| 220 | 9.35 | 276 | 4.24 | 332 | 13.0 |
| 222 | 8.32 | 278 | 3.41 | 334 | 19.3 |
| 224 | 7.22 | 280 | 8.26 | 336 | 13.1 |
| 226 | 6.30 | 282 | 7.58 | 338 | 8.96 |
| 228 | 5.44 | 284 | 7.26 | 340 | 5.65 |
| 230 | 4.68 | 286 | 5.17 | 342 | 3.81 |
| 232 | 4.10 | 288 | 10.4 | 344 | 2.68 |
| 234 | 3.52 | 290 | 17.0 | 346 | 1.96 |
|  |  |  |  | 348 | 1.48 |
|  |  |  |  | 350 | 1.18 |

### ClNO + h Cl + NO

Nitrosyl chloride has a continuous absorption extending beyond 650 nm.  There is good agreement between the work of Martin and Gareis [180] for the 240 to 420 nm wavelength region, of Ballash and Armstrong [14] for the 185 to 540 nm region, of Illies and Takacs [133] for the 190 to 400 nm region, and of Tyndall et al. [309] for the 190 to 350 region except around 230 nm, where the values of Ballash and Armstrong are larger by almost a factor of two.  Roehl et al. [259] measured the absorption cross sections between 350 and 650 nm at several temperatures between 223 and 343 K.  Their room temperature results agree to within 15% with those of Martin and Gareis [180], Ballash and Amstrong [14], and Tyndall et al. [309].  Table 37 lists the recommended cross sections: these are taken from the work of Tyndall et al. [309] between 190 and 350 nm (unchanged from the previous recommendation), and from Roehl et al. [259] beyond 350 nm.

The quantum yield for the primary photolytic process has been reviewed by Calvert and Pitts [47]. It is unity over the entire visible and near-ultraviolet bands.

###### Table 37.  Absorption Cross Sections of ClNO

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- | --- | --- | --- | --- |

| 190 | 4320 | 246 | 45.2 | 302 | 10.3 | 370 | 11.0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 192 | 5340 | 248 | 37.7 | 304 | 10.5 | 375 | 9.95 |
| 194 | 6150 | 250 | 31.7 | 306 | 10.8 | 380 | 8.86 |
| 196 | 6480 | 252 | 27.4 | 308 | 11.1 | 385 | 7.82 |
| 198 | 6310 | 254 | 23.7 | 310 | 11.5 | 390 | 6.86 |
| 200 | 5860 | 256 | 21.3 | 312 | 11.9 | 395 | 5.97 |
| 202 | 5250 | 258 | 19.0 | 314 | 12.2 | 400 | 5.13 |
| 204 | 4540 | 260 | 17.5 | 316 | 12.5 | 405 | 4.40 |
| 206 | 3840 | 262 | 16.5 | 318 | 13.0 | 410 | 3.83 |
| 208 | 3210 | 264 | 15.3 | 320 | 13.4 | 415 | 3.38 |
| 210 | 2630 | 266 | 14.4 | 322 | 13.6 | 420 | 2.89 |
| 212 | 2180 | 268 | 13.6 | 324 | 14.0 | 425 | 2.45 |
| 214 | 1760 | 270 | 12.9 | 326 | 14.3 | 430 | 2.21 |
| 216 | 1400 | 272 | 12.3 | 328 | 14.6 | 435 | 2.20 |
| 218 | 1110 | 274 | 11.8 | 330 | 14.7 | 440 | 2.20 |
| 220 | 896 | 276 | 11.3 | 332 | 14.9 | 445 | 2.07 |
| 222 | 707 | 278 | 10.7 | 334 | 15.1 | 450 | 1.87 |
| 224 | 552 | 280 | 10.6 | 336 | 15.3 | 455 | 1.79 |
| 226 | 436 | 282 | 10.2 | 338 | 15.3 | 460 | 1.95 |
| 228 | 339 | 284 | 9.99 | 340 | 15.2 | 465 | 2.25 |
| 230 | 266 | 286 | 9.84 | 342 | 15.3 | 470 | 2.50 |
| 232 | 212 | 288 | 9.71 | 344 | 15.1 | 475 | 2.61 |
| 234 | 164 | 290 | 9.64 | 346 | 15.1 | 480 | 2.53 |
| 236 | 120 | 292 | 9.63 | 348 | 14.9 | 485 | 2.33 |
| 238 | 101 | 294 | 9.69 | 350 | 14.2 | 490 | 2.07 |
| 240 | 82.5 | 296 | 9.71 | 355 | 13.6 | 495 | 1.78 |
| 242 | 67.2 | 298 | 9.89 | 360 | 12.9 | 500 | 1.50 |
| 244 | 55.2 | 300 | 10.0 | 365 | 12.0 |  |  |

### ClNO2 + h Products

The absorption cross sections of nitryl chloride, ClNO2, have been measured between 230 and 330 nm by Martin and Gareis [180], between 185 and 400 nm by Illies and Takacs [133], and between 270 and 370 nm by Nelson and Johnston [226], and by Ganske et al. [96] between 200 and 370 nm.  A major source of discrepancies in the data results from the presence of impurities.  Table 38 lists the recommended values, which are taken from Ganske et al.  Nelson and Johnston [226] report a value of one (within experimental error) for the quantum yield for production of chlorine atoms; they also report a negligible quantum yield for the production of oxygen atoms.

###### Table 38.  Absorption Cross Sections of ClNO2

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

190	2690	290	17.3

200	468	300	14.9

210	320	310	12.1

220	339	320	8.87

230	226	330	5.84

240	133	340	3.54

250	90.6	350	2.04

260	61.3	360	1.15

270	35.3	370	0.69

280	22.0

### ClONO + h Products

Measurements in the near-ultraviolet of the cross sections of chlorine nitrite (ClONO) have been made by Molina and Molina [200].  Their results are listed in Table 39.  The characteristics of the spectrum and the instability of ClONO strongly suggest that the quantum yield for decomposition is unity.  The Cl-O bond strength is only about 20 kilocalories, so that chlorine atoms are likely photolysis products.

###### Table 39.  Absorption Cross Sections of ClONO at 231 K

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

235	215.0	320	80.3

240	176.0	325	75.4

245	137.0	330	58.7

250	106.0	335	57.7

255	65.0	340	43.7

260	64.6	345	35.7

265	69.3	350	26.9

270	90.3	355	22.9

275	110.0	360	16.1

280	132.0	365	11.3

285	144.0	370	9.0

290	144.0	375	6.9

295	142.0	380	4.1

300	129.0	385	3.3

305	114.0	390	2.2

310	105.0	395	1.5

315	98.1	400	0.6

### ClONO2 + h Products

The recommended cross sections are taken from the work of Burkholder et al. [38]; the values are listed in Table 40, together with the parameters needed to compute their temperature dependency.  These values are in very good agreement with those reported by Molina and Molina [202], which provided the basis for the previous recommendation, and which supersedes the earlier work of Rowland, Spencer, and Molina [263].

The identity of the primary photolytic fragments has been investigated by several groups.  Smith et al. [287] report O + ClONO as the most likely products, using end product analysis and steady-state photolysis.  The results of Chang et al. [52], who employed the "Very Low Pressure Photolysis" (VLPPh) technique, indicate that the products are Cl + NO3.  Adler-Golden and Wiesenfeld [2], using a flash photolysis atomic absorption technique, find O-atoms to be the predominant photolysis product and report a quantum yield for Cl-atom production of less than 4%.  Marinelli and Johnston [178] report a quantum yield for NO3 production at 249 nm between 0.45 and 0.85, with a most likely value of 0.55; they monitored NO3 by tunable dye-laser absorption at 662 nm.  Margitan [173] used atomic resonance fluorescence detection of O- and Cl-atoms and found the quantum yield at 266 and at 355 nm to be 0.9 ± 0.1 for Cl-atom production and ~0.1 for O-atom production, with no discernible difference at the two wavelengths.  These results were confirmed by Knauth and Schindler [151], who used end-product analysis to infer the quantum yields.  Burrows et al. [44] report also Cl and NO3 as the photolysis products at 254 nm, with a quantum yield of unity within experimental error.  In contrast, Nikolaisen et al. [228] report relative branching ratios of 0.44 for production of ClO and NO2 and 0.56 for production of Cl and NO3 at wavelengths beyond 300 nm. Minton et al. [196], Nelson et al. [225], and Moore et al. [213] measured comparable yields for these two channels at 193, 248 and 308 nm, using a molecular beam technique.

The recommended quantum yield values for production of Cl + NO3 (1) and ClO + NO2 (2) are given at the bottom of Table 40 and are based on the work of Nelson et al. [225], Moore et al. [213], Nickolaisen et al. [228], and Ravishankara [248].  For wavelengths shorter than 308 nm the value of 1 is 0.6, and for 2 it is 0.4.  For longer wavelengths 1 increases linearly to 0.9 at 350 nm, with the corresponding decrease in 2 to 0.1.  There is no evidence for production of O + ClONO in the more recent work; the production of O-atoms reported in some of the earlier studies might have resulted from decomposition of excited NO3.

Recent work by Nickolaisen et al. [228] indicates that the photodissociation quantum yield is less than unity at wavelengths longer than about 330 nm, because of the formation of a long-lived intermediate that might be quenched under atmospheric conditions (a situation analogous to that of Cl2O).  Additional work is needed to address these issues, which have potentially important atmospheric consequences.

###### Table 40.  Absorption Cross Sections of ClONO2

|  (nm) | 1020 (cm2) | A1 | A2 |  |  (nm) | 1020 (cm2) | A1 | A2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| 196 | 310 | 9.90 (-5) | -8.38 (-6) |  | 316 | 1.07 | 5.07 (-3) | 1.56 (-5) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 198 | 294 | 6.72 (-5) | -8.03 (-6) |  | 318 | 0.947 | 5.24 (-3) | 1.69 (-5) |
| 200 | 282 | -5.34 (-6) | -7.64 (-6) |  | 320 | 0.831 | 5.40 (-3) | 1.84 (-5) |
| 202 | 277 | -1.19 (-4) | -7.45 (-6) |  | 322 | 0.731 | 5.55 (-3) | 2.00 (-5) |
| 204 | 280 | -2.60 (-4) | -7.50 (-6) |  | 324 | 0.647 | 5.68 (-3) | 2.18 (-5) |
| 206 | 288 | -4.12 (-4) | -7.73 (-6) |  | 326 | 0.578 | 5.80 (-3) | 2.36 (-5) |
| 208 | 300 | -5.62 (-4) | -8.05 (-6) |  | 328 | 0.518 | 5.88 (-3) | 2.54 (-5) |
| 210 | 314 | -6.96 (-4) | -8.41 (-6) |  | 330 | 0.466 | 5.92 (-3) | 2.70 (-5) |
| 212 | 329 | -8.04 (-4) | -8.75 (-6) |  | 332 | 0.420 | 5.92 (-3) | 2.84 (-5) |
| 214 | 339 | -8.74 (-4) | -9.04 (-6) |  | 334 | 0.382 | 5.88 (-3) | 2.96 (-5) |
| 216 | 345 | -9.03 (-4) | -9.24 (-6) |  | 336 | 0.351 | 5.80 (-3) | 3.05 (-5) |
| 218 | 341 | -8.86 (-4) | -9.35 (-6) |  | 338 | 0.326 | 5.68 (-3) | 3.10 (-5) |
| 220 | 332 | -8.28 (-4) | -9.38 (-6) |  | 340 | 0.302 | 5.51 (-3) | 3.11 (-5) |
| 222 | 314 | -7.31 (-4) | -9.34 (-6) |  | 342 | 0.282 | 5.32 (-3) | 3.08 (-5) |
| 224 | 291 | -6.04 (-4) | -9.24 (-6) |  | 344 | 0.264 | 5.07 (-3) | 2.96 (-5) |
| 226 | 264 | -4.53 (-4) | -9.06 (-6) |  | 346 | 0.252 | 4.76 (-3) | 2.74 (-5) |
| 228 | 235 | -2.88 (-4) | -8.77 (-6) |  | 348 | 0.243 | 4.39 (-3) | 2.42 (-5) |
| 230 | 208 | -1.13 (-4) | -8.33 (-6) |  | 350 | 0.229 | 4.02 (-3) | 2.07 (-5) |
| 232 | 182 | 6.18 (-5) | -7.74 (-6) |  | 352 | 0.218 | 3.68 (-3) | 1.76 (-5) |
| 234 | 158 | 2.27 (-4) | -7.10 (-6) |  | 354 | 0.212 | 3.40 (-3) | 1.50 (-5) |
| 236 | 138 | 3.72 (-4) | -6.52 (-6) |  | 356 | 0.205 | 3.15 (-3) | 1.27 (-5) |
| 238 | 120 | 4.91 (-4) | -6.14 (-6) |  | 358 | 0.203 | 2.92 (-3) | 1.06 (-5) |
| 240 | 105 | 5.86 (-4) | -5.98 (-6) |  | 360 | 0.200 | 2.70 (-3) | 8.59 (-6) |
| 242 | 91.9 | 6.64 (-4) | -6.04 (-6) |  | 362 | 0.190 | 2.47 (-3) | 6.38 (-6) |
| 244 | 81.2 | 7.33 (-4) | -6.27 (-6) |  | 364 | 0.184 | 2.22 (-3) | 3.66 (-6) |
| 246 | 71.6 | 8.03 (-4) | -6.51 (-6) |  | 366 | 0.175 | 1.93 (-3) | 2.42 (-7) |
| 248 | 62.4 | 8.85 (-4) | -6.59 (-6) |  | 368 | 0.166 | 1.62 (-3) | -3.62 (-6) |
| 250 | 56.0 | 9.84 (-4) | -6.40 (-6) |  | 370 | 0.159 | 1.33 (-3) | -7.40 (-6) |
| 252 | 50.2 | 1.10 (-3) | -5.93 (-6) |  | 372 | 0.151 | 1.07 (-3) | -1.07 (-5) |
| 254 | 45.3 | 1.22 (-3) | -5.33 (-6) |  | 374 | 0.144 | 8.60 (-4) | -1.33 (-5) |
| 256 | 41.0 | 1.33 (-3) | -4.73 (-6) |  | 376 | 0.138 | 6.73 (-4) | -1.54 (-5) |
| 258 | 37.2 | 1.44 (-3) | -4.22 (-6) |  | 378 | 0.129 | 5.01 (-4) | -1.74 (-5) |
| 260 | 33.8 | 1.53 (-3) | -3.79 (-6) |  | 380 | 0.121 | 3.53 (-4) | -1.91 (-5) |
| 262 | 30.6 | 1.62 (-3) | -3.37 (-6) |  | 382 | 0.115 | 2.54 (-4) | -2.05 (-5) |
| 264 | 27.8 | 1.70 (-3) | -2.94 (-6) |  | 384 | 0.108 | 2.25 (-4) | -2.11 (-5) |
| 266 | 25.2 | 1.78 (-3) | -2.48 (-6) |  | 386 | 0.103 | 2.62 (-4) | --2.11 (-5) |
| 268 | 22.7 | 1.86 (-3) | -2.00 (-6) |  | 388 | 0.0970 | 3.33 (-4) | -2.08 (-5) |
| 270 | 20.5 | 1.94 (-3) | -1.50 (-6) |  | 390 | 0.0909 | 4.10 (-4) | -2.05 (-5) |
| 272 | 18.5 | 2.02 (-3) | -1.01 (-6) |  | 392 | 0.0849 | 5.04 (-4) | -2.02 (-5) |
| 274 | 16.6 | 2.11 (-3) | -4.84 (-7) |  | 394 | 0.0780 | 6.62 (-4) | -1.94 (-5) |
| 276 | 14.9 | 2.02 (-3) | 9.02 (-8) |  | 396 | 0.0740 | 8.95 (-4) | -1.79 (-5) |
| 278 | 13.3 | 2.29 (-3) | 6.72 (-7) |  | 398 | 0.0710 | 1.14 (-3) | -1.61 (-5) |
| 280 | 11.9 | 2.38 (-3) | 1.21 (-6) |  | 400 | 0.0638 | 1.38 (-3) | -1.42 (-5) |
| 282 | 10.5 | 2.47 (-3) | 1.72 (-6) |  | 402 | 0.0599 | 1.63 (-3) | -1.20 (-5) |
| 284 | 9.35 | 2.56 (-3) | 2.21 (-6) |  | 404 | 0.0568 | 1.96 (-3) | -8.97 (-6) |
| 286 | 8.26 | 2.66 (-3) | 2.68 (-6) |  | 406 | 0.0513 | 2.36 (-3) | -5.15 (-6) |
| 288 | 7.24 | 2.75 (-3) | 3.09 (-6) |  | 408 | 0.0481 | 2.84 (-3) | -6.64 (-7) |
| 290 | 6.41 | 2.84 (-3) | 3.41 (-6) |  | 410 | 0.0444 | 3.38 (-3) | 4.47 (-6) |
| 292 | 5.50 | 2.95 (-3) | 3.74 (-6) |  | 412 | 0.0413 | 3.96 (-3) | 1.00 (-5) |
| 294 | 4.67 | 3.08 (-3) | 4.27 (-6) |  | 414 | 0.0373 | 4.56 (-3) | 1.60 (-5) |

Continued on next page

Table 40.   (Continued)

|  (nm) | 1020 (cm2) | A1 | A2 |  |  (nm) | 1020 (cm2) | A1 | A2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 296 | 4.09 | 3.25 (-3) | 5.13 (-6) |  | 416 | 0.0356 | 5.22 (-3) | 2.28 (-5) |
| 298 | 3.57 | 3.45 (-3) | 6.23 (-6) |  | 418 | 0.0317 | 5.96 (-3) | 3.07 (-5) |
| 300 | 3.13 | 3.64 (-3) | 7.36 (-6) |  | 420 | 0.0316 | 6.70 (-3) | 3.87 (-5) |
| 302 | 2.74 | 3.83 (-3) | 8.38 (-6) |  | 422 | 0.0275 | 7.30 (-3) | 4.58 (-5) |
| 304 | 2.39 | 4.01 (-3) | 9.30 (-6) |  | 424 | 0.0242 | 7.82 (-3) | 5.22 (-5) |
| 306 | 2.09 | 4.18 (-3) | 1.02 (-5) |  | 426 | 0.0222 | 8.41 (-3) | 5.95 (-5) |
| 308 | 1.83 | 4.36 (-3) | 1.11 (-5) |  | 428 | 0.0207 | 9.11 (-3) | 6.79 (-5) |
| 310 | 1.60 | 4.53 (-3) | 1.20 (-5) |  | 430 | 0.0189 | 9.72 (-3) | 7.52 (-5) |
| 312 | 1.40 | 4.71 (-3) | 1.30 (-5) |  | 432 | 0.0188 | 9.96 (-3) | 7.81 (-5) |
| 314 | 1.22 | 4.89 (-3) | 1.42 (-5) |  |  |  |  |  |

 (, T) =  (, 296) [1 + A1 (T - 296) + A2 (T - 296)2]; T in K

Quantum yields:	ClONO2 + h    Cl  +  NO3

1 = 0.6				( < 308 nm)

1 = 7.143x10-3  (nm) - 1.60		(308 nm <  < 364 nm)

1 = 1.0				( > 364 nm)

ClONO2 + h    ClO  +  NO2

2 = 1 - 1

### Halocarbon Absorption Cross Sections and Quantum Yields

The primary process in the photodissociation of chlorinated hydrocarbons is well established:  absorption of ultraviolet radiation in the lowest frequency band is interpreted as an n-* transition involving excitation to a repulsive electronic state (antibonding in C-Cl), which dissociates by breaking the carbon chlorine bond (Majer and Simons [169]).  As expected, the chlorofluoromethanes, which are a particular type of chlorinated hydrocarbons, behave in this fashion (Sandorfy [270]).  Hence, the quantum yield for photodissociation is expected to be unity for these compounds.  There are several studies that show specifically that this is the case for CF2Cl2, CFCl3, and CCl4.  These studies, which have been reviewed in CODATA [62], also indicate that at shorter wavelengths two halogen atoms can be released simultaneously in the primary process.

The absorption cross sections for various other halocarbons not listed in this evaluation have also been investigated:  CHCl2F by Hubrich et al. [128]; CClF3, CHCl3, CH2Cl2, CH2ClF, CF3CH2Cl, and CH3CH2Cl by Hubrich and Stuhl [127]; CHCl3, CHFCl2, C2HCl3, and C2H3Cl3 by Robbins [256]; CH2Cl2 and CHCl3 by Vanlaethem-Meuree et al. [314]; CHCl2F, CClF2CH2Cl, and CF3CH2Cl by Green and Wayne [111]; and CH2Br2 and CBrF2CF3 by Molina et al. [208].  Simon and co-workers have reported absorption cross section measurements over the temperature range 295-210 K for various other halocarbons not listed here.  These include the following:  CHCl3, CH2Cl2, CHFCl2, and CF3Cl by Simon et al. [283]. Orkin and Kasimovskaya [236] have measured cross sections at 295 K for CHF2Br, CHFBrCF3, CH2BrCF3, and CHClBrCF3 in the wavelength range 190-320 nm.

As before, the recommendation for the photodissociation quantum yield value is unity for all these species.

CF4 and C2F6 do not have any absorptions at wavelengths longer than 105 and 120 nm, respectively (Sauvageau et al. [271, 272]; Inn, [135]); therefore, they are not expected to photodissociate until they reach the mesosphere.

### CCl4 + h Products

### CCl3F (CFC-11) + h Products

### CCl2F2 (CFC-12) + h Products

Tables  41, 42, and 43 list the present recommendations for the cross sections of CCl4, CCl3F and CCl2F2, respectively.  These data are given by the mean of the values reported by various groups, i.e., Hubrich et al. [128], Hubrich and Stuhl [127], Vanlaethem-Meuree et al. [314, 315], and Green and Wayne [111], as well as those referred to in earlier evaluations (CODATA [62]).  Absorption cross sections for these species over the temperature range 295-210 K have also been reported by Simon et al. [283].  These results are in generally good agreement with the present recommendations.  Expressions for the temperature dependence of the CCl3F and CCl2F2 cross sections are given at the bottom of Tables 42 and 43, respectively.  These expressions are valid in the wavelength range of maximum solar photodissociation, i.e., about 190-210 nm, but may not exactly reproduce the experimental temperature dependences outside this wavelength range.  However, J-value calculations should not be affected.

###### Table 41.  Absorption Cross Sections of CCl4

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

174	995	218	21.8

176	1007	220	17.0

178	976	222	13.0

180	772	224	9.61

182	589	226	7.19

184	450	228	5.49

186	318	230	4.07

188	218	232	3.01

190	144	234	2.16

192	98.9	236	1.51

194	74.4	238	1.13

196	68.2	240	0.784

198	66.0	242	0.579

200	64.8	244	0.414

202	62.2	246	0.314

204	60.4	248	0.240

206	56.5	250	0.183

208	52.0	255	0.0661

210	46.6	260	0.0253

212	39.7	265	0.0126

214	33.3	270	0.0061

216	27.2	275	0.0024

###### Table 42.  Absorption Cross Sections of CCl3F

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

170	316	208	21.2

172	319	210	15.4

174	315	212	10.9

176	311	214	7.52

178	304	216	5.28

180	308	218	3.56

182	285	220	2.42

184	260	222	1.60

186	233	224	1.10

188	208	226	0.80

190	178	228	0.55

192	149	230	0.35

194	123	235	0.126

196	99	240	0.0464

198	80.1	245	0.0173

200	64.7	250	0.00661

202	50.8	255	0.00337

204	38.8	260	0.00147

206	29.3



T = 298 exp[1.0x10-4(-184.9)(T-298)]

Where 298 = cross section at 298 K

	:	nm

T	:	temperature, K

###### Table 43.  Absorption Cross Sections of CCl2F2

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

170	124	200	8.84

172	151	202	5.60

174	171	204	3.47

176	183	206	2.16

178	189	208	1.52

180	173	210	0.80

182	157	212	0.48

184	137	214	0.29

186	104	216	0.18

188	84.1	218	0.12

190	62.8	220	0.068

192	44.5	225	0.022

194	30.6	230	0.0055

196	20.8	235	0.0016

198	13.2	240	0.00029



T = 298 exp[4.1x10-4(-184.9)(T-298)]

Where 298 = cross section at 298 K

	:	nm

T	:	temperature, K

### CF2ClCFCl2 (CFC-113) + h Products

### CF2ClCF2Cl (CFC-114) + h Products

### CF3CF2Cl (CFC-115) + h Products

The recommended absorption cross section values for these species at 295 K and at 210 K are presented in Table 44, and are taken from Simon et al. [284].  These values are in good agreement with those reported by Hubrich and Stuhl [127], who also carried out measurements at lower temperatures.  They are also in good agreement with the data of Chou et al. [58], except that these authors report cross section values for CF3CF2Cl that are about 50% higher.  Also, for this species the temperature dependency is unimportant in the wavelength range of interest.

###### Table 44.  Absorption Cross Sections for CF2ClCFCl2, CF2ClCF2Cl and CF3CF2Cl

|  | 1020 (cm2) |  |
| --- | --- | --- |
|  | CF2ClCFCl2 | CF2ClCF2Cl | CF3CF2Cl |  |
| (nm) |  | 295 K | 210 K |  |  | 295 K | 210 K |  |  | 295 K |  |

172			69	69	5.65

174			55	55	4.05

176			43	43	2.85

178			34	34	2.05

180			26	26	1.45

182			19.8	19.8	1.05

184	118	118	15.0	15.0	0.75

186	104	104	11.0	11.0	0.53

188	83.5	83.5	7.80	7.72	0.38

190	64.5	64.5	5.35	5.03	0.27

192	48.8	48.8	3.70	3.28	0.19

194	36.0	36.0	2.56	2.13	0.13

196	26.0	24.3	1.75	1.39	0.090

198	18.3	15.9	1.20	0.88	0.063

200	12.5	10.1	0.80	0.55	0.044

202	8.60	6.54	0.54	0.34	0.031

204	5.80	4.09	0.37	0.22	0.021

206	4.00	2.66	0.24	0.13

208	2.65	1.68	0.16	0.084

210	1.8	1.12	0.104	0.051

212	1.15	0.696	0.068	0.031

214	0.760	0.452	0.044	0.020

216	0.505	0.298	0.029	0.012

218	0.318	0.184	0.019	0.007

220	0.220	0.125	0.012	0.004

222	0.145	0.081

224	0.095	0.053

226	0.063	0.034

228	0.041	0.022

230	0.027	0.014

### CCl2O + h Products, CClFO + h Products, and CF2O + h Products

The recommended absorption cross sections are listed in Table 45, as averages over the 500 cm-1 intervals commonly employed for atmospheric modeling (the wavelength given in the table is the center of the interval).  The values for CCl2O are based on the work of Gillotay et al. [105], who measured the cross sections between 170 and 320 nm at temperatures ranging from 210 to 295 K; the temperature effect is significant only at wavelengths longer than 250 nm.  These cross section values are in good agreement with those recommended earlier, which were based on the data of Chou et al. [57].  For CClFO the recommended values are based on this latter work between 184 and 199 nm, and they are taken from the work of Nölle et al. [231] at the longer wavelengths.  These workers measured the cross sections at temperatures ranging from 223 to 298 K; the temperature effect is not important for atmospheric photodissociation calculations, as is the case with CCl2O.  For CF2O the cross section values are taken from Molina and Molina [204] between 184 and 199 nm, and from Nölle et al. [232] at the longer wavelengths. These authors measured the cross sections at 296 K between 200 and 230 nm.

The photodissociation quantum yield for CCl2O is unity (Calvert and Pitts [47]); the spectrum is a continuum.  Similarly, the quantum yield for CClFO is taken as unity; the spectrum shows little structure.  In contrast, the CF2O spectrum is highly structured.Nnevertheless, its photodissociation quantum yield is also taken as unity, as reported by Nölle et al. [232].  The self-reaction of the CFO photodissociation product regenerates CF2O, and hence the apparent quantum yield is less than unity.

###### Table 45.  Absorption Cross Sections of CCl2O, CClFO and CF2O at 298 K

|  | 1020 (cm2) |
| --- | --- |
|  (nm) | CCl2O | CClFO | CF2O |
| 184.4 | 234 | - | - |
| 186.0 | 186 | 15.6 | 5.5 |
| 187.8 | 146 | 14.0 | 4.8 |
| 189.6 | 116 | 13.4 | 4.2 |
| 191.4 | 90.3 | 12.9 | 3.7 |
| 193.2 | 71.5 | 12.7 | 3.1 |
| 195.1 | 52.4 | 12.5 | 2.6 |
| 197.0 | 39.3 | 12.4 | 2.1 |
| 199.0 | 31.2 | 12.3 | 1.6 |
| 201.0 | 25.2 | 12.5 | 1.3 |
| 203.0 | 20.9 | 12.0 | 0.95 |
| 205.1 | 17.9 | 11.5 | 0.74 |
| 207.3 | 15.8 | 10.8 | 0.52 |
| 209.4 | 14.3 | 9.9 | 0.40 |
| 211.6 | 13.3 | 9.0 | 0.28 |
| 213.9 | 12.6 | 7.9 | 0.20 |
| 216.2 | 12.3 | 6.8 | 0.12 |
| 218.6 | 12.2 | 5.8 | 0.08 |
| 221.0 | 12.2 | 4.8 | 0.049 |
| 223.5 | 12.4 | 3.8 | 0.035 |
| 225.7 | 12.7 | 2.9 | 0.024 |
| 228.6 | 13.1 | 2.2 | 0.018 |

### CF3OH + h  Products

An upper limit of 10-21 cm2 has been determined experimentally by Molina and Molina [207] for the absorption cross sections of CF3OH in the 190 - 300 nm wavelength range.  This upper limit is in agreement with estimates based on similarities between CF3OH and CH3OH, as well as with quantum chemistry calculations, as reported by Schneider et al. [275].

### CH3Cl + h Products

The preferred absorption cross sections, listed in Table 46, are those given by Vanlaethem-Meuree et al. [314].  These values are in very good agreement with those reported by Robbins [255] at 298 K, as well as with those given by Hubrich et al. [128] at 298 K and 208 K, if the temperature trend is taken into consideration.  The results recently reported by Simon et al. [283] over the temperature range 295-210 K are in excellent agreement with the present recommendation.

###### Table 46.  Absorption Cross Sections of CH3Cl

|  | 1020 (cm2) |  |
| --- | --- | --- |
|  (nm) | 296 K | 279 K | 255 K |  |

186	24.7	24.7	24.7

188	17.5	17.5	17.5

190	12.7	12.7	12.7

192	8.86	8.86	8.86

194	6.03	6.03	6.03

196	4.01	4.01	4.01

198	2.66	2.66	2.66

200	1.76	1.76	1.76

202	1.09	1.09	1.09

204	0.691	0.691	0.691

206	0.483	0.475	0.469

208	0.321	0.301	0.286

210	0.206	0.189	0.172

212	0.132	0.121	0.102

214	0.088	0.074	0.059

216	0.060	0.048	0.033

### CH3CCl3 + h Products

The absorption cross sections have been measured by Robbins [256], Vanlaethem-Meuree et al. [316], Hubrich and Stuhl [127], and Nayak et al. [222]. Hubrich and Stuhl corrected the results to account for the presence of a UV-absorbing stabilizer in their samples, a correction that might account for the rather large discrepancy with the other three sets of measurements, that are in good agreement with each other.  The recommended values are taken from Vanlaethem-Meuree et al. [316], who report values at 210 K, 230 K, 250 K, 270 K and 295 K, every 2 nm, and in a separate table at wavelengths corresponding to the wavenumber intervals generally used in stratospheric photodissociation calculations.  Table 47 lists the values at 210 K, 250 K and 295 K, every 5 nm; the odd wavelength values were computed by linear interpolation.  These values agree within 10% with those reported by Nayak et al. at the atmospherically relevant 200-210 nm wavelength range; these authors carried out measurements between 160 and 260 nm, from 220 to 330 K.

###### Table 47.  Absorption Cross Sections of CH3CCl3

|  | 1020 (cm2) |  |
| --- | --- | --- |
|  (nm) | 295 K | 250 K | 210 K |  |

185	265	265	265

190	192	192	192

200	81.0	81.0	81.0

205	46.0	44.0	42.3

210	24.0	21.6	19.8

215	10.3	8.67	7.47

220	4.15	3.42	2.90

225	1.76	1.28	0.97

230	0.700	0.470	0.330

235	0.282	0.152	0.088

240	0.102	0.048	0.024

### CHClF2 (HCFC-22) + h Products

The absorption cross sections of CHClF2 (HCFC-22) have been measured at room temperature by Robbins and Stolarski [257] and by Chou et al. [59], at 208 K and 218 K by Hubrich et al. [128], and between 210 and 295 K by Simon et al. [283].  The agreement between these groups is reasonable.  The preferred absorption cross sections, listed in Table 48, are taken from work of Simon et al.  Photolysis of CHClF2 is rather unimportant throughout the atmosphere:  reaction with OH radicals is the dominant destruction process.

###### Table 48.  Absorption Cross Sections of CHClF2

|  |  |  | 1020 (cm2) |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| (nm) | 295 K | 270 K | 250 K | 230 K | 210 K |  |

174	5.72	5.72	5.72	5.72	5.72

176	4.04	4.04	4.04	4.04	4.04

178	2.76	2.76	2.76	2.76	2.76

180	1.91	1.91	1.91	1.91	1.91

182	1.28	1.28	1.28	1.28	1.28

184	0.842	0.842	0.842	0.842	0.842

186	0.576	0.576	0.576	0.576	0.576

188	0.372	0.372	0.372	0.372	0.372

190	0.245	0.245	0.245	0.245	0.242

192	0.156	0.156	0.156	0.152	0.148

194	0.103	0.102	0.099	0.096	0.093

196	0.072	0.069	0.067	0.064	0.062

298	0.048	0.045	0.043	0.041	0.039

200	0.032	0.029	0.029	0.0259	0.0159

202	0.0220	0.0192	0.0184	0.0169	0.0159

204	0.0142	0.0121	0.0114	0.0104	0.0096

### CH3CF2Cl (HCFC-142b) + h Products

The preferred absorption cross sections at 298 K, listed in Table 49, are the mean of the values reported by Gillotay and Simon [103] and Orlando et al. [238] over the wavelength range where the agreement is better than a factor of 2.  At lower wavelengths the agreement is much better; e.g., at 200 nm the agreement is within 5%.  Green and Wayne [111] and Hubrich and Stuhl [127] have also measured the cross sections in the ranges 185-200 nm and 160-230 nm, respectively.  The results of Green and Wayne are very different from the recommended value and were not considered for this evaluation.  The results of Hubrich and Stuhl (reported at 5 nm intervals) are in reasonable agreement with the more recent studies of Gillotay and Simon and of Orlando et al.  The temperature dependence of the cross sections has been measured by Orlando et al. and by Gillotay and Simon, but it has not been included in this evaluation.

### CF3CHCl2 (HCFC-123) + h Products

The preferred absorption cross sections at 298 K, listed in Table 49, are the mean of the values reported by Gillotay and Simon [103] and Orlando et al. [238].  The agreement is quite good over the entire wavelength range.  The measurements by Green and Wayne [111] over the range 185-205 nm are in reasonable agreement with the recommended values.  The temperature dependence of the cross sections has been measured by Orlando et al. and by Gillotay and Simon, but it is not included here.  Recent work by Nayak et al. ([221] yields values that are in good agreement (within 10%) with this recommendation.

### CF3CHFCl (HCFC-124) + h Products

The preferred values are the average of those reported by Orlando et al. [238] and Gillotay and Simon  [102], these being the only available sets of measurements between 190 and 230 nm.  The data are listed in Table 49.  The temperature dependence of the cross section has been measured by both groups but has not been evaluated here.  The quantum yield for the dissociation to give Cl atoms is expected to be unity.

### CH3CFCl2 (HCFC-141b) + h Products

The preferred absorption cross sections listed in Table 49 are taken from the work of Fahr et al. [86], who investigated the spectrum at 298 K both for the gas and liquid phases.  The agreement with the values reported by Gillotay and Simon [103] is very good; it is not as good with the results of Talkudar et al. [299].  These last two groups also report the temperature dependence of the cross sections down to 210 K.

### CF3CF2CHCl2 (HCFC-225ca) + h Products

### CF2ClCF2CHFCl (HCFC-225cb) + h Products

Table 50 lists the absorption cross sections for these molecules at 298 K, taken from the work of Braun et al. [28].  These values have been fitted with a mathematical expression for the wavelength range from 170 to 250 nm, for each of the two molecules. The expressions are listed in the original publication.  The authors also measured the cross sections in the liquid phase.

###### Table 49.  Absorption Cross Sections of Hydrochlorofluoroethanes at 298 K

|  | 1020 (cm2) at 298 K |  |
| --- | --- | --- |
|  (nm) | CH3CFCl2 (141b) | CH3CF2Cl (142b) | CF3CHCl2 (123) | CF3CHFCl (124) |  |

190	83.8	0.94	59.0	0.77

192	64.1	0.66	44.5	0.55

194	47.4	0.46	32.9	0.39

196	34.0	0.31	23.6	0.27

198	23.8	0.21	16.9	0.18

200	16.4	0.14	11.9	0.13

202	11.1	0.09	8.3	0.086

204	7.4	0.061	5.7	0.060

206	4.9	0.039	4.0	0.040

208	3.2	0.026	2.7	0.027

210	2.1	0.017	1.8	0.019

212	1.4	0.010	1.3	0.012

214	0.89	0.007	0.87	0.008

216	0.57	0.004	0.61	0.006

218	0.37	0.003	0.40	0.004

220	0.24	0.002	0.28	0.003

###### Table 50.  Absorption Cross Sections of CF3CF2CHCl2 and CF2ClCF2CHFCl

|  | 1020 (cm2) |  |
| --- | --- | --- |
|  (nm) | CF3CF2CHCl2 (225ca) | CF2ClCF2CHFCl (225cb) |  |

160	269	188

165	197	145

170	183	91

175	191	47

180	177	21

185	129	9.1

190	74	3.5

195	37	1.4

200	16	0.63

205	6.9	0.33

210	2.9	0.25

215	1.2

220	0.46

225	0.17

230	0.065

235	0.025

239	0.011

### CH3OCl + h  Products

The absorption cross sections of CH3OCl have been determined by Crowley et al. [75] and by Jungkamp et al. [149].  The preferred cross sections, listed in Table 51, are the mean of the values reported by these two groups.  The agreement between the two sets of measurements is excellent at wavelengths longer than 250 nm; at the maximum near 230 nm the results of Jungkamp et al. are about 15% smaller.

###### Table 51  Absorption Cross Sections of CH3OCl

|  | 1020  |  | 1020  |  | 1020  |
| --- | --- | --- | --- | --- | --- |
| (nm) | (cm2) | (nm) | (cm2) | (nm) | (cm2) |
| 230 | 14.9 | 290 | 1.32 | 350 | 0.662 |
| 232 | 15.4 | 292 | 1.34 | 352 | 0.611 |
| 234 | 15.7 | 294 | 1.35 | 354 | 0.574 |
| 236 | 15.9 | 296 | 1.37 | 356 | 0.529 |
| 238 | 15.8 | 298 | 1.40 | 358 | 0.482 |
| 240 | 15.5 | 300 | 1.43 | 360 | 0.445 |
| 242 | 14.9 | 302 | 1.45 | 362 | 0.411 |
| 244 | 14.2 | 304 | 1.47 | 364 | 0.389 |
| 246 | 13.2 | 306 | 1.48 | 366 | 0.356 |
| 248 | 12.2 | 308 | 1.49 | 368 | 0.331 |
| 250 | 11.1 | 310 | 1.49 | 370 | 0.298 |
| 252 | 9.96 | 312 | 1.48 | 372 | 0.273 |
| 254 | 8.86 | 314 | 1.47 | 374 | 0.246 |
| 256 | 7.77 | 316 | 1.46 | 376 | 0.225 |
| 258 | 6.80 | 318 | 1.43 | 378 | 0.209 |
| 260 | 5.87 | 320 | 1.41 | 380 | 0.202 |
| 262 | 5.05 | 322 | 1.37 | 382 | 0.186 |
| 264 | 4.31 | 324 | 1.33 | 384 | 0.17 |
| 266 | 3.69 | 326 | 1.30 | 386 | 0.16 |
| 268 | 3.16 | 328 | 1.24 | 388 | 0.15 |
| 270 | 2.71 | 330 | 1.20 | 390 | 0.13 |
| 272 | 2.35 | 332 | 1.14 | 392 | 0.14 |
| 274 | 2.06 | 334 | 1.09 | 394 | 0.13 |
| 276 | 1.83 | 336 | 1.04 |  |  |
| 278 | 1.64 | 338 | 0.980 |  |  |
| 280 | 1.53 | 340 | 0.918 |  |  |
| 282 | 1.42 | 342 | 0.875 |  |  |
| 284 | 1.37 | 344 | 0.822 |  |  |
| 286 | 1.33 | 346 | 0.760 |  |  |
| 288 | 1.32 | 348 | 0.709 |  |  |

### BrO + h Br + O

The BrO radical has a banded spectrum in the 290-380 nm range.  The strongest absorption feature is around 338 nm.  The measured cross sections are both temperature- and resolution-dependent.  As an example, the spectrum measured by Wahner et al. [319] is shown in Figure 5.  The bands are due to a vibrational progression in the A  X system, and the location of the bands, along with the assignments and cross sections measured using 0.4 nm resolution, are shown in Table 52.  BrO is expected to dissociate upon light absorption.  As a guide, the cross sections averaged over 5 nm wavelength intervals are taken from the work of Cox et al. [73], and are listed in Table 53.  These authors estimate a BrO lifetime against atmospheric photodissociation of ~20 seconds at the earth's surface, for a solar zenith angle of 30°.

The earlier BrO cross section measurements were carried out mostly around 338 nm, and these have been reviewed by CODATA ([61, 62]).

###### Table 52.  Absorption Cross Sections at the Peak of Various

Bands in the A  X Spectrum of BrO

|  | 1020 (cm2) |  |
| --- | --- | --- |
| ', " |  (nm) |  | 298 K | 223 K |  |

13,0	313.5	712	938

12,0	317.0	1010	1360

11,0	320.8	1180	1570

10,0	325.0	1130	1430

9,0	329.1	1130	1390

8,0	333.5	1210	1470

7,0	338.3	1550	1950

6,0	343.7	935	1110

5,0	348.8	703	896

4,0	354.7	722	1050

3,0	360.4	264	344

2,0	367.7	145	154

1,0	374.5	90	96

Spectral resolution is 0.4 nm, fwhm.

###### Table 53.  Absorption Cross Sections of BrO

|  (nm) | 1020 (cm2) average |
| --- | --- |

300 - 305	200

305 - 310	259

310 - 315	454

315 - 320	391

320 - 325	600

325 - 330	753

330 - 335	628

335 - 340	589

340 - 345	515

345 - 350	399

350 - 355	228

355 - 360	172

360 - 365	161

365 - 370	92

370 - 375	51

Figure 5.  Absorption Spectrum of BrO

### HOBr + h Products

The absorption spectrum of HOBr has been measured by Orlando and Burkholder [237], Deters et al. [84], Benter et al. [20], and Rattigan et al. [247].  The spectra cluster into two groups. Orlando and Burkholder, Deters et al., and Benter et al. agree reasonably well between 240 and 400 nm and show a sharp decrease in cross section above 400 nm. In contrast, the cross sections of Rattigan et al. are roughly 50% larger between 300 and 400 nm. Their spectrum also shows a pronounced absorption tail beyond 400 nm, leading to atmospheric photolysis rates for HOBr that are about a factor of 3 larger than those derived from the other studies. The long-wavelength tail observed by Rattigan et al. confirms the observations of Barnes et al. [16], who showed that laser photolysis of HOBr between 440-600 nm gives rise to OH fragments, implying the existence of weak HOBr absorption bands. The presence of a weak band beyond 400 nm is attributable to the presence of a forbidden transition from the ground electronic state to a triplet state predicted in ab initio  calculations by Francisco et al. [91]. The differences in the spectral shapes are probably attributable to impurities such as Br2O and Br2. However, these cannot entirely explain the large differences in cross sections at the peaks of the absorption bands.

Because there is strong evidence in support of an absorption tail beyond 400 nm the recommendation (Table 54) is based on the study of Rattigan et al. The discrepancies in the measured cross sections between this work and the other studies throughout the measured spectral range require the assignment of large uncertainties (see Table 5). Additional work is required to resolve the significant discrepancies between the published spectra.

Benter et al. measured quantum yields for HOBr photolysis at 261 and 363 nm (the peaks of the strongest absorption bands). The observed quantum yield for Br formation at 363 nm was greater than 0.95. HBr was not detected as a photolysis product. As indicated above, the laser photofragment study of Barnes et al. also showed that OH was the major photolysis product at wavelengths beyond 400 nm.

###### Table 54.  Absorption Cross Sections of HOBr

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- | --- | --- |
| 240 | 6.7 | 330 | 11 | 420 | 1.3 |
| 245 | 5.2 | 335 | 11.5 | 425 | 1.1 |
| 250 | 6.7 | 340 | 12 | 430 | 0.9 |
| 255 | 9.9 | 345 | 12.3 | 435 | 0.8 |
| 260 | 14.1 | 350 | 12.5 | 440 | 0.7 |
| 265 | 18.9 | 355 | 12.2 | 445 | 0.7 |
| 270 | 23.9 | 360 | 11.6 | 450 | 0.7 |
| 275 | 28 | 365 | 10.7 | 455 | 0.7 |
| 280 | 30.4 | 370 | 9.6 | 460 | 0.6 |
| 285 | 30.8 | 375 | 8.4 | 465 | 0.5 |
| 290 | 28.7 | 380 | 7.4 | 470 | 0.5 |
| 295 | 25.2 | 385 | 6.2 | 475 | 0.4 |
| 300 | 20.9 | 390 | 5.1 | 480 | 0.3 |
| 305 | 16.8 | 395 | 4.1 | 485 | 0.3 |
| 310 | 13.8 | 400 | 3.3 | 490 | 0.2 |
| 315 | 11.8 | 405 | 2.6 | 495 | 0.1 |
| 320 | 10.8 | 410 | 2.0 | 500 | 0.1 |
| 325 | 10.6 | 415 | 1.6 | 505 | .05 |

### BrONO2 + h Products

The bromine nitrate cross sections have been measured at room temperature by Spencer and Rowland [290] in the wavelength region 186-390 nm, and by Burkholder et al. [37] from 200-500 nm.  The results from both studies are in excellent agreement over the range of spectral overlap. The recommended cross sections (Table 55) are taken from Burkholder et al.

The only study of photolysis products is that of Nickolaisen and Sander [227].  In that study, quantum yields for the Br + NO3 and BrO + NO2 channels were measured using broadband photolysis in quartz (>200 nm) and pyrex (>300 nm) reaction cells with the assumption that these were the only reaction pathways. The quantum yields were BrO+NO2 = 0.71 and Br+NO3 = 0.29.

###### Table 55.  Absorption Cross Sections of BrONO2

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- | --- | --- |
| 200 | 530 | 305 | 15 | 410 | 1.6 |
| 205 | 440 | 310 | 13 | 415 | 1.4 |
| 210 | 340 | 315 | 12 | 420 | 1.3 |
| 215 | 290 | 320 | 10 | 425 | 1.3 |
| 220 | 260 | 325 | 9.3 | 430 | 1.2 |
| 225 | 240 | 330 | 8.4 | 435 | 1.1 |
| 230 | 210 | 335 | 7.8 | 440 | 1.1 |
| 235 | 180 | 340 | 7.2 | 445 | 1.0 |
| 240 | 140 | 345 | 6.8 | 450 | 0.91 |
| 245 | 100 | 350 | 6.3 | 455 | 0.80 |
| 250 | 75 | 355 | 5.8 | 460 | 0.70 |
| 255 | 55 | 360 | 5.4 | 465 | 0.59 |
| 260 | 42 | 365 | 4.9 | 470 | 0.49 |
| 265 | 35 | 370 | 4.4 | 475 | 0.38 |
| 270 | 31 | 375 | 3.9 | 480 | 0.29 |
| 275 | 28 | 380 | 3.4 | 485 | 0.22 |
| 280 | 26 | 385 | 3.0 | 490 | 0.14 |
| 285 | 24 | 390 | 2.6 | 495 | 0.086 |
| 290 | 22 | 395 | 2.2 | 500 | 0.041 |
| 295 | 20 | 400 | 2.0 |  |  |
| 300 | 17 | 405 | 1.7 |  |  |

### BrCl + h  Br + Cl

The recommended absorption cross sections are given by the expression listed at the bottom of Table 56, which is take from the work of Maric et al. [176].  For convenience, some room temperature values are also listed in the table.  Hubinger and Nee [126] have also measured the cross sections at room temperature.  Their results are in excellent agreement with the recommended values.

###### Table 56.  Absorption Cross Sections of BrCl at 298K

|  | 1020 |  | 1020 |
| --- | --- | --- | --- |
| (nm) | (cm2) | (nm) | (cm2) |
| 200 | 2.4 | 390 | 34.7 |
| 210 | 4.0 | 400 | 28.2 |
| 220 | 5.4 | 410 | 21.9 |
| 230 | 6.0 | 420 | 16.9 |
| 240 | 5.1 | 430 | 14.2 |
| 250 | 3.7 | 440 | 12.4 |
| 260 | 2.5 | 450 | 11.1 |
| 270 | 1.5 | 460 | 9.6 |
| 280 | 1.2 | 470 | 8.0 |
| 290 | 0.63 | 480 | 6.8 |
| 300 | 0.61 | 490 | 5.0 |
| 310 | 1.2 | 500 | 3.8 |
| 320 | 2.8 | 510 | 3.1 |
| 330 | 7.4 | 520 | 2.3 |
| 340 | 14.2 | 530 | 1.5 |
| 350 | 22.9 | 540 | 0.96 |
| 360 | 33.3 | 550 | 0.76 |
| 370 | 38.7 | 560 | 0.31 |
| 380 | 38.5 |  |  |

where  in nm and Tinnm < nm; 300K > T > 195K.

### CH3Br + h Products

Table 57 lists the recommended absorption cross sections at 298 K, taken from Gillotay and Simon [100].  These authors measured the cross sections down to 210 K; for < 210 nm the temperature effect is negligible.  Molina et al. [208] and Robbins [255] have also measured the absorption cross sections for this molecule at room temperature; the agreement among the three studies is very good.

###### Table 57.  Absorption Cross Sections of CH3Br

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- |

190	44	230	15

192	53	232	12

194	62	234	9.9

196	69	236	7.6

198	76	238	5.9

200	79	240	4.5

202	80	242	3.3

204	79	244	2.5

206	77	246	1.8

208	73	248	1.3

210	67	250	0.96

212	61	252	0.69

214	56	254	0.49

216	49	256	0.34

218	44	258	0.23

220	38	260	0.16

222	32

224	28

226	23

228	19

### CHBr3 + h Products

The absorption cross sections have been measured by Gillotay et al. [99] in the wavelength range from 190 to 310 nm, between 295 K and 240 K, and more recently by Moortgat et al. [215] in the 245 - 360 nm range at temperatures between 296 K and 256 K; the agreement in the overlap region is excellent.  The recommended cross sections at room temperature are listed in Table 58.  This new recommendation combines the two sets of values: between 190 and 285 nm they are taken from Gillotay et al. and at longer wavelengths from Moortgat et al.  Table 58 also lists an expression, taken from Moortgat et al., that yields the cross sections as a function of temperature for wavelengths longer than 290 nm, the atmospherically important range.  At these longer wavelengths the cross sections are relatively small; the presence of impurities as well as optical artifacts arising, e.g., from adsorption of CHBr3 on the cell windows complicate the measurements.  Hence, additional investigations of the spectra would be useful.

###### Table 58.  Absorption Cross Sections of CHBr3 at 296 K

|  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |  (nm) | 1020  (cm2) |
| --- | --- | --- | --- | --- | --- |
| 190 | 399 | 248 | 194 | 306 | 0.298 |
| 192 | 360 | 250 | 174 | 308 | 0.226 |
| 194 | 351 | 252 | 158 | 310 | 0.171 |
| 196 | 366 | 254 | 136 | 312 | 0.127 |
| 198 | 393 | 256 | 116 | 314 | 0.0952 |
| 200 | 416 | 258 | 99 | 316 | 0.0712 |
| 202 | 433 | 260 | 83 | 318 | 0.0529 |
| 204 | 440 | 262 | 69 | 320 | 0.0390 |
| 206 | 445 | 264 | 57 | 322 | 0.0289 |
| 208 | 451 | 266 | 47 | 324 | 0.0215 |
| 210 | 468 | 268 | 38 | 326 | 0.0162 |
| 212 | 493 | 270 | 31 | 328 | 0.0121 |
| 214 | 524 | 272 | 25 | 330 | 0.0092 |
| 216 | 553 | 274 | 20 | 332 | 0.0069 |
| 218 | 574 | 276 | 16 | 334 | 0.0052 |
| 220 | 582 | 278 | 12 | 336 | 0.0040 |
| 222 | 578 | 280 | 9.9 | 338 | 0.0031 |
| 224 | 558 | 282 | 7.8 | 340 | 0.0024 |
| 226 | 527 | 284 | 6.1 | 342 | 0.0018 |
| 228 | 487 | 286 | 4.81 | 344 | 0.0013 |
| 230 | 441 | 288 | 3.75 | 346 | 0.0010 |
| 232 | 397 | 290 | 2.88 | 348 | 0.00080 |
| 234 | 362 | 292 | 2.22 | 350 | 0.00064 |
| 236 | 324 | 294 | 1.70 | 352 | 0.00054 |
| 238 | 295 | 296 | 1.28 | 354 | 0.00046 |
| 240 | 273 | 298 | 0.951 | 356 | 0.00032 |
| 242 | 253 | 300 | 0.719 | 358 | 0.00024 |
| 244 | 234 | 302 | 0.530 | 360 | 0.00017 |
| 246 | 214 | 304 | 0.394 | 362 | 0.00013 |

(,T) = exp [(0.06183 - 0.000241 ) (273 - T) - (2.376 + 0.14757 )]

: nm; T: K; : cm2

290 nm <  < 340 nm; 210 K < T < 300 K

### CF3Br (Halon-1301) + h Products

The preferred absorption cross sections at 298 K, listed in Table 59, are the mean of the values reported by Gillotay and Simon [101] at 2 nm intervals and Burkholder et al. [40] at 1 nm intervals over the wavelength range where the agreement is acceptable, i.e., better than 70%.  At longer wavelengths Burkholder et al. [40] measure larger values than those reported by Gillotay and Simon.  Molina et al. [208] have also measured these cross sections, which agree better with Gillotay and Simon.  However, the agreement in the wavelength range 190-230 nm among the three studies is excellent.  More recently, Orkin and Kasimovskaya [236] measured the cross sections at room temperature; their results are in good agreement with the recommended values over the wavelength region relevant for atmospheric photodissociation, i.e., ~ 200-220 nm.  The temperature dependence of the cross sections has been measured by Gillotay and Simon as well as Burkholder et al. [40].  The agreement between these two studies is poor.  We have not evaluated the temperature dependence of the cross sections, and the readers are referred to the original publications for this information.  For all the bromofluoromethanes, photolysis is expected to cleave the C-Br bond with unit quantum efficiency. Orkin and Kasimovskaya  measured the cross sections in the wavelength range 190-320 nm, at 295 K; their results agree with the recommendation.

### CF2Br2 (Halon-1202) + h Products

The preferred absorption cross sections at 298 K, listed in Table 59, are the mean of the values reported by Gillotay and Simon [101] at 2 nm intervals and Burkholder et al. [40] at 1 nm intervals over the wavelength range where the agreement is no more than a factor of 2.  At wavelengths longer than ~250 nm, Burkholder et al. [40] measured cross sections larger than those reported by Gillotay and Simon [101] and Molina et al. [208].  The discrepancy increases with wavelength and is more than a factor of 2 beyond 280 nm.  However, the agreement between all three measurements is acceptable below 250 nm.  The values of Molina et al. agree with those of Gillotay and Simon over the entire range of wavelengths.  The temperature dependence of the cross sections has been measured by Gillotay and Simon as well as Burkholder et al. [40].  The agreement between these two studies is poor.  Orkin and Kasimovskaya [236] measured the cross sections in the wavelength range 190-320 nm at 295 K; their results agree with the recommended values.

The quantum yield for the dissociation of CF2Br2 has been measured to be unity at 206, 248 and 308 nm by Molina and Molina [205], independent of pressure, in contrast to an earlier report by Walton [323] that the quantum yield at 265 nm decreases from unity when the system pressure is raised to 50 torr of CO2.  Orkin and Kasimovskaya [236] measured the cross sections in the wavelength range 190-320 nm, at 295 K; their results agree with the recommendation.

### CF2BrCF2Br (Halon-2402) + h Products

The preferred absorption cross sections at 298 K, listed in Table 59, are the mean of the values reported by Gillotay et al. [104] at 2 nm intervals and Burkholder et al. [40] at 1 nm intervals over the wavelength range where the agreement is acceptable, i.e., ~70%.  At longer wavelengths, Burkholder et al. [40] measured larger cross sections than those measured by Gillotay et al.  Molina et al. [208] have also measured these cross sections, and they agree with the results of Gillotay et al. at longer wavelengths.  The agreement between the three studies at wavelengths shorter than 250 nm is good.  The results of Robbins [256] and of Orkin and Kasimovskaya [236] are in good agreement with the recommended values.

The temperature dependence of the cross sections has been measured by Gillotay et al. and Burkholder et al.   The agreement between the two studies is poor at longer wavelengths.  We have not evaluated the temperature dependence of the cross section, and the readers are referred to the investigators for the information. Orkin and Kasimovskaya  measured the cross sections in the wavelength range 190-320 nm, at 295 K; their results agree with the recommendation.

###### Table 59.  Absorption Cross Sections of CF2ClBr, CF2Br2, CF3Br, and CF2BrCF2Br at 298 K

|  | 1020 (cm2) |  |
| --- | --- | --- |
|  (nm) | CF2ClBr (1211) | CF2Br2 (1202) | CF3Br (1301) | CF2BrCF2Br (2402) |  |

190	47	114	6.4	109

192	58	109	7.5	114

194	70	100	8.5	119

196	83	91	9.5	122

198	96	82	10.4	124

200	112	75	11.2	124

202	118	72	11.8	124

204	121	74	12.2	120

206	122	81	12.4	117

208	121	93	12.4	112

210	117	110	12.0	106

212	112	136	11.4	100

214	106	155	10.7	92

216	98	180	9.8	85

218	90	203	8.8	77

220	81	224	7.7	69

222	72	242	6.7	61

224	64	251	5.7	54

226	56	253	4.7	47

228	49	250	3.8	40

230	42	241	3.1	35

232	36	227	2.4	29

234	31	209	1.9	24

236	26	189	1.4	20

238	22	168	1.1	16

240	18	147	0.81	13

242	15	126	0.59	11

244	12	106	0.43	8.4

246	10	88	0.31	6.7

248	8.0	73	0.22	5.2

250	6.5	59	0.16	4.1

252	5.1	47	0.11	3.1

254	4.0	37	0.076	2.3

256	3.2	29	0.053	1.8

258	2.4	23	0.037	1.3

260	1.9	18	0.026	0.95

262	1.4	13	0.018	0.71

264	1.1	10	0.012	0.53

266	0.84	7.6	0.009	0.39

268	0.63	5.7	0.006	0.28

270	0.48	4.2		0.21

272	0.36	3.1		0.16

Continued on next page. . .

Table 59.  (Continued)

|  | 1020 (cm2) |  |
| --- | --- | --- |
|  (nm) | CF2ClBr (1211) | CF2Br2 (1202) | CF3Br (1301) | CF2BrCF2Br (2402) |  |

274	0.27	2.2		0.11

276	0.20	1.6		0.082

278	0.15	1.2		0.060

280	0.1	0.89		0.044

282	0.079	0.65

284	0.058	0.48

286	0.043	0.34

288	0.031	0.24

290		0.18

292		0.13

294		0.096

296		0.068

298		0.050

300		0.036

### CF2ClBr (Halon-1211) + h Products

The preferred absorption cross sections at 298 K, listed in Table 59, are the mean of the values reported by Gillotay and Simon [101] at 2 nm intervals and Burkholder et al. [40] at 1 nm intervals.  Molina et al. [208], Giolando et al. [106], and Orkin and Kasimovskaya have also measured the cross sections at 5 nm and 10 nm intervals, respectively.  The agreement among all these studies is quite good.

The temperature dependence of the cross sections has been measured by Gillotay and Simon, as well as Burkholder et al.   The agreement between the two studies is poor.  We have not evaluated the temperature dependence of the cross section, and the readers are referred to the original publications for this information.  Orkin and Kasimovskaya measured the cross sections in the wavelength range 190-320 nm, at 295 K; their results agree with the recommendation.

### CF3I + h CF3 + I

Table 60 lists the recommended absorption cross sections:  The 298 K values are the average of the data from Solomon et al. [288] and Fahr et al. [87].  The fit of the temperature dependent data of Fahr et al. agrees with that of Solomon et al. to better than 15% at all temperatures and wavelengths.  The B values in the table are from Solomon et al.  The temperature effect is significant at the longer wavelengths: at 350 nm, the cross sections decrease by about 30% at 253 K and by about 40% at 233 K, compared to the room temperature value.  Walters et al. [322] have also measured the cross sections as a function of temperature at the atmospherically important wavelengths beyond 300 nm.  The Fahr et al. values are about 18% higher than those of Walters et al.; however, at the longer wavelengths and lower temperatures (253 K) the disagreement is larger.

###### Table 60.  Absorption Cross Sections of CF3I at 298 K and temperature coefficient B*

|  (nm) | 1020 (cm2) | Bx103 (K-1) |  |  (nm) | 1020 (cm2) | Bx103 (K-1) |
| --- | --- | --- | --- | --- | --- | --- |
| 240 | 13.7 | 0.582 |  | 294 | 16.3 | 3.565 |
| 242 | 16.6 | 0.466 |  | 296 | 13.4 | 3.978 |
| 244 | 20.1 | 0.344 |  | 298 | 10.9 | 4.405 |
| 246 | 24.0 | 0.219 |  | 300 | 8.9 | 4.876 |
| 248 | 28.5 | 0.093 |  | 302 | 7.2 | 5.361 |
| 250 | 33.4 | -0.042 |  | 304 | 5.8 | 5.806 |
| 252 | 38.8 | -0.176 |  | 306 | 4.6 | 6.201 |
| 254 | 44.2 | -0.304 |  | 308 | 3.7 | 6.542 |
| 256 | 49.6 | -0.425 |  | 310 | 2.9 | 6.824 |
| 258 | 54.7 | -0.530 |  | 312 | 2.3 | 7.045 |
| 260 | 59.5 | -0.613 |  | 314 | 1.8 | 7.220 |
| 262 | 63.1 | -0.670 |  | 316 | 1.5 | 7.355 |
| 264 | 65.9 | -0.701 |  | 318 | 1.2 | 7.459 |
| 266 | 67.5 | -0.696 |  | 320 | 0.93 | 7.531 |
| 268 | 67.6 | -0.650 |  | 322 | 0.73 | 7.584 |
| 270 | 66.5 | -0.568 |  | 324 | 0.56 | 7.670 |
| 272 | 64.4 | -0.444 |  | 326 | 0.44 | 7.742 |
| 274 | 61.0 | -0.271 |  | 328 | 0.34 | 7.777 |
| 276 | 56.9 | -0.056 |  | 330 | 0.27 | 7.906 |
| 278 | 52.3 | 0.206 |  | 332 | 0.21 | 8.046 |
| 280 | 47.0 | 0.520 |  | 334 | 0.16 | 8.105 |
| 282 | 41.9 | 0.878 |  | 336 | 0.13 | 8.276 |
| 284 | 36.8 | 1.280 |  | 338 | 0.10 | 8.484 |
| 286 | 32.5 | 1.729 |  | 340 | 0.08 | 8.522 |
| 288 | 27.9 | 2.215 |  | 342 | 0.06 | 8.533 |
| 290 | 23.6 | 2.715 |  | 344 | 0.05 | 8.384 |
| 292 | 19.9 | 3.169 |  |  |  |  |

(,T) = (298) exp [B() (T-298)]; T in K

300 K > T > 210 K

### SO2 + h Products

The UV absorption spectrum of SO2 is highly structured, with a very weak absorption in the 340-390 nm region, a weak absorption in the 260-340 nm region, and a strong absorption extending from 180 to 235 nm; the threshold wavelength for photodissociation is ~220 nm.  The atmospheric photochemistry of SO2 has been reviewed by Heicklen et al. [120] and by Calvert and Stockwell [48].  Direct photo-oxidation at wavelengths longer than ~300 nm by way of the electronically excited states of SO2 appears to be relatively unimportant.

The absorption cross sections have been measured by McGee and Burris [188] at 295 and 210 K, between 300 and 324 nm, which is the wavelength region commonly used for atmospheric monitoring of SO2.  Manatt and Lane [171] have recently compiled and evaluated the earlier cross section measurements between 106 and 403 nm.

### CS2 + h CS + S

The CS2 absorption spectrum is rather complex.  Its photochemistry has been reviewed by Okabe [234].  There are two distinct regions in the near UV spectrum:  a strong absorption extending from 185 to 230 nm, and a weaker one in the 290-380 nm range.  The threshold wavelength for photodissociation is ~280 nm.  Absorption cross section measurements have been reported recently by Xu and Joens [331] between 187 and 230 nm.

The photo-oxidation of CS2 in the atmosphere has been discussed by Wine et al. [327], who report that electronically excited CS2 may react with O2 to yield eventually OCS.

### OCS + h CO + S

The absorption cross sections of OCS have been measured by Breckenridge and Taube [29], who presented their 298 K results in graphical form, between 200 and 260 nm; by Rudolph and Inn [264] between 200 and ~300 nm (see also Turco et al. [306]), at 297 and 195 K; by Leroy et al. [157] at 294 K, between 210 and 260 nm, using photographic plates; and by Molina et al. [199] between 195 and 260 nm, in the 195 K to 403 K temperature range.  The results are in good agreement in the regions of overlap, except for  > 280 nm, where the cross section values reported by Rudolph and Inn [264] are significantly larger than those reported by Molina et al. [199].  The latter authors concluded that solar photodissociation of OCS in the troposphere occurs only to a negligible extent.

The recommended cross sections, given in Table 61, are taken from Molina et al. [199].  (The original publication also lists a table with cross section values averaged over 1 nm intervals, between 185 and 300 nm.)

Rudolph and Inn [264] reported a quantum yield for photodissociation of 0.72, based on measurements of the quantum yield for CO production in the 220-254 nm range.  Additional measurements would be useful.

###### Table 61.  Absorption Cross Sections of OCS

|  | 1020(cm2) |  | 1020(cm2) |  |  |
| --- | --- | --- | --- | --- | --- |
| (nm) | 295 K | 225 K | (nm) | 295 K | 225 K |

186.1	18.9	13.0	228.6	26.8	23.7

187.8	8.33	5.63	231.2	22.1	18.8

189.6	3.75	2.50	233.9	17.1	14.0

191.4	2.21	1.61	236.7	12.5	9.72

193.2	1.79	1.53	239.5	8.54	6.24

195.1	1.94	1.84	242.5	5.61	3.89

197.0	2.48	2.44	245.4	3.51	2.29

199.0	3.30	3.30	248.5	2.11	1.29

201.0	4.48	4.50	251.6	1.21	0.679

203.1	6.12	6.17	254.6	0.674	0.353

205.1	8.19	8.27	258.1	0.361	0.178

207.3	10.8	10.9	261.4	0.193	0.0900

209.4	14.1	14.2	264.9	0.0941	0.0419

211.6	17.6	17.6	268.5	0.0486	0.0199

213.9	21.8	21.8	272.1	0.0248	0.0101

216.2	25.5	25.3	275.9	0.0119	0.0048

218.6	28.2	27.7	279.7	0.0584	0.0021

221.5	30.5	29.4	283.7	0.0264	0.0009

223.5	31.9	29.5	287.8	0.0012	0.0005

226.0	30.2	27.4	292.0	0.0005	0.0002

296.3	0.0002	-

### SF6 + h  Products

The species SF6 does not absorb at wavelengths longer than 130 nm; it is expected to have an atmospheric residence time of thousands of years (Ravishankara et al. [250]; Ko et al. [152]).

### NaOH + h Na + OH

The spectrum of NaOH vapor is poorly characterized.  Rowland and Makide [261] inferred the absorption cross section values and the average solar photodissociation rate from the flame measurements of Daidoji [78].  Additional measurements are required.

### NaCl + h Na + Cl

There are several studies of the UV absorption spectra of NaCl vapor.  For a review of the earlier work, which was carried out at high temperatures, see Rowland and Rogers [262].  The recommended cross sections, listed in Table 62, are taken from the work of Silver et al. [281], who measured spectra of gas phase NaCl at room temperature in the range from ~190 to 360 nm by directly monitoring the product Na atoms.

###### Table 62.  Absorption Cross Sections of NaCl Vapor at 300 K

| (nm) | 1020(cm2) |
| --- | --- |

189.7	612

193.4	556

203.1	148

205.3	90.6

205.9	89.6

210.3	73.6

216.3	151

218.7	46.3

225.2	146

230.4	512

231.2	947

234.0	1300

237.6	638

241.4	674

248.4	129

251.6	251

254.8	424

260.2	433

268.3	174

277.0	40

291.8	0.8

### References for Photochemistry Section

1.	The Stratosphere 1981:  Theory and Measurements,  World Meteorological Organization Global Ozone Research and Monitoring Project, Report No. 11; see NASA-TM-84125, 1982, National Aeronautics and Space Administration.

2.	Adler-Golden, S.M. and J.R. Wiesenfeld, 1981, Chem. Phys. Lett., 82, 281.

3.	Allen, M. and J.E. Frederick, 1982, J. Atmos. Sci., 39, 2066-2075.

4.	Amimoto, S.T., A.P. Force, J.R. Wiesenfeld, and R.H. Young, 1980, J. Chem. Phys., 73, 1244-1247.

5.	Amoruso, A., M. Cacciani, A. DiSarra, and G. Fiocco, 1990, J. Geophys. Res., 95, 20565.

6.	Amoruso, A., L. Crescentini, G. Fiocco, and M. Volpe, 1993, J. Geophys. Res., 98, 16857-16863.

7.	Amoruso, A., L. Crescentini, M. Silvia Cola, and G. Fiocco, 1996, J. Quant. Spectrosc. Radiat. Transfer, 56, 145-152.

8.	Anderson, G.P. and L.A. Hall, 1983, J. Geophys. Res., 88, 6801-6806.

9.	Anderson, G.P. and L.A. Hall, 1986, J. Geophys. Res., 91, 14509-14514.

10.	Arnold, I., F.J. Comes, and G.K. Moortgat, 1977, Chem. Phys., 24, 211-217.

11.	Baer, S., H. Hippler, R. Rahn, M. Siefke, N. Seitzinger, and J. Troe, 1991, J. Chem. Phys., 95, 6463-6470.

12.	Ball, S.M., G. Hancock, I.J. Murphy, and S.P. Rayner, 1993, Geophys. Res. Lett., 20, 2063-2066.

13.	Ball, S.M., G. Hancock, and F. Winterbottom, 1995, Faraday Discuss., 100, 215.

14.	Ballash, N.M. and D.A. Armstrong, 1974, Spectrochim Acta, 30A, 941-944.

15.	Barker, J.R., L. Brouwer, R. Patrick, M.J. Rossi, P.L. Trevor, and D.M. Golden, 1985, Int. J. Chem. Kinet., 17, 991-1006.

16.	Barnes, R.J., M. Lock, J. Coleman, and A. Sinha, 1996, J. Phys. Chem., 100, 453-457.

17.	Bass, A.M., L.C. Glasgow, C. Miller, J.P. Jesson, and S.L. Filken, 1980, Planet. Space Sci., 28, 675.

18.	Bass, A.M., A.E. Ledford, and A.H. Laufer, 1976, J. Res. NBS, 80A, 143-166.

19.	Bauer, D., J.N. Crowley, and G.K. Moortgat, 1992, J. Photochem. and Photobiol., A65, 3530-3538.

20.	Benter, T., C. Feldmann, U. Kirchner, M. Schmidt, S. Schmidt, and R.N. Schindler, 1995, Ber. Bunsenges. Phys. Chem., 99, 1144-1147.

21.	Biaume, F., 1973, J. Photochem., 2, 139.

22.	Birk, M., R.R. Friedl, E.A. Cohen, H.M. Pickett, and S.P. Sander, 1989, J. Chem. Phys., 91, 6588-6597.

23.	Birks, J.W., B. Shoemaker, T.J. Leck, R.A. Borders, and L.J. Hart, 1977, J. Chem. Phys., 66, 4591.

24.	Bishenden, E., J. Haddock, and D.J. Donaldson, 1991, J. Phys. Chem., 95, 2113.

25.	Bishenden, E., J. Haddock, and D.J. Donaldson, 1992, J. Phys. Chem., 96, 6513.

26.	Bongartz, A., J. Kames, F. Welter, and U. Schurath, 1991, J. Phys. Chem., 95, 1076-1082.

27.	Brandon, J.T., S.A. Reid, D.C. Robie, and H. Reisler, 1992, J. Chem. Phys., 97, 5246.

28.	Braun, M., A. Fahr, R. Klein, M.J. Kurylo, and R.E. Huie, 1991, J. Geophys. Res., 96, 13009.

29.	Breckenridge, W. and H.H. Taube, 1970, J. Chem. Phys., 52, 1713-1715.

30.	Brion, J., A. Chakir, D. Daumont, J. Malicet, and C. Parisse, 1993, Chem. Phys. Lett., 213, 610-612.

31.	Brock, J.C. and R.T. Watson, 1980, Chem. Phys., 46, 477-484.

32.	Brock, J.C. and R.T. Watson, 1980, Chem. Phys. Lett., 71, 371-375.

33.	Burkholder, J.B., 1993, J. Geophys. Res., 98, 2963-2974.

34.	Burkholder, J.B. and E.J. Bair, 1983, J. Phys. Chem., 87, 1859-1863.

35.	Burkholder, J.B., R.L. Mauldin, R.J. Yokelson, S. Solomon, and A.R. Ravishankara, 1993, J. Phys. Chem., 97, 7597-7605.

36.	Burkholder, J.B., J.J. Orlando, and C.J. Howard, 1990, J. Phys. Chem., 94, 687-695.

37.	Burkholder, J.B., A.R. Ravishankara, and S. Solomon, 1995, J. Geophys. Res., 100, 16793-16800.

38.	Burkholder, J.B., R.K. Talukdar, and A.R. Ravishankara, 1994, Geophys. Res. Lett., 21, 585-588.

39.	Burkholder, J.B., R.K. Talukdar, A.R. Ravishankara, and S. Solomon, 1993, J. Geophys. Res., 98, 22937-22948.

40.	Burkholder, J.B., R.R. Wilson, T. Gierczak, R. Talukdar, S.A. McKeen, J.J. Orlando, G.L. Vaghjiani, and A.R. Ravishankara, 1991, J. Geophys. Res., 96, 5025-5043.

41.	Burley, J.D., C.E. Miller, and H.S. Johnston, 1993, J. Molec. Spec, 158, 377-391.

42.	Burrows, J.P., G.S. Tyndall, and G.K. Moortgat,  paper presented at the 16th Informal Conf. on Photochemistry, 1984,  Boston.

43.	Burrows, J.P., G.S. Tyndall, and G.K. Moortgat, 1985, J. Phys. Chem., 89, 4848-4856.

44.	Burrows, J.P., G.S. Tyndall, and G.K. Moortgat, 1988, J. Phys. Chem., 92, 4340-4348.

45.	Butler, P.J.D. and L.F. Phillips, 1983, J. Phys. Chem., 87, 183-184.

46.	Cacciani, M., A.D. Sarra, G. Fiocco, and A. Amoruso, 1989, J. Geophys. Res., 94, 8485-8490.

47.	Calvert, J.G. and J.N. Pitts,  Photochemistry, 1966, New York: John Wiley & Sons, Inc., pp. 230-231.

48.	Calvert, J.G. and W.R. Stockwell, 1983, Acid Precipitation: SO2, NO, NO2 Oxidation Mechanisms: Atmospheric  Considerations,  Ann Arbor Sci. Publishers,  Ann Arbor, Michigan.

49.	Canosa-Mas, C.E., M. Fowles, P.J. Houghton, and R.P. Wayne, 1987, J. Chem. Soc. Faraday Trans. 2, 83, 1465.

50.	Cantrell, C.A., J.A. Davidson, A.H. McDaniel, R.E. Shetter, and J.G. Calvert, 1990, J. Phys. Chem., 94, 3902-3908.

51.	Cantrell, C.A., J.A. Davidson, R.E. Shetter, B.A. Anderson, and J.G. Calvert, 1987, J. Phys. Chem., 91, 5858-5863.

52.	Chang, J.S., J.R. Barker, J.E. Davenport, and D.M. Golden, 1979, Chem. Phys. Lett., 60, 385-390.

53.	Cheung, A.S.C., K. Yoshino, J.R. Esmond, S.S.L. Chiu, D.E. Freeman, and W.H. Parkinson, 1990, J. Chem. Phys., 92, 842-849.

54.	Cheung, A.S.C., K. Yoshino, W.H. Parkinson, and D.E. Freeman, 1984, Geophys. Res. Lett., 11, 580-582.

55.	Cheung, A.S.C., K. Yoshino, W.H. Parkinson, S.L. Guberman, and D.E. Freeman, 1986, Planet. Space Sci., 34, 1007-1021.

56.	Chiu, S.S.L., A.S.C. Cheung, K. Yoshino, J.R. Esmond, D.E. Freeman, and W.H. Parkinson, 1990, J. Chem. Phys., 93, 5539-5543.

57.	Chou, C.C., G. Crescentini, H. Vera-Ruiz, W.S. Smith, and F.S. Rowland,  paper presented at the 173rd American Chemical Society Meeting, 1977,  New Orleans, LA.

58.	Chou, C.C., R.J. Milstein, W.S. Smith, H. Vera-Ruiz, M.J. Molina, and F.S. Rowland, 1978, J. Phys. Chem., 82, 1.

59.	Chou, C.C., H. Vera-Ruiz, K. Moe, and F.S. Rowland, 1976, unpublished results.

60.	Clark, J.H., C.B. Moore, and N.S. Nogar, 1978, J. Chem. Phys., 68, 1264-1271.

61.	CODATA, 1980, J. Phys. Chem. Ref. Data, 9, 295-471.

62.	CODATA, 1982, J. Phys. Chem. Ref. Data, 11, 327-496.

63.	Colussi, A.J., 1990, J. Phys. Chem., 94, 8922-8926.

64.	Colussi, A.J., S.P. Sander, and R.R. Friedl, 1992, J. Phys.Chem., 96, 4442-4445.

65.	Cooper, I.A., P.J. Neill, and J.R. Wiesenfeld, 1993, J. Geophys. Res., 98, 12795-12800.

66.	Coquart, B., A. Jenouvier, and M.F. Merienne, 1995, J. Atm. Chem, 21, 251-261.

67.	Coquart, B., M.F. Merienne, and A. Jenouvrier, 1990, Planet. Space Sci., 38, 287.

68.	Corcoran, T.C., E.J. Beiting, and M.O. Mitchell, 1992, J. Molecular Spectroscopy, 154, 119-128.

69.	Cox, R.A., R.A. Barton, E. Ljungstrum, and D.W. Stocker, 1984, Chem. Phys. Lett., 108, 228-232.

70.	Cox, R.A. and J.P. Burrows, 1979, J. Phys. Chem., 83, 2560-2568.

71.	Cox, R.A. and G.D. Hayman, 1988, Nature, 332, 796-800.

72.	Cox, R.A. and R. Patrick, 1979, Int. J. Chem. Kinet., 11, 635.

73.	Cox, R.A., D.W. Sheppard, and M.P. Stevens, 1982, J. Photochem., 19, 189-207.

74.	Coxon, J.A., W.E. Jones, and D.A. Ramsey,  paper presented at the 12th International Symposium on Free Radicals, 1976,  Laguna Beach, California.

75.	Crowley, J.N., R. Helleis, R. Muller, G.K. Moortgat, P.J. Crutzen, and J.J. Orlando, 1994, J. Geophys. Res., 99, 20683-20688.

76.	Crowley, J.N., F.G. Simon, J.P. Burrows, G.K. Moortgat, M.E. Jenkin, and R.A. Cox, 1991, J. Photochem. and Photobiol. A: Chem., 60, 1-10.

77.	Dagaut, P. and M.J. Kurylo, 1990, J. Photochem. and Photobiol. A:Chem., 51, 133.

78.	Daidoji, H., 1979, Bunseki Kagaku, 28, 77.

79.	Daumont, D., J. Brion, J. Charbonnier, and J. Malicet, 1992, J. Atmos. Chem., 15, 145-155.

80.	Davenport, J.E., 1978, Report No. FAA-EQ-78-14, Federal Aviation Administration, Washington, DC.

81.	Davidson, J.A., C.A. Cantrell, A.H. McDaniel, R.E. Shetter, S. Madronich, and J.G. Calvert, 1988, J. Geophys. Res., 93, 7105-7112.

82.	Davis, H.F. and Y.T. Lee, 1992, J. Phys. Chem., 96, 5681-5684.

83.	DeMore, W.B. and E. Tschuikow-Roux, 1990, J. Phys. Chem., 94, 5856-5860.

84.	Deters, B., J.P. Burrows, S. Himmelmann, and C. Blindauer, 1996, Ann. Geophysicae, 14, 468-475.

85.	Eberstein, I.J., 1990, Geophys. Res. Lett., 17, 721-724.

86.	Fahr, A., W. Braun, and M.J. Kurylo, 1993, J. Geophys. Res., 98, 20467-20472.

87.	Fahr, A., A.K. Nayak, and R. Huie, 1995, Chem. Phys., 199, 275-284.

88.	Fairchild, C.E., E.J. Stone, and G.M. Lawrence, 1978, J. Chem. Phys., 69, 3632-3638.

89.	Fenter, F.F., V. Catoire, R. Lesclaux, and P.D. Lightfoot, 1993, J. Phys. Chem., 97, 3530-3538.

90.	Fergusson, W.C., L. Slotin, and W.G. Style, 1936, Trans. Far. Soc., 32, 956.

91.	Francisco, J.S., M.R. Hand, and I.H. Williams, 1996, J. Phys. Chem., 100, 9250-9253.

92.	Frederick, J.E. and R.D. Hudson, 1979, J. Atmos. Sci., 36, 737-745.

93.	Frederick, J.E. and J.E. Mentall, 1982, Geophys. Res. Lett., 9, 461-464.

94.	Frost, G.J., L.M. Goss, and V. Vaida, 1996, J. Geophys. Res, 101, 3869-3877.

95.	Frost, G.J., L.M. Goss, and V. Vaida, 1996, J. Geophys. Res., 101, 3879-3884.

96.	Ganske, J.A., H.N. Berko, and B.J. Finlayson-Pitts, 1992, J. Geophys. Res., 97, 7651-7656.

97.	Gardner, E.P., P.D. Sperry, and J.G. Calvert, 1987, J. Geophys. Res., 92, 6642-6652.

98.	Gibson, G.E. and N.S. Bayliss, 1933, Phys. Rev., 44, 188.

99.	Gillotay, D., A. Jenouvrier, B. Coquart, M.F. Merienne, and P.C. Simon, 1989, Planet. Space Sci., 37, 1127-1140.

100.	Gillotay, D. and P.C. Simon, 1988, Annales Geophysicae, 6, 211-215.

101.	Gillotay, D. and P.C. Simon, 1989, J. Atmos. Chem., 8, 41-62.

102.	Gillotay, D. and P.C. Simon, 1991, J. Atmos. Chem., 13, 289-299.

103.	Gillotay, D. and P.C. Simon, 1991, J. Atmos. Chem., 12, 269-285.

104.	Gillotay, D., P.C. Simon, and L. Dierickx, 1988, Aeronomica Acta, A335, 1-25.

105.	Gillotay, D., P.C. Simon, and L. Dierickx, 1993, Aeronomica Acta, A368, 1-15.

106.	Giolando, D.M., G.B. Fazekas, W.D. Taylor, and G.A. Takacs, 1980, J. Photochem., 14, 335.

107.	Goodeve, C.F. and F.D. Richardson, 1937, Trans. Faraday. Soc., 33, 453-457.

108.	Graham, R.A., 1975, Ph. D. Thesis, "Photochemistry of NO3 and the Kinetics of the N2O5-O3 System", University of California, Berkeley, CA.

109.	Graham, R.A. and H.S. Johnston, 1978, J. Phys. Chem., 82, 254-268.

110.	Graham, R.A., A.M. Winer, and J.N. Pitts Jr., 1978, Geophys. Res. Lett., 5, 909.

111.	Green, R.G. and R.P. Wayne, 1976/77, J. Photochem., 6, 375-377.

112.	Greenblatt, G.D. and A.R. Ravishankara, 1990, J. Geophys. Res., 95, 3539-3547.

113.	Harder, J.W., J.W. Brault, P.V. Johnston, and G.H. Mount, 1996, J. Geophys. Res., submitted.

114.	Harker, A.B., W. Ho, and J.J. Ratto, 1977, Chem. Phys. Lett., 50, 394-397.

115.	Harwood, M.H. and R.L. Jones, 1994, J. Geophys. Res., 99, 22995-22964.

116.	Harwood, M.H., R.L. Jones, R.A. Cox, E. Lutman, and O.V. Rattigan, 1993, J. Photochem. Photobiol. A: Chem., 73, 167-175.

117.	Harwood, M.H., D.M. Rowley, R.A. Freshwater, R.A. Cox, and R.L. Jones, 1995, J. Chem. Soc. Faraday Trans, 91, 3027-3032.

118.	Hayman, G.D. and R.A. Cox, 1989, Chem. Phys. Lett., 155, 1-7.

119.	Hearn, A.G., 1961, Proc. Phys. Soc. London, 78, 932-940.

120.	Heicklen, J., N. Kelly, and K. Partymiller, 1980, Rev. Chem. Intermediates, 3, 315-404.

121.	Herman, J.R. and J.E. Mentall, 1982, J. Geophys. Res., 87, 8967-8975.

122.	Herzberg, G. and K.K. Innes, 1957, Canad. J. Phys., 35, 842.

123.	Hochanadel, C.J., J.A. Ghormley, and P.J. Ogren, 1972, J. Chem. Phys., 56, 4426-4432.

124.	Horowitz, A. and J.G. Calvert, 1978, Int. J. Chem. Kinet., 10, 805.

125.	Hubinger, S. and J.B. Nee, 1994, Chem. Phys., 181, 247-257.

126.	Hubinger, S. and J.B. Nee, 1995, J. Photochem. and Photobiol. A: Chem., 85, 1-7.

127.	Hubrich, C. and F. Stuhl, 1980, J. Photochem., 12, 93-107.

128.	Hubrich, C., C. Zetzsch, and F. Stuhl, 1977, Ber. Bunsenges. Phys. Chem., 81, 437-442.

129.	Huder, K.J. and W.B. DeMore, 1995, J. Phys. Chem., 99, 3905-3908.

130.	Hudson, R.D., 1971, Reviews of Geophysics and Space Physics, 9, 305-399.

131.	Hudson, R.D., 1974, Canad. J. Chem., 52, 1465-1478.

132.	Hudson, R.D. and L.J. Kieffer, 1975, "Absorption Cross Sections of Stratospheric Molecules," The Natural Stratosphere of 1974, Monograph 1,  CIAP, pp. (5-156)-(5-194).

133.	Illies, A.J. and G.A. Takacs, 1976, J. Photochem., 6, 35-42.

134.	Inn, E.C.Y., 1975, J. Atmos. Sci., 32, 2375.

135.	Inn, E.C.Y., 1980, J. Geophys. Res., 85, 7493.

136.	Inn, E.C.Y. and Y. Tanaka, 1953, J. Opt. Soc. Am., 43, 870-873.

137.	Jenouvrier, A., B. Coquart, and M.F. Merienne, 1986, J. Quant. Spectros. Radiat. Transfer, 36, 349-354.

138.	Jensen, F. and J. Oddershede, 1990, J. Phys. Chem., 94, 2235.

139.	Johnston, H.S., S. Chang, and G. Whitten, 1974, J. Phys. Chem., 78, 1-7.

140.	Johnston, H.S., H.F. Davis, and Y.T. Lee, 1996, J. Phys. Chem., 100, 4713-4723.

141.	Johnston, H.S. and R. Graham, 1973, J. Chem. Phys., 77, 62.

142.	Johnston, H.S. and R. Graham, 1974, Canad. J. Chem., 52, 1415-1423.

143.	Johnston, H.S., E.D. Morris Jr., and J. Van den Bogaerde, 1969, J. Am. Chem. Soc., 91, 7712.

144.	Johnston, H.S., M. Paige, and F. Yao, 1984, J. Geophys. Res., 89, 661.

145.	Jolly, G.S., D.L. Singleton, D.J. McKenney, and G. Paraskevopoulos, 1986, J. Chem. Phys., 84, 6662-6667.

146.	Jones, E.L. and O.R. Wulf, 1937, J. Chem. Phys., 5, 873.

147.	Jones, I.T.N. and K. Bayes, 1973, J. Chem. Phys., 59, 4836-4844.

148.	Jourdain, J.L., G. Le Bras, G. Poulet, J. Combourieu, P. Rigaud, and B. LeRoy, 1978, Chem. Phys. Lett., 57, 109.

149.	Jungkamp, T.P.W., U. Kirchner, M. Schmidt, and R.N. Schindler, 1995, J. Photochem. Photobiol. A: Chemistry, 99, 1-999.

150.	Knauth, H.D., H. Alberti, and H. Clausen, 1979, J. Phys. Chem., 83, 1604-1612.

151.	Knauth, H.D. and R.N. Schindler, 1983, Z. Naturforsch., 38a, 893.

152.	Ko, M.K.W., D.S. Nien, W.C. Wang, G. Shia, A. Goldman, F.J. Murcray, D.G. Murcray, and C.P. Rinsland, 1993, J. Geophys. Res., 98, 10499-10507.

153.	Kurylo, M.J., T.J. Wallington, and P.A. Ouellette, 1987, J. Photochem., 39, 201-215.

154.	Langhoff, S.R., L. Jaffe, and J.O. Arnold, 1977, J. Quant. Spectrosc. Radiat. Transfer, 18, 227.

155.	Lawrence, W.G., K.C. Clemitshaw, and V.A. Apkarian, 1990, J. Geophys. Res., 95, 18591.

156.	Lee, L.C., 1982, J. Chem. Phys., 76, 4909-4915.

157.	Leroy, B., G. Le Bras, and P. Rigaud, 1981, Ann. Geophys., 37, 297-302.

158.	Lewis, B.R., L. Berzins, and J.H. Carver, 1986, J. Quant. Spectrosc. Radiat. Transfer, 36, 209-232.

159.	Lewis, B.R., L. Berzins, J.H. Carver, and S.T. Gibson, 1986, J. Quant. Spectrosc. Radiat. Transfer, 36, 187-207.

160.	Libuda, H.G. and F. Zabel, 1995, Ber. Bunsenges. Phys. Chem., 99, 1205-1213.

161.	Lightfoot, P.D., R.A. Cox, J.N. Crowley, M. Destriau, G.D. Hayman, M.E. Jenkin, G.K. Moortgat, and F. Zabel, 1992, Atmos. Environ., 26A, 1805-1961.

162.	Lightfoot, P.D. and A.A. Jemi-Alade, 1991, J.Photochem. and Photobiol. A: Chem., 59, 1-10.

163.	Lin, C.L., 1976, J. Chem. Eng. Data, 21, 411.

164.	Lin, C.L., N.K. Rohatgi, and W.B. DeMore, 1978, Geophys. Res. Lett., 5, 113-115.

165.	Lopez, M.I. and J.E. Sicre, 1988, J. Phys. Chem., 92, 563-564.

166.	Lopez, M.I. and J.E. Sicre, 1990, J. Phys. Chem., 94, 3860-3863.

167.	MacLeod, H., G.P. Smith, and D.M. Golden, 1988, J. Geophys. Res., 93, 3813-3823.

168.	Magnotta, F. and H.S. Johnston, 1980, Geophys. Res. Lett., 7, 769-772.

169.	Majer, J.R. and J.P. Simons, 1964, "Photochemical Processes in Halogenated Compounds," Advances in Photochemistry, 2,  Interscience, pp. 137-181.

170.	Malicet, J., D. Daumont, J. Charbonnier, C. Parisse, A. Chakir, and J. Brion, 1995, J. Atm. Chem, 21, 263-273.

171.	Manatt, S.L. and A.L. Lane, 1993, J. Quant. Spectrosc. Radiat. Transfer, 50, 267-276.

172.	Mandelman, M. and R.W. Nicholls, 1977, J. Quant. Spectrosc. Radiat. Trans., 17, 483.

173.	Margitan, J.J., 1983, J. Phys. Chem., 87, 674-679.

174.	Margitan, J.J. and R.T. Watson, 1982, J. Phys. Chem., 86, 3819-3824.

175.	Maric, D., J.P. Burrows, R. Meller, and G.K. Moortgat, 1993, J. Photochem. Photobiol. A Chem., 70, 205-214.

176.	Maric, D., J.P. Burrows, and G.K. Moortgat, 1994, J. Photochem. Photobiol A: Chem., 83, 179-192.

177.	Maricq, M.M. and T.J. Wallington, 1992, J. Phys. Chem., 96, 982-986.

178.	Marinelli, W.J. and H.S. Johnston, 1982, Chem. Phys. Lett., 93, 127-132.

179.	Marinelli, W.J., D.M. Swanson, and H.S. Johnston, 1982, J. Chem. Phys., 76, 2864-2870.

180.	Martin, H. and R. Gareis, 1956, Z. Elektrochemie, 60, 959-964.

181.	Mauersberger, K., J. Barnes, D. Hanson, and J. Morton, 1986, Geophys. Res. Lett., 13, 671-673.

182.	Mauersberger, K., D. Hanson, J. Barnes, and J. Morton, 1987, J. Geophys. Res., 92, 8480-8482.

183.	Mauldin, R.L., III, J.B. Burkholder, and A.R. Ravishankara, 1992, J. Phys. Chem., 96, 2582-2588.

184.	Mazely, T.L., R.R. Friedl, and S.P. Sander, 1995, J. Phys. Chem., 99, 8162-8169.

185.	Mazely, T.L., S.P. Sander, and R.R. Friedl, 1997, Manuscript in preparation.

186.	McAdam, K., B. Veyret, and R. Lesclaux, 1987, Chem. Phys. Lett., 133, 39-44.

187.	McElcheran, D.E., M.H.J. Wijnen, and E.W.R. Steacie, 1958, Can. J. Chem., 36, 321.

188.	McGee, T.J. and J. Burris, 1987, J. Quant. Spectrosc. Radiat. Trans., 37, 165-182.

189.	McGrath, M.P., K.C. Clemitshaw, F.S. Rowland, and W.J. Hehre, 1988, Geophys. Res. Lett., 15, 883-886.

190.	McGrath, M.P., K.C. Clemitshaw, F.S. Rowland, and W.J. Hehre, 1990, J. Phys. Chem., 94, 6126.

191.	Merienne, M.F., B. Coquart, and A. Jenouvrier, 1990, Planet. Space Sci., 38, 617-625.

192.	Merienne, M.F., A. Jenouvrier, and B. Coquart, 1995, J. Atm. Chem, 20, 281-297.

193.	Michelsen, H.A., R.J. Salawitch, P.O. Wennberg, and J.G. Anderson, 1994, Geophys. Res. Lett., 21, 2227-2230.

194.	Minschwaner, K., G.P. Anderson, L.A. Hall, and K. Yoshino, 1992, J. Geophys. Res., 97, 10103-10108.

195.	Minschwaner, K. and D.E. Siskind, 1993, J. Geophys. Res., 98, 20401-20412.

196.	Minton, T.K., C.M. Nelson, T.A. Moore, and M. Okumura, 1992, Science, 258, 1342-1345.

197.	Mishalanie, E.A., J.C. Rutkowski, R.S. Hutte, and J.W. Birks, 1986, J. Phys. Chem., 90, 5578-5584.

198.	Mitchell, D.N., R.P. Wayne, P.J. Allen, R.P. Harrison, and R.J. Twin, 1980, J. Chem. Soc. Faraday Trans. 2, 76, 785.

199.	Molina, L.T., J.J. Lamb, and M.J. Molina, 1981, Geophys. Res. Lett., 8, 1008.

200.	Molina, L.T. and M.J. Molina, 1977, Geophys. Res. Lett., 4, 83-86.

201.	Molina, L.T. and M.J. Molina, 1978, J. Phys. Chem., 82, 2410-2414.

202.	Molina, L.T. and M.J. Molina, 1979, J. Photochem., 11, 139-144.

203.	Molina, L.T. and M.J. Molina, 1981, J. Photochem., 15, 97.

204.	Molina, L.T. and M.J. Molina,  paper presented at the 182nd American Chemical Society National Meeting, 1982,  New York.

205.	Molina, L.T. and M.J. Molina, 1983, J. Phys. Chem., 87, 1306.

206.	Molina, L.T. and M.J. Molina, 1986, J. Geophys. Res., 91, 14,501-14,508.

207.	Molina, L.T. and M.J. Molina, 1996, Geophys. Res. Lett., 23, 563-565.

208.	Molina, L.T., M.J. Molina, and F.S. Rowland, 1982, J. Phys. Chem., 86, 2672-2676.

209.	Molina, L.T., S.D. Schinke, and M.J. Molina, 1977, Geophys. Res. Lett., 4, 580-582.

210.	Molina, M.J. and G. Arguello, 1979, Geophys. Res. Lett., 6, 953-955.

211.	Molina, M.J., A.J. Colussi, L.T. Molina, R.N. Schindler, and T.L. Tso, 1990, Chem. Phys. Lett., 173, 310.

212.	Molina, M.J., T. Ishiwata, and L.T. Molina, 1980, J. Phys. Chem., 84, 821-826.

213.	Moore, T.A., M. Okumura, M. Tagawa, and T.K. Minton, 1995, Faraday Discuss, 100, 295-307.

214.	Moortgat, G.K., W. Klippel, K.H. Mobius, W. Seiler, and P. Warneck, 1980, Report No.  FAA-EE-80-47,  Federal Aviation Administration, Washington, DC.

215.	Moortgat, G.K., R. Meller, and W. Schneider, 1993, "Temperature dependence (256-296K) of the absorption cross-sections of bromoform in the wavelength range 285-360 nm," The Tropospheric Chemistry of Ozone in the Polar Regions, H. Niki and K.H. Becker, Editors,  Springer-Verlag,  Berlin, pp. 359-369.

216.	Moortgat, G.K., W. Seiler, and P. Warneck, 1983, J. Chem. Phys., 78, 1185-1190.

217.	Moortgat, G.K., B. Veyret, and R. Lesclaux, 1989, J. Phys. Chem., 93, 2362-2368.

218.	Moortgat, G.K. and P. Warneck, 1979, J. Chem. Phys., 70, 3639-3651.

219.	Morel, O., R. Simonaitis, and J. Heicklen, 1980, Chem. Phys. Lett., 73, 38.

220.	Murtagh, D.P., 1988, Planet. Space Sci., 36, 819-828.

221.	Nayak, A.K., T.J. Buckley, M.J. Kurylo, and A. Fahr, 1996, J. Geophys. Res., 101, 9055-9062.

222.	Nayak, A.K., M.J. Kurylo, and A. Fahr, 1995, J. Geophys. Res, 100, 11185-11189.

223.	Nee, J.B., 1991, J. Quant. Spectrosc. Radiat. Transfer, 46, 55.

224.	Nelson, C.M., T.A. Moore, and M. Okumura, 1994, J. Chem. Phys., 100, 8055-8064.

225.	Nelson, C.M., T.A. Moore, M. Okumura, and T.K. Minton, 1996, Chem. Phys, 2248, 287-307.

226.	Nelson, H.H. and H.S. Johnston, 1981, J. Phys. Chem., 85, 3891.

227.	Nickolaisen, S.L. and S.P. Sander, 1996, Manuscript in preparation.

228.	Nickolaisen, S.L., S.P. Sander, and R.R. Friedl, 1996, J. Phys. Chem., 100, 10165.

229.	Nicolet, M. and R. Kennes, 1989, Planet. Space Sci., 37, 459-491.

230.	Nicovich, J.M. and P.H. Wine, 1988, J. Geophys. Res., 93, 2417.

231.	Nolle, A., H. Heydtmann, R. Meller, and G.K. Moortgat, 1993, Geophys. Res. Lett., 20, 707-710.

232.	Nölle, A., H. Heydtmann, R. Meller, W. Schneider, and G.K. Moortgat, 1992, Geophys. Res. Lett., 19, 281-284.

233.	Oh, D., W. Sisk, A. Young, and H. Johnston, 1986, J. Chem. Phys., 85, 7146-7158.

234.	Okabe, H., 1978, Photochemistry of Small Molecules,  John Wiley and Sons Inc.,  New York, pp. 217.

235.	Okabe, H., 1980, J. Chem. Phys., 72, 6642.

236.	Orkin, V.L. and E.E. Kasimovskaya, 1995, J. Atm. Chem, 21, 1-11.

237.	Orlando, J.J. and J.B. Burkholder, 1995, J. Phys. Chem., 99, 1143-1150.

238.	Orlando, J.J., J.B. Burkholder, S.A. McKeen, and A.R. Ravishankara, 1991, J. Geophys. Res., 96, 5013-5023.

239.	Orlando, J.J., G.S. Tyndall, G.K. Moortgat, and J.G. Calvert, 1993, J. Phys. Chem., 97, 10996-11000.

240.	Paraskevopoulos, G. and R.J. Cvetanovic, 1969, J. Am. Chem. Soc., 91, 7572.

241.	Parrish, D.D., P.C. Murphy, D.L. Albritton, and F.C. Fehsenfeld, 1983, Atmos. Environ., 17, 1365.

242.	Paukert, T.T. and H.S. Johnston, 1972, J. Chem. Phys., 56, 2824-2838.

243.	Permien, T., R. Vogt, and R.N. Schindler, 1988, "Mechanisms of Gas Phase-Liquid Phase Chemical Transformations," Air Pollution Report #17, R.A. Cox, Editor,  Environmental Research Program of the CEC.,  Brussels.

244.	Preston, K.F. and R.F. Barr, 1971, J. Chem. Phys., 54, 3347-3348.

245.	Rattigan, O., E. Lutman, R.L. Jones, and R.A. Cox, 1992, J. Photochem. Photobiol. A: Chem., 66, 313-326.

246.	Rattigan, O., E. Lutman, R.L. Jones, R.A. Cox, K. Clemitshaw, and J. Williams, 1992, J. Photochem. Photobiol. A: Chem., 69, 125-126.

247.	Rattigan, O.V., D.J. Lary, R.L. Jones, and R.A. Cox, 1996, J. Geophys. Res., 101, 23021-23033.

248.	Ravishankara, A.R., 1995, Faraday Discuss, 100, 335.

249.	Ravishankara, A.R. and R.L. Mauldin, 1986, J. Geophys. Res., 91, 8709-8712.

250.	Ravishankara, A.R., S. Solomon, A.A. Turnipseed, and R.F. Warren, 1993, Science, 259, 194-199.

251.	Ravishankara, A.R. and P.H. Wine, 1983, Chem. Phys. Lett., 101, 73.

252.	Ravishankara, A.R., P.H. Wine, C.A. Smith, P.E. Barbone, and A. Torabi, 1986, J. Geophys. Res., 91, 5355-5360.

253.	Reid, S.A., J.T. Brandon, and H. Reisler, 1993, J. Phys. Chem., 97, 540.

254.	Rigaud, P., B. Leroy, G. Le Bras, G. Poulet, J.L. Jourdain, and J. Combourieu, 1977, Chem. Phys. Lett., 46, 161.

255.	Robbins, D.E., 1976, Geophys. Res. Lett., 3, 213-216. See also Erratum, GRL, 1976, Vol. 3,   p. 757.

256.	Robbins, D.E.,  paper presented at the International Conference on Problems Related to the Stratosphere, 1977,  Pasadena, California Jet Propulsion Laboratory, California Institute of Technology.

257.	Robbins, D.E. and R.S. Stolarski, 1976, Geophys. Rev. Lett., 3, 603-606.

258.	Roehl, C.M., D. Bauer, and G.K. Moortgat, 1996, J. Phys. Chem., 100, 4038-4047.

259.	Roehl, C.M., J.J. Orlando, and J.G. Calvert, 1992, J. Photochem. Photobiol. A: Chem., 69, 1-5.

260.	Rogers, J.D., 1990, J. Phys. Chem., 94, 4011-4015.

261.	Rowland, F.S. and Y. Makide, 1982, Geophys. Res. Lett., 9, 473.

262.	Rowland, F.S. and P.J. Rogers, 1982, Proc. Natl. Acad. Sci. USA, 79, 2737.

263.	Rowland, F.S., J.E. Spencer, and M.J. Molina, 1976, J. Phys. Chem., 80, 2711-2713.

264.	Rudolph, R.N. and E.C.Y. Inn, 1981, J. Geophys. Res., 86, 9891.

265.	Ruhl, E., A. Jefferson, and V. Vaida, 1990, J. Phys. Chem., 94, 2990.

266.	Safary, E., J. Romand, and B. Vodar, 1951, J. Chem. Phys., 19, 379.

267.	Sander, S.P., 1986, J. Phys. Chem., 90, 4135-4142.

268.	Sander, S.P. and R.R. Friedl, 1989, J. Phys. Chem., 93, 4764-4771.

269.	Sander, S.P., M. Peterson, R.T. Watson, and R. Patrick, 1982, J. Phys. Chem., 86, 1236-1240.

270.	Sandorfy, C., 1976, Atmos. Environ., 10, 343-351.

271.	Sauvageau, P., J. Doucet, R. Gilbert, and C. Sandorfy, 1974, J. Chem. Phys., 61, 391.

272.	Sauvageau, P., R. Gilbert, P.P. Berlow, and C. Sandorfy, 1973, J. Chem. Phys., 59, 762.

273.	Schiffman, A., D.D. Nelson Jr., and D.J. Nesbitt, 1993, J. Chem. Phys., 98, 6935-6946.

274.	Schneider, W., G.K. Moortgat, J.P. Burrows, and G.5. Tyndall, 1987, J. Photochem. Photobiol., 40, 195-217.

275.	Schneider, W.F., T.J. Wallington, K. Minschwaner, and E.A. Stahlberg, 1995, Environ. Sci. Technol., 29, 247.

276.	Seery, D.J. and D. Britton, 1964, J. Phys. Chem., 68, 2263.

277.	Selwyn, G., J. Podolske, and H.S. Johnston, 1977, Geophys. Res. Lett., 4, 427-430.

278.	Senum, G.I., Y.-N. Lee, and J.S. Gaffney, 1984, J. Phys. Chem., 88, 1269-1270.

279.	Shardanand and A.D.P. Rao, 1977, J. Quant. Spectrosc. Radiat. Transfer, 17, 433-439.

280.	Shetter, R.E., J.A. Davidson, C.A. Cantrell, N.J. Burzynski, and J.G. Calvert, 1988, J. Geophys. Res., 93, 7113-7118.

281.	Silver, J.A., D.R. Worsnop, A. Freedman, and C.E. Kolb, 1986, J. Chem. Phys., 84, 4378-4384.

282.	Simon, F.G., W. Schneider, G.K. Moortgat, and J.P. Burrows, 1990, J. Photochem. Photobiol., A55, 1-23.

283.	Simon, P.C., D. Gillotay, N. Vanlaethem-Meuree, and J. Wisemberg, 1988, J. Atmos. Chem., 7, 107-135.

284.	Simon, P.C., D. Gillotay, N. Vanlaethem-Meuree, and J. Wisemberg, 1988, Annales Geophysicae, 6, 239-248.

285.	Simonaitis, R., R.I. Greenberg, and J. Heicklen, 1972, Int. J. Chem. Kinet., 4, 497.

286.	Singer, R.J., J.N. Crowley, J.P. Burrows, W. Schneider, and G.K. Moortgat, 1989, J. Photochem. Photobiol., 48, 17-32.

287.	Smith, W.S., C.C. Chou, and F.S. Rowland, 1977, Geophys. Res. Lett., 4, 517-519.

288.	Solomon, S., J.B. Burkholder, A.R. Ravishankara, and R.R. Garcia, 1994, J. Geophys. Res., 99, 20929-20935.

289.	Sparks, R.K., L.R. Carlson, K. Shobatake, M.L. Kowalczyk, and Y.T. Lee, 1980, J. Chem. Phys., 72, 1401-1402.

290.	Spencer, J.E. and F.S. Rowland, 1978, J. Phys. Chem., 82, 7-10.

291.	Stanton, J.F. and R.J. Bartlett, 1993, J. Phys. Chem., 98, 9335-9339.

292.	Stanton, J.F., C.M.L. Rittby, R.J. Bartlett, and D.W. Toohey, 1991, J. Phys. Chem., 95, 2107-2110.

293.	Steinfeld, J.I., S.M. Adler-Golden, and J.W. Gallagher, 1987, J. Phys. Chem. Ref. Data, 16, 911-951.

294.	Stief, L.J., W.A. Payne, and R.B. Klemm, 1975, J. Chem. Phys., 62, 4000-4008.

295.	Stockwell, W.R. and J.G. Calvert, 1978, J. Photochem., 8, 193-203.

296.	Suto, M. and L.C. Lee, 1985, J. Geophys. Res., 90, 13037-13040.

297.	Swanson, D., B. Kan, and H.S. Johnston, 1984, J. Phys. Chem., 88, 3115.

298.	Takahashi, K., Y. Matsumi, and M. Kawasaki, 1996, J. Phys. Chem., 100, 4084-4089.

299.	Talukdar, R., A. Mellouki, T. Gierczak, J.B. Burkholder, S.A. McKeen, and A.R. Ravishankara, 1991, J. Phys. Chem., 95, 5815-5821.

300.	Talukdar, R.K., J.B. Burkholder, A.-M. Schmoltner, J.M. Roberts, R. Wilson, and A.R. Ravishankara, 1995, J. Geophys. Res., 100, 14163-14173.

301.	Tang, K.Y., P.W. Fairchild, and E.K.C. Lee, 1979, J. Phys. Chem., 83, 569.

302.	Thelen, M.-A., P. Felder, and J.R. Huber, 1993, Chem. Phys. Lett., 213, 275-281.

303.	Trolier, M., R.L. Mauldin III, and A.R. Ravishankara, 1990, J. Phys. Chem., 94, 4896-4907.

304.	Trolier, M. and J.R. Wiesenfeld, 1988, J. Geophys. Res., 93, 7119-7124.

305.	Turco, R.P., 1975, Geophys. Surveys, 2, 153-192.

306.	Turco, R.P., R.J. Cicerone, E.C.Y. Inn, and L.A. Capone, 1981, J. Geophys. Res., 86, 5373.

307.	Turnipseed, A.A., G.L. Vaghjiani, T. Gierczak, J.E. Thompson, and A.R. Ravishankara, 1991, J. Chem. Phys., 95, 3244-3251.

308.	Turnipseed, A.A., G.L. Vaghjiani, J.E. Thompson, and A.R. Ravishankara, 1992, J. Chem. Phys., 96, 5887.

309.	Tyndall, G.S., K.M. Stedman, W. Schneider, J.P. Burrows, and G.K. Moortgat, 1987, J. Photochem., 36, 133-139.

310.	Vaghjiani, G.L. and A.R. Ravishankara, 1989, J. Geophys. Res., 94, 3487-3492.

311.	Vaghjiani, G.L. and A.R. Ravishankara, 1990, J. Chem. Phys., 92, 996.

312.	Vaghjiani, G.L., A.A. Turnipseed, R.F. Warren, and A.R. Ravishankara, 1992, J. Chem. Phys., 96, 5878.

313.	Vaida, V., S. Solomon, E.C. Richards, E. Ruhl, and A. Jefferson, 1989, Nature, 342, 405.

314.	Vanlaethem-Meuree, N., J. Wisemberg, and P.C. Simon, 1978, Bull. Acad. Roy. Belgique Cl. Sci., 64, 31.

315.	Vanlaethem-Meuree, N., J. Wisemberg, and P.C. Simon, 1978, Bull. Acad. Roy. Belgique Cl. Sci., 64, 42.

316.	Vanlaethem-Meuree, N., J. Wisemberg, and P.C. Simon, 1979, Geophys. Res. Lett., 6, 451-454.

317.	Vasudev, R., 1990, Geophys. Res. Lett., 17, 2153-2155.

318.	Vogt, R. and R.N. Schindler, 1992, J. Photochem. Photobiol. A: Chem., 66, 133-140.

319.	Wahner, A., A.R. Ravishankara, S.P. Sander, and R.R. Friedl, 1988, Chem. Phys. Lett., 152, 507.

320.	Wahner, A., G.S. Tyndall, and A.R. Ravishankara, 1987, J. Phys. Chem., 91, 2734-2738.

321.	Wallington, T.J., P. Dagaut, and M.J. Kurylo, 1992, Chem. Rev., 92, 667-710.

322.	Walters, E.A., M. Gupta, J.T. Clay, D.D. Baldyga, J.R. Smith, and K. Glidden, 1994, personal communication.

323.	Walton, J.C., 1972, J. Chem. Soc. Farad. Trans., 68, 1559.

324.	Watson, R.T., 1977, J. Phys. Chem. Ref. Data, 6, 871-917.

325.	Wayne, R.P., 1987, Atm. Environ., 21, 1683-1694.

326.	Wayne, R.P., I. Barnes, J.P. Burrows, C.E. Canosa-Mas, J. Hjorth, G. Le Bras, G.K. Moortgat, D. Perner, G. Poulet, G. Restelli, and H. Sidebottom, 1991, Atmos. Environ., 25A, 1-203.

327.	Wine, P.H., W.L. Chameides, and A.R. Ravishankara, 1981, Geophys. Res. Lett., 8, 543-546.

328.	Wine, P.H. and A.R. Ravishankara, 1982, Chem. Phys., 69, 365-373.

329.	Wine, P.H., A.R. Ravishankara, D.L. Philen, D.D. Davis, and R.T. Watson, 1977, Chem. Phys. Lett., 50, 101.

330.	WMO, Atmospheric Ozone: 1985,  World Meteorological Organization Global Ozone Research and Monitoring Project, Report No. 16, 1986, Geneva: National Aeronautics and Space Administration.

331.	Xu, H. and J.A. Joens, 1993, Geophys. Res. Lett., 20, 1035-1037.

332.	Yao, F., I. Wilson, and H. Johnston, 1982, J. Phys. Chem., 86, 3611.

333.	Yokelson, R.J., J.B. Burkholder, R.W. Fox, R.K. Talukdar, and A.R. Ravishankara, 1994, J. Phys. Chem., 98, 13144-13150.

334.	Yoshino, K., A.S.C. Cheung, J.R. Esmond, W.H. Parkinson, D.E. Freeman, S.L. Guberman, A. Jenouvrier, B. Coquart, and M.F. Merienne, 1988, Planet. Space Sci., 36, 1469-1475.

335.	Yoshino, K., J.R. Esmond, A.S.-C. Cheung, D.E. Freeman, and W.H. Parkinson, 1992, Planet. Space Sci., 40, 185-192.

336.	Yoshino, K., J.R. Esmond, A.S.C. Cheung, D.E. Freeman, and W.H. Parkinson, 1990, J. Geophys. Res., 95, 11743.

337.	Yoshino, K., J.R. Esmond, D.E. Freeman, and W.H. Parkinson, 1993, J. Geophys. Res., 98, 5205-5211.

338.	Yoshino, K., D.E. Freeman, J.R. Esmond, R.S. Friedman, and W.H. Parkinson, 1988, Planet. Space Sci., 36, 1201-1210.

339.	Yoshino, K., D.E. Freeman, J.R. Esmond, R.S. Friedman, and W.H. Parkinson, 1989, Planet. Space Sci., 37, 419-426.

340.	Yoshino, K., D.E. Freeman, J.R. Esmond, and W.H. Parkinson, 1987, Planet. Space Sci., 35, 1067-1075.

341.	Yoshino, K., D.E. Freeman, and W.H. Parkinson, 1984, J. Phys. Chem. Ref. Data, 13, 207-227.

342.	Yoshino, K., D.F. Freeman, J.R. Esmond, and W.H. Parkinson, 1983, Planet. Space Sci., 31, 339-353.

343.	Zelikoff, M. and L.M. Aschenbrand, 1954, J. Chem. Phys., 22, 1685-1687.

344.	Zetzsch, C., 1989, Proceedings of the International Ozone Symposium 1988, R. Bojkov and P. Fabian, Editors,  Deepak,  Hampton, VA.

## HETEROGENEOUS CHEMISTRY

We have evaluated and tabulated the currently available information on heterogeneous stratospheric processes.  In addition, because of the increasing level of interest in tropospheric processes with a direct bearing on the fluxes of reactive species into the stratosphere, such as heterogeneous loss processes for partially oxidized degradation products of hydrohalocarbons and heterogeneous contrail and cloud processing of exhaust species from aircraft, we have included kinetic data for selected heterogeneous interactions relevant to modeling cloud droplet and aqueous aerosol chemistry in the free troposphere. However, both stratospheric and tropospheric heterogeneous chemistry are relatively new and rapidly developing fields, and further results can be expected to change our quantitative and even our qualitative understanding on a regular basis. The  complexity is compounded by the difficulty of characterizing the chemical and physical properties of atmospheric heterogeneous surfaces and then reproducing suitable simulations in the laboratory [99].

### Surface Types

To a first approximation there are three major types of surfaces believed to be present at significant levels in the stratosphere.  They are:  1) Type I - polar stratospheric clouds (PSCs), nominally composed of nitric acid trihydrate (HNO3 • 3H2O);  2) crystals of relatively  pure water ice, designated as Type II PSCs because they form at lower temperatures than Type I and are believed to be nucleated by Type I (similar surfaces may form as contrails behind high-altitude aircraft under some stratospheric conditions); and  3) sulfuric acid aerosol, which is nominally a liquid phase surface generally composed of 60 - 80 weight percent H2SO4 and, concomitantly, 40-20 weight percent H2O.  While PSCs, as their name suggests, are formed primarily in the cold winter stratosphere at high latitudes, sulfuric acid aerosol is present year round at all latitudes and may influence stratospheric chemistry on a global basis, particularly after large injections of volcanic sulfur episodically increase their abundance and surface area.   There is also increasing evidence that ternary H2SO4/HNO3/H2O liquid solutions may play a significant role in PSC formation.

In addition to the  major stratospheric surface types noted above, several other types of heterogeneous surfaces are found in the stratosphere and may play a significant role in some stratospheric processes.  For instance, recent laboratory work has indicated that nitric acid dihydrate (NAD) may play an important role in the nucleation of Type I PSCs (Worsnop et al. [180]; Fox et al. [44]) and that mixtures of solid nitric acid hydrates and sulfuric acid tetrahydrate (SAT) (Molina et al. [122]; Zhang et al. [188]) and/or a more complex sulfuric acid/nitric acid hydrate (Fox et al. [44]) may also be key to understanding Type I PSC nucleation and evolution.  Analyses of the range of atmospheric conditions possible in the polar stratosphere have also led to interest in solid SAT surfaces and possibly other forms of frozen sulfuric acid aerosols (Toon et al. [164]; Middlebrook et al. [117]), as well as liquid sulfuric acid aerosols significantly more dilute than the 60-80 weight percent normally present at lower latitudes (Wolff and Mulvaney [179]; Hofmann and Oltmans [77]; Toon et al. [164]).  Some modeling studies also suggest that certain types of major volcanic eruptions transport significant levels of sodium chloride into the stratosphere (Michelangeli et al. [116]), so studies of stratospheric trace species interacting with solid NaCl or similar salts, as well as salt solutions, have also been included.  Finally, aircraft and rocket exhausts contribute small but measurable amounts of carbonaceous soot (Pueschel et al. [133]) and aluminized solid propellant rocket exhausts and spacecraft debris produce increasing levels of alumina (Al2O3) and similar metal oxide particles (Zolensky et al. [189]) in the stratosphere.  In the free troposphere the primary heterogeneous surfaces of interest are liquid or solid water (cloud droplets, contrails) or aqueous sulfate solutions representative of background aerosols.

The detailed composition and morphology of each surface type are uncertain and probably subject to a significant range of natural variability.  Certain chemical and physical properties of these surfaces, such as their ability to absorb and/or solvate HCl and HNO3, are known to be strongly dependent on their detailed chemical composition.  Moreover, most heterogeneous processes studied under laboratory conditions (and in some cases proceeding under stratospheric conditions) can change the chemical composition of the surface in ways that significantly affect the kinetic or thermodynamic processes of interest.  Thus, a careful analysis of the time-dependent nature of the active surface is required in the evaluation of measured uptake kinetics experiments.  Experimental techniques which allow the measurement of mass accommodation or surface reaction kinetics with high time resolution and/or with low trace gas fluxes are often more credible in establishing that measured kinetic parameters are not seriously compromised by surface saturation or changing surface chemical composition.

The measured kinetic uptake parameters, mass accommodation coefficients, and surface reaction probabilities are separately documented for relevant atmospheric trace gas species for the  major and, where available, the minor stratospheric surfaces noted above.  Since these parameters can vary significantly with surface composition (e.g., the H2SO4/H2O ratio for sulfate aerosol or the HNO3/H2O ratio for Type I PSC) the dependence of these parameters on surface composition is reviewed where sufficient data are available.  Furthermore, data are also compiled for liquid water for several reasons.   First, this surface is one asymptote of the H2SO4/H2O aerosol continuum; second, the interactions of some trace species with liquid water and water ice (Type II PSC) surfaces are often similar; and third, the uptake of some trace species by water surfaces in the troposphere can play a key role in understanding their tropospheric chemical lifetimes and, thus, the fraction that may be transported into the stratosphere.

### Surface Porosity

The experimental techniques utilized to measure mass accommodation, heterogeneous reaction, and other uptake coefficients generally require knowledge of the surface area under study. For solid surfaces, and most particularly for water and acid ice surfaces formed in situ, the determination of how the molecular scale ice surface differs from the geometrical surface of the supporting substrate is not easy.  Keyser, Leu,  and coworkers have investigated the structure of water and nitric acid ice films prepared under conditions similar to those used in their flow reactor for uptake studies (Keyser et al. [97]; Keyser and Leu [95]; Keyser and Leu [94]).  They have demonstrated that ice films grown in situ from the vapor can have a considerably larger available surface than that represented by the  geometry of the substrate;  they have also developed a simple model to attempt to correct measured uptake rates for this effect (Keyser et al. [97]; Keyser et al. [96]).  This model predicts that correction factors are largest for small uptake coefficients and thick films.  The application of the model to experimental uptake data remains controversial (Keyser et al. [96]; Hanson and Ravishakara [71]; Kolb et al. [99]).  Some experimenters prefer to attempt growing ice surfaces as smooth as possible and to demonstrate that their measured uptake coefficients are only weakly dependent on surface thickness (Hanson and Ravishankara, [68]).  Similar issues arise for uptake experiments performed on powered, fused and single crystal salt or oxide surfaces (Fenter et al.[41]; Hanning-Lee et al. [57]).  The degree to which measured uptake parameters must be corrected for porosity effects will remain in some doubt until a method is devised for accurately determining the effective surface area for the surfaces actually used in uptake studies.  Most studies evaluated in this review assume that the effective ice or salt surface area is the geometrical area.

### Temperature Dependence

A number of laboratory studies have shown that mass accommodation coefficients and, to some extent, surface reaction probabilities can be temperature dependent.  While these dependencies have not been characterized for many systems of interest, temperature effects on kinetic data are noted where available.  More work that fully separates heterogeneous kinetic temperature effects from temperature controlled surface composition is obviously needed.

### Solubility Limitations

Experimental data on the uptake of some trace gases by various stratospherically relevant surfaces can be shown to be governed by solubility limitations rather than kinetic processes.  In these cases properly analyzed data can yield measurements of trace gas solubility parameters relevant to stratospheric conditions.  In general, such parameters can be strongly dependent on both condensed phase composition and temperature.  Such parameters may be very important in stratospheric models, since they can govern the availability of a reactant for a bimolecular heterogeneous process (e.g., the concentration of HCl available for the HCl + ClONO2 reaction on sulfuric acid aerosols) or the gas/condensed phase partitioning of a heterogeneous reaction product (e.g., the HNO3 formed by the reaction of N2O5 on sulfuric acid aerosols).

### Data Organization

Data for trace gas heterogenous interactions with relevant condensed phase surfaces are tabulated in Tables 63, 64, and 65.  These are organized into:

Table 63 - Mass Accommodation Coefficients

Table 64 - Surface Reaction Probabilities

Table 65 - Solubility Data

### Parameter Definitions

Mass accommodation coefficients (), represent the probability of reversible uptake of a gaseous species colliding with the condensed surface of interest.  For liquid surfaces this process is associated with interfacial (gas-to-liquid) transport and is generally followed by bulk liquid phase solvation.  Examples include:  simple surface absorption, absorption followed by ionic dissociation and solvation (e.g., HCl + nH2O  H+(aq) + Cl- (aq)), and absorption followed by a reversible chemical reaction with a condensed phase substituent (e.g., SO2 + H2O  H+ + HSO3- or CH2O + H2O CH2(OH)2).

The term "sticking coefficient" is often used for mass accommodation on solid surfaces where physisorption or chemisorption takes the place of true interfacial mass transport.

Processes involving liquid surfaces are subject to Henry’s law, which limits the fractional uptake of a gas phase species into a liquid.  If the gas phase species is simply solvated, a physical Henry’s law constraint holds; if the gas phase species reacts with a condensed phase substituent, as in the sulfur dioxide  or formaldehyde hydrolysis cases noted above, a “chemically modified” or “effective” Henry’s law constraint holds  (Clegg and Brimblecombe [26]; Schwartz [149]; Watson et al. [174]). Henry's law constants relate the equilibrium concentration of a species in the gas phase to the concentration of the same species in a liquid phase, and they have, in this report, units of M atm-1. These are tabulated for liquid surfaces in Table 65. Effective Henry's law constants are designated H*, while simple physical Henry's law constants are represented by H.  Effective Henry's law constants are also employed to represent decreased trace gas solubilities in moderate ionic strength acid or salt solutions with the use of a Setchenow coefficient formulation which relates H* to the concentration of the acid or salt [81].  It is presently unclear whether “surface solubility” effects govern the uptake on nominally solid water ice or HNO3/H2O ice surfaces in a manner analogous to bulk solubility effects for liquid substrates.

For some trace species on some surfaces, experimental data suggest that mass accommodation coefficients untainted by experimental saturation limitations have been obtained.  These are tabulated in Table 63.  In other cases experimental data can be shown to be subject to Henry’s law constraints, and Henry’s law constants, or at least their upper limits, can be determined.    Some experimental data sets are insufficient to determine if measured “uptake” coefficients are true accommodation coefficients or if the measurement values are lower limits compromised by saturation effects.  These are currently tabulated, with suitable caveats, in Table 63.

Surface reaction probabilities () are kinetic values for generally irreversible reactive uptake of trace gas  species on condensed surfaces.  Such processes may not be  rate limited by Henry’s law constraints; however, the fate of the uptake reaction products may be subject to saturation limitations.  For example, N2O5 has been shown to react with sulfuric acid aerosol surfaces.  However, if the H2SO4/H2O ratio is too high, the product HNO3 will be insoluble, and a large fraction will be expelled back into the gas phase.  Surface reaction probabilities for substantially irreversible processes are presented in Table 64.  Reaction products are identified where known. .

The total experimental uptake coefficient measured in laboratory heterogeneous kinetic experiments are also often symbolized by the symbol .  In those cases where surface and/or bulk reaction dominate the uptake, the total uptake coefficient (total) and reactive uptake coefficient (rxn) may well be identical.  More formally, for cases where bulk liquid phase reaction is facile and there are no gas phase diffusion constraints, the total uptake coefficient can be approximated in terms of rxn and sol as [99]:

where

and

where t is the time the trace gas is exposed to the liquid surface, R is the gas constant, D is the liquid phase diffusion coefficient, and  is the mean trace gas molecular speed.  In the limit of low solubility or long exposure time sol becomes negligible and:

Discussion of how to use this approach to model chemical reactions in liquid stratospheric aerosols can be found in Hanson et al. [74] and Kolb et al. [99].  Note that these formulations are approximate.  In cases where separate terms are competitive, more rigorous solution of kinetic differential operations may be appropriate.

For solid surfaces, bulk diffusion is generally too slow to allow bulk solubility or bulk kinetic processes to dominate uptake.  For solids, reactive uptake is driven by chemisorption/chemical reaction at the interface, a process that can also influence trace gas uptake on liquids.  In these cases surface reaction (surf) occurs in parallel, rather than in series with mass accommodation, thus:

Examples where this more complex situation holds for liquid surfaces can be found in Hu et al. [78] and Jayne et al.[88]. In such cases  may be significantly larger than .

The data in Tables 63 and 64 are organized by trace gas species, since some systematic variation may be expected for surface accommodation or reaction as the surface composition and/or phase is varied.  Data  presented for one surface may be  judged for “reasonableness” by comparing with data for a “similar” surface.  In some cases it is not yet clear if surface uptake is truly reversible (accommodation) or irreversibly reactive in nature.  In such cases the available uptake coefficients are generally tabulated in Table 63 as accommodation coefficients, a judgment yhat will be subject to change if more definitive data become available.

Where a specific evaluated value for an accommodation coefficient or reaction probability has been obtained, an estimated uncertainty factor is also tabulated.  However, when the data evaluation yielded only a lower or upper limit, no uncertainty factor can be reliably estimated and none is presented.

Description of and reference citations to many of the laboratory techniques used to obtain the data in the following three tables can be found in Kolb et al. [99].

### Table 63.  Mass Accommodation Coefficients ()

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| O | Sulfuric Acid | H2SO4 • nH2O(l) (97 wt.% H2SO4) | 298 | See Note |  | 1 |
| O3 | Water Ice Liquid Water Nitric Acid Ice Sulfuric Acid | H2O(s) H2O(l) HNO3 • 3H2O(s) H2SO4 • nH2O(l) (50 wt.% H2SO4) (97 wt.% H2SO4) | 195-262 292 195 195 196 | >0.04 >2 x 10-3‡ 2.5 x 10-4‡ See Note See Note | 3 | 2 3 2 4 4 |
| OH | Water Ice Liquid Water Sulfuric Acid Alumina | H2O(s) H2O(l) H2SO4 • nH2O(l) (28 wt.% H2SO4) (97 wt.% H2SO4) Al2O3(s) | 205-253 275 275 298 253-348 | >0.1 >4 x 10-3 >0.07 >5 x 10-4‡ 0.04 | 5 | 5 6 7 7 8 |
| HO2 | Liquid Water Aqueous Salts Sodium Chloride Potassium Chloride | H2O(l) NH4HSO4(aq) and LiNO3(aq) NaCl(s) KCl(s) | 275 293 295 295 | > 0.02 > 0.2 2 x 10-2 2 x 10-2 | 5 5 | 9 9 10 10 |
| H2O | Water Ice Liquid Nitric Acid Nitric Acid Ice Sulfuric Acid Sodium Chloride Carbon/Soot | H2O(s) HNO3•nH2O(l) HNO3• 3H2O(s) H2SO4 • nH2O (96 wt.% H2SO4) NaCl(s) NaCl(aq) (C(s) | 200 278 197 298 ~298 ~299 ~298 | 0.5 >0.3 See Note > 2 x 10-3‡ See Note > 0.5 >4 x 10-4 | 2 | 11 12 13 14 15 16 |
| H2O2 | Liquid Water Sulfuric Acid | H2O(l) H2SO4 • nH2O(l) (96 wt.% H2SO4) | 273 298 | 0.18* > 8 x 10-4‡ | 2 | 18 19 |
| NO | Water Ice Sulfuric Acid | H2O(s) H2SO4 • nH2O (70 wt.% H2SO4) (97 wt.% H2SO4) | 195 193-243 298 | See Note See Note See Note See Note |  | 20 21 21 |

Table 63.  (Continued)

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| NO2 | Water Ice | H2O(s) | 195 | See Note |  | 22 |
| HONO | Water Ice | H2O(s) | 180-200 | >1.0 x 10-3 |  | 23 |
| HNO3 | Water Ice Liquid Water Nitric Acid Ice Liquid Nitric Acid Sulfuric Acid | H2O(s) H2O(l) HNO3 • 3H2O(s) HNO3 • nH2O(l) H2SO4 • nH2O(l) (57.7 wt.% H2SO4) (73 wt.% H2SO4) (75 wt.% H2SO4) (97 wt.% H2SO4) | 200 268 191-200 278 191-200 283 230 295 | 0.3 0.2* 0.4 0.6 >0.3 0.1 >2 x 10-3 >2.4 x 10-3 | 3 2 2 2 2 | 24 25 26 27 28 28 28 28 |
|  | Sulfuric Acid Tetrahydrate | H2SO4 • 4 H2O(s) | ~192 | >0.02* |  | 28 |
| HO2NO2 | Water Ice Sulfuric Acid | H2O(s) H2SO4 • nH2O(l) (97 wt.% H2SO4) | ª200 298 | 0.1‡ See Note | 3 | 29 30 |
| NH3 | Liquid Water | H2O(l) | ~295 | 0.06* | 3 | 31 |
| CO2 | Liquid Water | H2O(l) | 293 | See Note |  | 32 |
| CH3OH | Liquid Water | H2O(l) | 260-291 | 0.12-0.02* | 2 | 33 |
| CH3CH2OH | Liquid Water | H2O(l) | 260-291 | 0.13-0.02* | 2 | 34 |
| CH3CH2CH2OH Liquid Water |  | H2O(l) | 260-291 | 0.08-0.02* | 2 | 35 |
| CH3CH(OH)CH3 Liquid Water |  | H2O(l) | 260-291 | 0.10-0.02* | 2 | 35 |
| HOCH2CH2OH Liquid Water |  | H2O(l) | 260-291 | 0.13-0.04* | 2 | 36 |
| CH2O | Liquid Water Sulfuric Acid | H2O(l) H2SO4 • nH2O(l) | 260-270 235-300 | 0.04 0.04 | 3 3 | 37 37 |
| CH3O2 | Sodium Chloride | NaCl(s) | 296 | >4 x 10-3 |  | 38 |
| CH3CHO | Liquid Water | H2O(l) | 267 | >0.03* |  | 39 |
| CH3C(O)CH3 | Liquid Water | H2O(l) | 260-285 | 0.07-0.01* | 2 | 40 |
| HC(O)OH | Liquid Water | H2O(l) | 260-291 | 0.10-0.02* | 2 | 41 |
| CH3C(O)OH | Liquid Water | H2O(l) | 260-291 | 0.15-0.03* | 2 | 42 |

Table 63.  (Continued)

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Cl2 | Water Ice | H2O(s) | 200 | See Note |  | 43 |
| OClO | Water Ice | H2O(s) | 100,189, 200 | See Note |  | 44 |
| HCl | Water Ice Liquid Water Nitric Acid Ice Sulfuric Acid | H2O(s) H2O(l) HNO3 • 3H2O(s) H2SO4 • nH2O(l) (n≥8, ≤40 wt.% H2SO4) | 191- 211 274 191- 211 283 218 | 0.3 0.2* 0.3 0.15* >0.005* | 3 2 3 2 | 45 46 47 48 |
|  |  | (n<8, >40 wt.% H2SO4) (No data - all measurements limited by HCl solubility) |  |  |  |  |
|  | Sulfuric Acid Tetrahydrate | H2SO4 • 4H2O(s) | 192-201 | See Note |  | 49 |
| CCl2O | Liquid Water | H2O(l) | 260-290 | See Note |  | 50 |
| CCl3CClO | Liquid Water | H2O(l) | 260-290 | See Note |  | 50 |
| HBr | Water Ice Nitric Acid Ice | H2O(s) HNO3 • 3H2O(s) | 200 200 | > 0.2 > 0.3 |  | 51 51 |
| HOBr | Sulfuric Acid | H2SO4 in H2O(l) (58 wt. % H2SO4) | -228 | >0.05‡ |  | 52 |
| CHBr3 | Water Ice Sulfuric Acid | H2O(l) H2SO4 • nH2O(l) (97 wt.% H2SO4) | 220 220 | See Note >3 x 10-3‡ |  | 53 53 |
| HF | Water Ice Nitric Acid Ice | H2O(s) HNO3 • 3H2O(s) | 200 200 | See Note See Note |  | 54 54 |
| CF2O | Water Ice Liquid Water Nitric Acid Ice Sulfuric Acid | H2O(s) H2O(l) HNO3 • 3H2O(s) H2SO4 • nH2O(l) (40 wt.% H2SO4) (60 wt.% H2SO4) | 192 260-290 192 215-230 | See Note See Note See Note >3 x 10-6‡ >6 x 10-5‡ |  | 55 50 55 55 55 |
| CF3CFO | Liquid Water | H2O(l) | 260-290 | See Note |  | 50 |
| CF3COOH | Liquid Water | H2O(l) | 263-288 | 0.2-0.1* | 2 | 56 |
| CF3CClO | Liquid Water | H2O(l) | 260-290 | See Note |  | 50 |
| SO2 | Liquid Water Sulfuric Acid Carbon/Soot | H2O(l) H2SO4 • nH2O(l) (97 wt.% H2SO4) C(s) | 260-292 298 298 | 0.11 See Note 3 x 10-3 | 2 5 | 57 58 59 |

Table 63.  (Continued)

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| CH3S(O)CH3 | Liquid Water | H2O(l) | 262-281 | 0.16-0.08* | 2 | 60 |
| CH3S(O2)CH3 Liquid Water |  | H2O(l) | 262-281 | 0.27-0.08* | 2 | 60 |
| CH3S(O2)OH | Liquid Water | H2O(l) | 264-278 | 0.17-0.11* | 2 | 60 |

*Varies with T, see Notes

‡May be affected by surface saturation

#### Notes to Table 63

1.	O on H2SO4 • nH2O - Knudsen cell experiment of Baldwin and Golden [9] measured an uptake coefficient limit of <10-6; this result probably cannot be equated with an accommodation coefficient due to surface saturation.

2.	O3 on H2O(s) and HNO3 • nH2O - Undoped ice surfaces saturate too quickly for reliable measurements.  When ice is doped with Na2SO3 to chemically remove absorbed O3 the apparent  increases to 1 x 10-2 (0.1M) or up to 4 x 10-2 (1M) (Dlugokencky and Ravishankara [34]).  Limit of   < 10-6 for undoped ice is consistent with earlier measurement by Leu [103] of ≤1 x 10-4 and with < 6 x 10-5 obtained by Kenner et al. [93].  Dlugokencky and Ravishankara also measured the tabulated value of an uptake coefficient for O3 on a NAT “like” surface, but the data were difficult to reproduce and the surfaces were not well characterized. Kenner et al. also measured a lower limit for an uptake coefficient of 8 x 10-5 on NAT at 183 K, but this measurement is also certainly limited by surface saturation.

3.	O3 on H2O(l) - Utter et al. [165] used a wetted wall flow tube technique with various chemical scavengers to measure a lower limit for  of 2 x 10-3.  The stopped flow measurement technique using an SO3 = scavenger (Tang and Lee [157]) is subject to saturation effects, so their quoted  of 5.3 x 10-4 is also taken as a lower limit.

4.	O3 on H2SO4 • nH2O - Recent flow tube measurements (Dlugokencky and Ravishankara [34]) of an uptake coefficient limit of <10-6 on both 50 and 97 wt. % H2SO4 surfaces are consistent with earlier, but probably less quantitative, static systems measurements of Olszyna et al. [129] and aerosol chamber measurements of Harker and Ho [75], who report uptake coefficients of the order 10-8 or less for a variety of sulfuric acid concentrations and temperatures.  In these earlier experiments, doping the H2SO4 with Ni2+, Cr2+, Al3+, Fe3+ and NH4+ (Olszyna et al. [129]) or Al2O3 or Fe2O3 (Harker and Ho [75]) did not significantly increase measured O3 loss.  A lower limit of 1 x 10-6 was also reported by Baldwin and Golden [8] for 97 wt % H2SO4 at 295 K.  All measurements are subject to solubility limitations and probably do not reflect true limits on mass accommodation.

5.	OH on H2O(s) - Cooper and Abbatt[27] analyzed uptake rates in a wall-coated flow tube to determine an initial  ~ 0.1 over the temperature range of 205 - 230 K.  Uptake coefficients decreased at longer exposure times, indicating surface saturation.  These data indicate that  is at least 0.1 and possibly much larger.  This is confirmed by an earlier experiment using a coated insert/flow tube technique by Gerhenzon et al. [50], which yielded  > 0.4 at 253 K.

6.	OH on H2O(l) - see Note for HO2 on H2O(l). The OH and HO2 measurements of Hanson et al. [60] are subject to same analysis issues.

7.	OH on H2SO4•nH2O - See Note for HO2 on  H2O(l) for measurement (28 wt.% H2SO4) by Hanson et al. [60] and Note for O on H2SO4 for measurement (97 wt. % H2SO4) by Baldwin and Golden [9].

8.	OH on Al2O3(s) - Measured value is from flow tube experiment with native oxide on aluminum as the active surface. An uptake coefficient of 0.4 ± 0.2 independent of temperature over the range of 253-348 K was measured (Gershenzon et al. [50]).

9.	HO2 on H2O(l) - Determination of  in liquid-wall flow tube (Hanson et al. [60]) is dependent on gas-phase diffusion corrections; measured limit ( >0.02) is consistent with  = 1.  In the aqueous salt aerosol measurements of Mozurkewich et al. [125], HO2 was chemically scavenged by Cu++  from added CuSO4 to avoid Henry’s law constraints; the measured limit of >0.2 is also consistent with  =1.

10.	HO2 on NaCl(s) and KCl(s) - Measured values of  = 1.8 x 10-2 for KCl and 1.6 x 10-2 for NaCl, both at 295 K by Gersherzon et al.[52] supplementing an earlier value of  - 8 x 10-3 measured by Gersherzon and Purmal [51], results have not been calibrated with a competitive technique.

11.	H2O on H2O(s) - Measurements are available from Leu [104] giving 0.3 (+0.7, -0.1) at 200 K and Haynes et al. [76] (1.06 ± 0.1 to 0.65 ± 0.08) from 20 to 185 K.  Brown et al.[18] used molecular beam reflection techniques to measure a value of  = 0.99 ± 0.03 between 85 and 150 K and optical interference methods to obtain  = 0.97 ± 0.10 between 97 and 145 K.

12.	H2O on HNO3/H2O(l) - Rudolf and Wagner[147] used aerosol expansion chamber techniques to illustrate that on liquid water/nitric acid aerosols  is greater than 0.3 and is consistent with 1.0 at 278 K.

13.	H2O on HNO3•nH2O(s) - Middlebrook et al. [118] measured an uptake coefficient of .002 for water vapor co-depositing with nitric acid over NAT at 197 K.

14.	H2O on H2SO4 • nH2O - Baldwin and Golden [8] measured  ~2 x 10-3, which is almost certainly affected by surface saturation.  See Note 15 for H2O2 on H2SO4 • nH2O.

15.	H2O on NaCl(s) - Fenter et al.[40] used Knudsen cell/mass spectrometry methods to measure  < 2 x 104 for H2O(g) uptake on NaCl powders, an observation confirmed by Beichert and Finlayson-Pitts[13], who found  < 1 x 10-5.  However, Dai et al.[28] used FTIR spectroscopy on NaCl crystallite films at 240 and 296 K to determine that a water adlayer does adhere to dry salt and that a small fraction of surface sites (< 1%) cause H2O dissociation.  It is likely that the measurements of Fenter et al. and Beichert and Finlayson-Pitts were affected by surface saturation.

16.	H2O on NaCl(aq) - Fung et al.[46] used Mie resonance scattering techniques to quantify aqueous NaCl droplet growth (5.8 to 7.8 µm), yielding fitted values of  > 0.5 and consistent with 1.0.

17.	H2O on C(s) - Rogaski et al.[142] used initial Knudsen cell uptake measurements to estimate  = (4 ±2) x  10-4 for H2O vapor on amorphous carbon at 298 K.  Pretreatment of the carbon surface with gaseous O3, NO2, and SO2 made little change in .  However, pretreatment with HNO3 and H2SO4 increased uptake coefficients dramatically to (11 ±1) x 10-3 and (27 ±1) x 10-3, respectively.

18.	H2O2 on H2O(l) - Measured accommodation coefficient (Worsnop et al. [181]) has a strong negative temperature dependence over the measured range of 260-292 K, with  = 0.3 at 260 K decreasing to 0.1 at 292 K.

19.	H2O2 on H2SO4•nH2O - Knudsen cell uptake measurements are subject to surface saturation, thus uptake coefficient value of 7.8 x 10-4 quoted by Baldwin and Golden [8] is almost certainly a lower limit for .  This effect is probably also responsible for the lack of measured uptake ( <10-6) for NO, NO2, SO2, Cl2, and other species reported in this reference and Baldwin and Golden [9].

20.	NO on H2O(s) -  NO data (Leu [103], Saastad et al. [148]) subject to same concerns as NO2.  See Note for NO2 on H2O(s).

21.	NO on H2SO4•nH2O -  See Notes for H2O2 on H2SO4 • nH2SO4 and NO2 on H2SO4 • nH2O.  NO is subject to the same concerns as NO2 for both reported measurements (Saastad et al. [148]; Baldwin and Golden [8]).

22.	NO2 on H2O(s) - In the absence of a chemical sink, Leu [103] measured no sustained uptake of NO2 on ice yielding an apparent  ≤1 x 10-4.  Saastad et al. [148] measured a lower limit of 5 x 10-5 for temperatures between 193 and 243 K.  However these values are probably influenced by surface saturation.

23.	HONO on H2O(s) - Fenter and Rossi[42] measured reversible uptake on water ice between 180 and 200 K using a Knudsen cell technique.  An initial uptake coefficient of 1 x 10- 3 suggests that  equals or exceeds this value.

24.	HNO3 on H2O(s) - Leu [104] reports 0.3 (+0.7, -0.1).  Some additional uncertainty is introduced by effective ice surface area in fast-flow measurement (see Keyser et al. [97]).  Hanson [58] measured an uptake coefficient of > 0.3 at 191.5 and 200 K.

25.	HNO3 on H2O(l) - Measured  has a strong negative temperature dependence varying from 0.19 ± 0.02 at 268 K to 0.07 ± 0.02 at 293 K (Van Doren et al. [167]).  Ponche et al. [132] measured an accommodation coefficient of 0.05 ± 0.01 at 297 K.

26.	HNO3 on HNO3 • nH2O(s) - Hanson [58] measured uptake coefficients of > 0.3 and >0.2 on NAT surfaces at 191 K and 200 K, respectively.  Middlebrook et al. [118] measured an uptake coefficient of 0.7 on NAT at 197 K under conditions where both nitric acid and water vapor were co-depositing.

27.	HNO3 on HNO3 • nH2O(l) - Rudolf and Wagner used aerosol expansion chamber techniques to deduce that  for HNO3 on 278 K H2O/HNO3 droplets is > 0.3 and probably close to 1.  The consistency of this value with smaller (~0.2) values measured for uptake on pure water by Van Doren et al. [167] is unclear, since the mechanism of co-condensation is unknown and the composition of the surface in the aerosol expansion chamber experiments may be kinetically controlled and has not been well determined.

28.	HNO3 on H2SO4•nH2O and H2SO4 • 4H2O(s) - Initial uptake at 73 wt. % H2SO4 allows a measurement of  = 0.11 ± 0.01 at 283 K (Van Doren et al. [167]).  This value is expected to increase at lower temperatures, in a manner similar to H2O(1) uptake (Van Doren et al. [166]).  Total HNO3  uptake is subject to Henry’s law solubility constraints, even at stratospheric temperatures (Reihs et al. [135]).  Solubility limitations also affected the earlier “sticking coefficient” measurements of Tolbert et al. [161] for 75 wt % H2SO4 at 230 K.  Hanson [58] measured an uptake coefficient of >0.3 for frozen 57.7 wt. % sulfuric acid at 191.5 and 200 K.  Baldwin and Golden [8] reported a lower limit of 2.4 x 10-4 on 97 wt. % H2SO4 at 295 K, also reflecting solubility limits.  Iraci et al. [83] monitored nitric acid trihydrate growth on sulfuric acid tetrahydrate with infrared techniques, measuring HNO3 uptake coefficient limits of >0.03 at 192.5 K and >0.08 at 192 K.  These measurements involved co-deposition of water vapor.

29.	HO2NO2 on H2O(s) - Li et al. [106] measured an uptake coefficient of 0.15 ±0.10; uptake may be limited by surface saturation.

30.	HO2NO2 on H2SO4•nH2O(l) - Baldwin and Golden measured  = 2.7 x 10-5, which is probably solubility limited; see Note 15 for H2O2 on H2SO4 • nH2O.

31.	NH3 on H2O(l) - Ponche et al. [132] used a droplet train technique to obtain  = (9.7 ±0.9) x 10-2 at 290 K, and Bongartz et al.[16] used a liquid jet technique to obtain  = 4.0 (+3.0, - 0.05) x 10-2.  Earlier levitated droplet evaporation experiments [158] on NH4Cl obtained a larger evaporation coefficient of  = 0.29 ±0.03, which is discounted because of the indirect nature of the experiment.

32.	CO2 on H2O(l) - Noyes et al.[128] used a dynamic stirring technique to monitor pressure decreases in a closed cylinder.  They inferred  = (5.5±0.5) x 10- 8 at 293 K.  This technique is uncalibrated against more widely used procedures and probably suffers from surface saturation effects.  Measured  is probably many orders of magnitude too small.

33.	CH3OH on H2O(l) - Jayne et al. [86] measured uptake from 260-291 K and derived accommodation coefficients fitting /(1-) = exp(-G‡obs/RT),  where  G‡obs = -8.0 kcal/mol + 34.9  cal  mol-1  K–1  T(K).

34.	CH3CH2OH on H2O(l) - Jayne et al. [86] measured uptake from 260-291 K and derived accommodation coefficients fitting /(1-) = exp(-G‡obs/RT), where G‡obs = -11.0 kcal/mol + 46.2 cal mol-1 K-1 T(K).  Similar, but somewhat larger values were reported for chloro-, bromo-,  and iodo-ethanols.

35.	CH3CH2CH2OH and CH3CH(OH)CH3 on H2O(l) - Jayne et al. [86] measured uptake coefficients between 260 and 291 K and derived accommodation coefficients fitting /(1-) = exp (-G‡obs/RT),  where G‡obs = - 9.2 kcal mol-1 + 40.9 cal mol-1 K-1 T(K) for 1-propanol and -9.1 kcal mol-1 + 43.0 cal mol-1 K-1 T(K) for 2-propanol.  Similar data for t-butanol were also reported.

36.	HOCH2CH2OH on H2O(l) - Jayne et al. [86] measured uptake coefficients for ethylene gycol between 260 and 291 K  and derived accommodation coefficients fitting /(1-) = exp(-G‡obs/RT), where G‡obs =             - 5.3 kcal mol-1 + 24.5 cal mol-1 K-1 T(K).

37.	CH2O + H2O(l), H2 SO4 • mHNO3 • nH2O(l) - Jayne et al.[88]  report uptake measurements for 0 - 85 wt % H2SO4 and 0 - 54 wt% HNO3 over a temperature range of 241 - 300 K.  Measured uptake coefficients vary from 0.0027 - 0.027, increasing with H+ activity (Jayne et al ([88]; Tolbert et al., [160]), and with increasing pH above 7 (Jayne et al., [87]).  Reversible uptake is solubility limited through reactions to form H2C(OH)2 and CH3O.+  Model of uptake kinetics (Jayne et al., [88]) consistent with  = 0.04 ± 0.01 for all compositions.  A chemisorbed surface complex dominates uptake at 10 - 20 wt % H2SO4, and CH3O+ formation dominates above 20 wt % (Tolbert et al., [94/1564]; Jayne et al.[88]).  These chemical mechanisms allow  to greatly exceed  for strong acid and basic solutions.  A full uptake model for acid solutions is presented in Jayne et al. [88], and for basic solutions  in Jayne et al. [87].

38.	CH3O2 + NaCl(s) - Gershenzon et al.[52] measured the uptake of CH3O2 on crystalline NaCl(s) in a central  rod  flow  apparatus.   They determined a value of  = (4 ±1) x 10-3 at 296 K,  suggesting that  ≥ 4  x   10-3.

39.	CH3CHO on H2O(l) - Jayne et al. [87] measured a lower accommodation coefficient limit of > 0.03 at 267 K.  Uptake can be limited by Henry's law and hydrolysis kinetics effects - see reference.

40.	CH3C(O)CH3 on H2O(l) - Duan et al. [36] measured uptake between 260 and 285 K, deriving  = 0.066 at the lower temperature and 0.013 at the higher, with several values measured in between.  Measured values fit       /(1-) = exp(-G‡obs/RT), where G‡obs = -12.7 kcal/mol + 53.6 cal mol-1 K-1 T(K).

41.	HC(O)OH on H2O(l) - Jayne et al. [86] measured uptake coefficients for formic acid between  260 and  291 K and  derived accommodation coefficients fitting /(1-) = exp(-G‡obs/RT), where G‡obs = -7.9 kcal mol-1 + 34.9 cal mol-1 K-1 T(K).

42.	CH3C(O)OH on H2O(l) - Jayne et al. [86] measured uptake coefficients for acetic acid between  260 and  291 K  and derived an accommodation coefficient fitting /(1-) = exp(-G‡obs/RT), where G‡obs =         - 8.1 kcal mol-1 + 34.9 cal mol-1 K-1 T(K).

43.	Cl2 on H2O(s) - Measurement of Leu [104] yielded a limit of <1 x 10-4 for Cl2 and is subject to same concern as NO2 (see note 18).  A similar limit of < 5 x 10-5 has been measured by Kenner et al. [93], which is also probably limited by surface saturation.

44.	OClO + H2O(s) - Brown et al.[19] and Graham et al.[56] used complementary ultra high-vacuum (UHV) and coated-wall flow tube techniques to show sub-monolayer reversible absorption of OClO on water ice at 100 K (UVH) and 189 and 200 K (flow tube).  No kinetic data are available at stratospheric temperatures but the mass accommodation coefficient for 100 K ice surfaces is near unity, with values of 0.8 ± 0.2 reported for amorphous ice and 0.6 ±0.2 for crystalline ice [56].

45.	HCl on H2O(s) - Leu [104] (0.4; +0.6, -0.2) and Hanson and Ravishankara, [66] ( ≥ 0.3) are in reasonable agreement at stratospheric ice temperatures.  More recently, a great deal of experimental effort (Abbatt et al. [4], Koehler et al. [98],  Chu et al. [25], Graham and Roberts [54], Graham and Roberts[55]; Rieley et al.[136]) has gone into understanding the uptake of HCl by ice surfaces.  Rieley et al. measured  = 0.95±0.05 at 80 - 120 K.  Water ice at stratospheric temperatures can take up a large fraction of a monolayer even at HCl partial pressures typical of the stratosphere.  Both the thermodynamic and spectroscopic properties of this absorbed HCl indicate that it has dissociated to ions, forms ionic hydrates, and is highly reactive.  These experimental results contrast with initial theoretical calculations that predicted undissociated HCl hydrogen bonded to the ice surface and a very small adsorption probability at stratospheric temperatures (Kroes and Clary [100]); more recent simulations result in higher adsorption energies and theoretical accommodation coefficients of one for 190 K surfaces [Wang and Clary [173]].  Recent  molecular dynamics calculations by Gertner and Hynes[53] also show that ionic absorption is thermodynamically favorable by about 5 kcal/mole.  At HCl partial pressures significantly above those typical of the stratosphere, a liquid surface layer forms on the ice, greatly enhancing the total amount of HCl that the surface can absorb.

46.	HCl on H2O(1)  -  Recommendation is based on Van Doren et al. [166].  Measured ’s decrease from 0.18 ±0.02 at 274 K to 0.064 ±0.01 at 294 K, demonstrating a strong negative temperature dependence.  Tang and Munkelwitz [158] have measured a larger (0.45 ±0.4) HCl evaporation coefficient for an aqueous NH4Cl droplet at 299 K.

47.	HCl on HNO3 • nH2O - There was previously severe disagreement between Hanson and Ravishankara [66] (≥0.3) for  NAT (54 wt. % HNO3), and Leu and coworkers (Moore et al. [123],  Leu  et  al. [105]).  However, subsequent experiments  at lower HCl concentrations by Leu and coworkers (Chu et al. [25]) as well as Abbatt and Molina [5] are generally consistent with Hanson and Ravishankara.  In particular, Abbatt and Molina [5] report a large uptake coefficient ( >0.2).  The measurements of Hanson and Ravishankara are consistent with = 1.  The experiments at stratospherically representative HCl concentrations show that HNO3 rich NAT surfaces adsorb significantly less HCl than H2O rich surfaces.

48.	HCl on H2SO4•nH2O - Measurements by Watson et al. [174] at 284 K show  = 0.15±0.01 independent of n for n ≥ 8.  Experimental uptake and, therefore, apparent  falls off for n ≤8 (≥40 wt. % H2SO4).  This behavior is also observed at stratospheric temperature (218 K) by Hanson and Ravishankara [66].  More recent measurements by Robinson et al. (to be published) extend mass accommodation measurements to lower temperatures, yielding significantly higher values. Solubility constraints also controlled earlier low temperature uptake measurements of Tolbert et al. [161].  A review of the most recent solubility data is presented in Table 60.

49.	HCl on H2SO4 • 4H2O(s) - Uptake is a strong function of temperature and water vapor partial pressure (relative humidity) (Zhang et al. [188]), both of which affect adsorbed surface water.

50.	Halocarbonyls on H2O(l) - Uptake is limited by Henry's law solubility and hydrolysis rate constants (De Bruyn et al. and George et al. [47, 49]. See Table 60.

51.	HBr on H2O(s) and HNO3 • nH2O - Hanson and Ravishankara [67, 69] have reported large uptake  coefficients for HBr on 200  K ice and NAT.  Lower limits of >0.3 and  >0.2  for ice are reported in the two referenced publications, respectively, and a limit of >0.3 is reported for NAT.  No surface saturation was observed, leading to the supposition that HBr, like HCl, dissociates to ions on ice surfaces at stratospheric temperatures.  Abbatt [1] measured an uptake coefficient lower limit of >0.03 on water ice at 228 K in agreement with Hanson and Ravishankara.  Rieley et al. measured an  of 1.0 ± 0.05 for water ice at 80 - 120K and Chu and Heron[23] report equilibrium HBr coverages for ice at 188 and 195 K.

52.	HOBr on H2SO4 • nH2O(l) - Abbatt [1] measured an uptake coefficient of 0.06 ±(0.02) by measuring HOBr gas phase loss at 228 K. This result may well be a lower limit due to surface saturation effects.

53.	CHBr3 on H2O(s) and H2SO4•nH2O(l) - Hanson and Ravishankara [69] investigated the uptake of bromoform on ice and 58 wt.% sulfuric acid at 220 K.  No uptake on ice was observed, with a measured uptake coefficient of <6 x 10-5.  Reversible uptake by the sulfuric acid surface was observed with an initial uptake coefficient of >3 x 10-3; both measurements are probably limited by surface saturation.

54.	HF on H2O(s) and HNO3 • nH2O(s) - Hanson and Ravishankara [67] attempted to measure the uptake of HF by 200 K water ice and NAT surfaces but were unable to observe measurable adsorption.  They surmise that, unlike HCl and HBr, HF does not dissociate to ions on ice or NAT surfaces at 200 K.  Lack of measurable uptake is probably due to surface saturation.

55.	CF2O on H2O(s), HNO3 • nH2O and H2SO4 • nH2O -  Uptake coefficient measurements by Hanson and Ravishankara [64] on stratospheric surfaces are probably subject to surface and/or bulk saturation effects and may not represent accommodation coefficient measurements, particularly the lower limits of >3 x 10-6 reported for water and nitric acid ices.

56.	CF3COOH on H2O(l) - Hu et al. [79] measured mass accommodation coefficients for five haloacetic acids, including trifluoroacetic acid (TFA); the others were mono-, di-, trichloro-, and chlorodifluoro-acetic acids.  All displayed a negative temperature dependence and values for of about 0.1 at 273 K.

57.	SO2 on H2O(1) - Measured  of 0.11 ± 0.02 has no significant temperature variation over a temperature range of 260 - 292 K (Worsnop et al. [181]).  Ponche et al. [132] measured  0.13 ± 0.01 at  298 K, in agreement with the earlier measurement.  Shimono and Koda[151] estimated an of 0.2 at 293.5 K from analysis of pH-dependent uptake coefficients in a novel liquid impingement technique that has not been calibrated with other gases. Donaldson et al. ([35]) have used second harmonic generation spectroscopy to detect a chemisorbed SO2 surface species which was predicted from earlier uptake measurements by Jayne et al.[85]; this surface complex may play a role in SO2 heterogeneous reactions on aqueous surfaces.

58.	SO2 on H2SO4 • nH2O.  See Note for H2O2 on H2SO4 • nH2O.

59.	SO2 on C(s) - Initial and longer-term uptake Knudsen cell values of Rogaski et al. yielded 1) x 10-3 for room temperature amorphous carbon, suggesting ~ 3 x 10-3 since no reaction products were observable with gas phase mass spectrometry.

60.	CH3S(O)CH3, CH3S(O2)CH3 and CH3S(O2)OH on H2O(l)  -  De Bruyn et al. [32]  measured  uptake  over  the  temperature  range ~262-281 K and  derived  accommodation  coefficients  fitting  / (1 - ) =         exp(-G‡obs/RT), where G‡obs = - 0.12 kcal mol-1 + 23.1 cal mol-1 K-1 T(K) for dimethylsulfoxide,       -10.7 kcal mol-1 + 43.0 cal mol-1 K-1 T(K) for dimethylsulfone and -3.50 kcal mol-1 + 16.7 cal mol-1   K-1 T(K) for methanesulfonic acid.

### Table 64.  Gas/Surface Reaction Probabilities ()

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| O3 + Surface  Products |  |  |  |  |  |  |
| O3 | Alumina Carbon/Soot Sodium Chloride | Al2O3(s) C(s) NaCl(s) | 210-300 300 300 | See Note 3 x 10-3 >2 x 15-10 | 20 | 1 2 1 |
| OH + Surface Products |  |  |  |  |  |  |
| OH | Water Ice Hydrochloric Acid Nitric Acid Ice Sulfuric Acid Sodium Chloride | H2O(s) HCl • nH2O(l) HNO3 • 3HzO(s) H2SO4 • nH2O(l) NaCl(s) | 205-230 220 200-228 200-298 245-339 | >0.01 >0.2 >0.2 >0.2 1.2 x 10-5 exp 1750/T | 3 | 3 4 5 6 7 |
| HO2 + Surface Products |  |  |  |  |  |  |
|  | Water Ice Sulfuric Acid | H2O(s) H2SO4 • nH2O(l) (28 wt %) (55 wt %) (80-96 wt %) | 223 275 223 243 | 0.025 .0.07 >0.05 >0.2 | 3 | 8 8 |
| 2NO2 + H2O(l) HONO + HNO3 |  |  |  |  |  |  |
| NO2 | Liquid Water | H2O(l) |  | See Note |  | 9 |
|  | Sulfuric Acid | H2SO4 • nH2O |  | See Note |  | 10 |
| NO2 + C(s) Products |  |  |  |  |  |  |
| NO2 | Carbon/Soot | C(s) |  | See Note |  | 11 |
| 2NO2 + NaCl(s) ClNO + NaNO3 |  |  |  |  |  |  |
| NO2 | Sodium Chloride | NaCl(s) | 298 | See Note |  | 12 |
| NO3 + H2O(l) HNO3 + OH |  |  |  |  |  |  |
| NO3 | Liquid Water | H2O(l) | 273 | 2 x 10-4 | 20 | 13 |

Table 64.  Continued

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| N2O5 + H2O 2HNO3 |  |  |  |  |  |  |
| N2O5 | Water Ice Liquid Water Nitric Acid Ice Sulfuric Acid Sulfuric Acid Monohydrate Sulfuric Acid Tetrahydrate Ternary Acid | H2O(s) H2O(l) HNO3 • 3H2O(s) H2SO4 • nH2O(l) H2SO4 • H2O(s) H2SO4 • 4H2O(s) H2SO4 • nHNO3 • nH2O(l) | 195-200 260-295 200 195-300 200-300 195-207 195-218 | 0.01 0.05* 3 x 10-4 0.1 See Note 0.006 See Note | 3 2 3 See Note 3 2 | 14 15 16 17 18 19 17 |
| N2O5 + HCl(s)  ClNO2 + HNO3 |  |  |  |  |  |  |
| N2O5 | Water Ice Nitric Acid Ice Sulfuric Acid Monohydrate | H2O(s) • HCl(s) HNO3 • 3H2O(s) • HCl(s) H2SO4 • H2O(s) | 190-220 200 195 | 0.03 0.003 <1 x 10-4 | See Note 2 | 20 21 22 |
| N2O5 + NaCl(s)  ClNO2 + NaNO3(s) |  |  |  |  |  |  |
| N2O5 | Sodium Chloride | NaCl(s) NaCl(aq) | -300 | 5 x 10-4 >0.02 | 20 | 23 23 |
| N2O5 + HBr(s) BrNO2 + HNO3 |  |  |  |  |  |  |
| N2O5 | Nitric Acid Ice | HNO3 • 3H2O(s) | 200 | 0.005 | 10 | 24 |
| N2O5 + MBr(s) Products |  |  |  |  |  |  |
| N2O5 | Sodium Bromide Potassium Bromide | NaBr(s) KBr(s) | ~300 ~300 | 4 x 10-3 | See Note 10 | 25 25 |
| HONO + H2O Products |  |  |  |  |  |  |
| HONO | Liquid Water | H2O(l) | 247-297 | 0.04 | 5 | 26 |
| HONO + H2SO4 Products |  |  |  |  |  |  |
| HONO | Sulfuric Acid | H2SO4(l) | 180-200 | See Note |  | 27 |
| HONO + HCl ClNO + H2O |  |  |  |  |  |  |
| HONO | Water Ice | H2O(s) | 180-200 | 0.05 | 3 | 28 |

Table 64.  Continued

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| HONO + NaCl Products |  |  |  |  |  |  |
| HONO | Sodium Chloride | NaCl(s) | ~300 | <1 x 10-4 |  | 29 |
| HNO3 + C(s) Products |  |  |  |  |  |  |
| HNO3 | Carbon/Soot | C(s) | 190-440 | 0.04 | 5 | 30 |
| HNO3 + NaX(s) HX + NaNO3 |  |  |  |  |  |  |
| HNO3 | Sodium Chloride Sodium Bromide Potassium Chloride Potassium Bromide | NaCl(s) NaBr(s) KCl(s) KBr(s) | 295-298 ~290 ~290 ~290 | 0.02 0.02 0.02 0.02 | 3 10 10 10 | 31 31 31 31 |
| NH3 + H2SO4 NH4HSO4 |  |  |  |  |  |  |
| NH3 | Sulfuric Acid | H2SO4 • nH2O | 288-300 | 0.4 | 2.5 | 32 |
| CH3C(O)O2 + H2O CH3C(O)OH + HO2 |  |  |  |  |  |  |
| CH3C(O)O2 | Liquid Water Sulfuric Acid | H2O(l) H2SO4 • nH2O (84 wt % H2SO4) (51 wt % H2SO4) (71 wt % H2SO4) | 225 246 223 298 | 4 x 10-3 3 x 10-3 1 x 10-3 1 x 10-3 | 3 3 3 3 | 33 33 |
| Cl + Surface Products |  |  |  |  |  |  |
| Cl | Sulfuric Acid | H2SO4 • nH2O(l) | 221-296 | 2 x 10-4 | 10 | 34 |
| Cl2 + HBr(s) BrCl + HCl |  |  |  |  |  |  |
| Cl2 | Water Ice • HBr(s) | H2O(s) | 200 | >0.2 |  | 35 |
| Cl2 + KBr(s) BrCl + KCl(s) |  |  |  |  |  |  |
| Cl2 | Potassium Bromide | KBr(s) | ~295 | >0.1 |  | 36 |
| Cl2 + NaX (aq) ClX + NaCl (aq) |  |  |  |  |  |  |
| Cl2 | Aqueous Sodium Bromide Aqueous Sodium Iodine | NaBr(aq) NaI(aq) | See Note See Note |  |  | 37 37 |

Table 64.  Continued

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| ClO + Surface Products |  |  |  |  |  |  |
| ClO | Water Ice Nitric Acid Ice Sulfuric Acid | H2O(s) HNO3 • 3H2O(s) H2SO4 • nH2O(l) (60 to 95 wt.% H2SO4) | 190 183 221-296 | See Note See Note See Note |  | 38 38 39 |
| HOCl + HCl(s) Cl2 + H2O |  |  |  |  |  |  |
| HOCl | Water Ice Nitric Acid Ice Sulfuric Acid | H2O(s) • HCl(s) HNO3•3H2O(s)•HCl(s) H2SO4•nH2O(l) | 195-200 195-200 198-209 | 0.3 0.1 See Note | 3 3 | 40 40 41 |
| ClNO + NaCl(s) Products |  |  |  |  |  |  |
| ClNO | Sodium Chloride | NaCl(s) | 298 | >1 x 10-5 |  | 42 |
| ClNO2 + NaCl(s) Products |  |  |  |  |  |  |
| ClNO2 | Sodium Chloride | NaCl(s) | 298 | <1 x 10-5 |  | 42 |
| ClONO2 + H2O(s) HOCl + HNO3 |  |  |  |  |  |  |
| ClNO2 | Water Ice Nitric Acid Ice Sulfuric Acid Sulfuric Acid Monodydrate Sulfuric Acid Tetrahydrate | H2O(s) HNO3 • 3H2O(s) H2SO4 • nH2O(l) H2SO4 • H2O(s) H2SO4 • 4H2O(s) | 180-200 200-202 200-265 195 196-206 | 0.3 0.001* See Note <1 x 10-3 See Note | 3 10 | 43 44 45 46 46 |
| ClONO2 + HCl(s) Cl2 + HNO3 |  |  |  |  |  |  |
| ClONO2 | Water Ice Nitric Acid Ice Sulfuric Acid Sulfuric Acid Monodydrate Sulfuric Acid Tetrahydrate Alumina | H2O(s) HNO3•3H2O•HCl H2SO4•nH2O(l)•HCl(l) H2SO4•H2O(s) H2SO4 • 4H2O(s) Al2O3 | 180-202 200-202 195 195-206 180-200 | 0.3 0.1 See Note <1 x 10-4 See Note 0.3 | 5 3 3 | 47 48 49 50 50 51 |
| ClONO2 + MX(s) XCl + MNO3 |  |  |  |  |  |  |
| ClONO2 | Sodium Chloride Potassium Bromide Sodium Bromide | NaCl(s) KBr(s) NaBr(s) | 200-300 ~295 ~295 | 5 x 10-2 5 x 10-2 See Note | 10 10 | 52 52 52 |

Table 64.  Continued

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| ClONO2 + HBr(s) BrCl + HNO3 |  |  |  |  |  |  |
| ClONO2 | Water Ice Nitric Acid Ice | H2O(s) • HBr(s) HNO3•3H2O(s)•HBr(s) | 200 200 | >0.3 >0.3 |  | 53 53 |
| ClONO2 + HF(s) Products |  |  |  |  |  |  |
| ClONO2 | Water Ice Nitric Acid Ice | H2O(s) • HF(s) H2O(s)•HNO3(s)•HF(s) | 200 200 | See Note See Note |  | 54 54 |
| CFxCly + Al2O3(s)  Products |  |  |  |  |  |  |
| CCl4 CFCl3 CF2Cl2 CF3Cl | Alumina Alumina Alumina Alumina | Al2O3(s) Al2O3(s) Al2O3(s) Al2O3(s) | 120-300 120-300 120-300 120-300 | 1 x 10-5 1 x 10-5 1 x 10-5 1 x 10-5 | 10 10 10 10 | 55 55 55 55 |
| BrCl + KBr(s)  Br2 + KCl(s) |  |  |  |  |  |  |
| BrCl | Potassium Bromide | KBr(s) | ~295 | >0.1 |  | 36 |
| Br2 + Nal(aq)  Brl + NaBr(aq) |  |  |  |  |  |  |
| Br2 | Aqueous Sodium Iodine | Nal(aq) | See Note |  |  | 37 |
| 2BrO  Br2 + O2 |  |  |  |  |  |  |
| BrO | Water Ice Sulfuric Acid Aqueous Sodium Chloride | H2O(s) H2SO4 • nH2O (60 wt% H2SO4) (70 wt % H2SO4) NaCl(aq) (23 wt% NaCl) | 213 213 213 253 | See Note See Note See Note See Note |  | 56 56 56 56 |
| HOBr + HCl(s)  BrCl + H2O |  |  |  |  |  |  |
| HOBr | Water Ice Sulfuric Acid | H2O(s) • HBr(s) H2SO4 • nH2O (60-69 wt% H2SO4) | 228 228 | 0.3 0.2 | 3 3 | 57 57 |
| HOBr + HBr(s)  Br2 + H2O |  |  |  |  |  |  |
| HOBr | Water Ice Sulfuric Acid | H2O(s) • HBr(s) H2SO4 • nH2O | 228 228 | 0.1 See Note | 3 | 58 58 |

Table 64.  Continued

| Gaseous Species | Surface Type | Surface Composition | T(K) |  | Uncertainty Factor | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| BrONO2 + H2O  HOBr + HNO3 |  |  |  |  |  |  |
| BrONO2 | Water Ice Sulfuric Acid | H2O(s) H2SO4 • nH2O | 200 210-298 | >0.3 0.8 | 2 | 59 60 |
| BrONO2 + HCl  BrCl + HNO3 |  |  |  |  |  |  |
| BrONO2/HCl | Water Ice Sulfuric Acid | H2O(s) H2SO4 • nH2O | 200 229 | See Note 0.9 | 2 | 59 60 |
| CF2Br2 + Al2O3(s)  Products |  |  |  |  |  |  |
| CF2Br2 | Alumina | Al2O3 | 210, 315 | 2 x 10-5 | 10 | 55 |
| CF3OH + H2O  Products |  |  |  |  |  |  |
| CF3OH | Water Ice Sulfuric Acid | H2O(l) H2SO4 • nH2O (40 wt% H2SO4) (45 wt% H2SO4) (50 wt% H2SO4) (50 wt% H2SO4) | 274 210-250 210-250 210-250 210-250 | >0.01 0.07 0.04 0.01 0.001 | 3 3 3 3 | 61 61 61 61 61 |

* is temperature dependent

#### Notes to Table 64

1.	O3 + Al2O3(s) and NaCl(s) - Very low ozone decomposition efficiencies for reaction on coarse (3 µm dia.) and fine (0.1 µm dia., partially hydroxylated) -alumina and course (3 µm dia.) -alumina were measured in flowing and static systems by Hanning-Lee et al.[57] at temperatures ranging between 212 and 473 K.  Based on measured BET surface areas, s ranged from 2 x 10-11 to 4 x 10-10 over the 212 to 298 K temperature range.  s for -alumina at lower temperatures exceeded those for -alumina.  Results are roughly consistent with earlier, unpublished flow tube data from L.F. Keyser and from fluidized bed reactor studies of Alebic'-Juretic' et al. [7].  Note that s based on geometic surface particle surface areas would be significantly (104 - 107) larger.  Alebic'-Juretic' et al.  also studied ozone decomposition on small (<180 µm) NaCl crystals in their fluidized bed reactor and observed no effect, indicating  for O3 decomposition on NaCl(s) is much smaller than that for -alumina.

2.	O3 + C(s) - Fendel et al. [38] expand on earlier work reported by Fendel and Ott [39] showing large uptake coefficients for O3 on small C(s) particles (<10 - 100 nm) formed from C(g) and added to an atmospheric pressure flow containing O3.  A  of 3.3 x 10-3 was measured for the lowest O3 concentration (160 ppbv) studied. Smaller values, ranging down to ~2 x 10-4, were measured for higher O3 concentrations.  Rogaski et al. [142] used initial Knudsen cell uptake measurements to yield  = 1 (±0.5) x 10-3 for amorphous carbon at room temperature.  Smith et al. [152] report that the ozone/soot reaction is first order in ozone, with CO, CO2, and H2O the only stable gaseous products.  Stephens et al. [153] measured CO, CO2, and O2 as products, with an O2 produced for each O3 reacted; they measured uptake coefficients which varied from 10-3 to 10-5 depending on carbon sample and O3 exposure.  The O3/C(s) reaction probability is clearly dependent on the C(s) surface history.

3.	OH + H2O(s) - Cooper and Abbatt [27] measured initial irreversible OH uptake coefficients of ~ 0.1 for water ice between 205 - 230 K; these decayed to  = 0.03 ±0.02 after repeated exposure to OH.  Self reaction to form H2O or H2O2 was indicated by the lack of observable gas phase products despite observation of first order OH loss.

4.	OH + HCl • nH2O(l) - Cooper and Abbatt [27] demonstrated significant enhancement of OH uptake (to  > 0.2) after HCl doping of 220 K ice surfaces sufficient to melt the surface layer.  It is unclear whether OH is lost to self-reaction or reaction with hydrated Cl- ions.

5.	OH + HNO3 • 3H2O - Cooper and Abbatt [27] measured  > 0.2 for nitric acid doped ice surfaces under conditions suitable for NAT formation at 200 and 228 K.  Increase over pure ice uptake rates is probably due to HNO3 + OH H2O + NO3 reaction.

6.	OH + H2SO4 • nH2O - Lower limits of 0.2 for uptake coefficients on 45-65 wt %  H2SO4 between 220 and 230 K and for 96 wt % H2SO4 at 230 and 298 K by Cooper and Abbatt [27] are consistent with a lower limit of 0.07 on 28 wt % H2SO4 at 275 K in similar experiments by Hanson et al. [60] and a probable surface saturated value of (4.9 ±0.5) x 10-4 from Knudsen cell measurements by Baldwin and Golden [9] and an estimate of  = 1 on ~96 wt % H2SO4 at 298 K by Gerhenzon et al. [50] using a coated insert flow tube technique.  Uptake is probably reactive with OH + HSO4-   H2O + SO4- the hypothesized process.

7.	OH + NaCl(s) - Ivanov et al. [84] used a fast flow reactor with a central salt coated rod to measure heterogeneous loss of OH between 245 and 339 K.  Their fit for NaCl(s) yielded  = (1.2 ±0.7) x 10-5 exp[(1750 ±200)/T].  Similar data for NH4NO3 yielded  - (1.4 ±0.5) x 10-4 exp [(1000 ±100)].  Since uptake was irreversible, it is assumed that the loss was self-reaction.

8.	HO2 on H2O(s) and H2SO4 • nH2O(l) - Uptake of HO2 on ice and super-cooled 55 wt % sulfuric acid at 223 K has been demonstrated to be limited by HO2 surface saturation by Cooper and Abbatt [27].  They argue that self-reaction, presumably 2HO2   H2O2 + O2 is limiting measured uptake coefficients of 0.025 ±0.005 for ice and 0.055 ±0.020 for 55 wt % H2SO4.  However, Gersherzon et al. [52] measured  > 0.2 for 80 and 96 wt % H2SO4 at 243 K and Hanson et al. [60] measured a lower limit for 28 wt % H2SO4 at 275 K of 0.07.  However, large gas phase diffusion corrections mean this value is consistent with  = 1.

9.	NO2 + H2O(1) - Value for  of (6.3 ± 0.7) x 10-4 at 273 K (Tang and Lee, [157]) was achieved by chemical consumption of NO2 by SO3=; their stopped-flow measurement was probably still affected by surface saturation, leading to the measurement of a lower limit.  Ponche et al. [132] measured an uptake coefficient of 1.5 (±0.6) x 10-3 at 298 K, which was also probably subject to saturation limitations.  Mertes and Wahner[115] used a liquid jet technique to measure a lower limit of  ≥ 2 x 10-4 at 278 K, and they observed partial conversion of the absorbed NO2 to HONO.  Msibi et al. [127] used a cylindrical/annular flow reactor to derive g = (8.7 ±0.6) x 10-5 on pH = 7 deionized  water surfaces and (4.2 ± 0.9) x 10-4 on  pH = 9.3 wet ascorbate surfaces; it seems likely that these results are also subject to surface saturation given the gas/surface interaction times involved in the  experiment.  Data are consistent with an  ≥ 1 x 10-3 for 278 - 298 K and a liquid phase second-order hydrolysis of NO2 to HONO and HNO3 which depends on temperature and pH.  However, the interplay between accommodation, possible surface reaction, and bulk reaction may be complex.

10.	NO2 +  H2SO4•nH2O - Saastad et al. [148] measured a lower limit of 5 x 10-5 for an uptake coefficient on 70 wt % H2SO4 between 193 and 243 K.  Baldwin and Golden [8] measured an uptake coefficient limit of <1.0 x 10-6 on 96 wt. % H2SO4.  See Note 15 for H2O2 on H2SO4 • nH2O.  Both measurements were probably limited by surface saturation.

11.	NO2 + C(S) - Tabor et al. [156] extended their previously published study (Tabor et al. [155]) to three types of amorphous carbon particles exposed to NO2 in a low pressure Knudsen cell reactor.  All three types of C(s) particles were reported to show initial  values of (5.1 ±1.7), (8.3 ±2.7), and (5.7 ±1.3) x  10- 2, compared with (4.8 ± 0.6) x 10- 2 reported in Tabor et al., all assuming a geometrical surface area for the bulk C(s) powder.  NO was observed as a product from all samples, and some samples evolved CO, CO2, and a mass spectrometric peak consistent with NO3 or N2O5 upon thermal desorption.  The amount of NO evolved varied widely with the type of C(s) particle.  Co-deposition of H2O vapor had no major effect on NO2 uptake.  On the other hand, room temperature Knudsen cell studies of amorphous carbon by Rogaski et al. report an initial  of 0.11 ±0.04, although  for longer times agrees reasonably well with Tabor et al.[156].  However, 13NO2 uptake studies with suspended small aerosol particles of graphitic or amorphous carbon by Kalberer et al. [90] measured uptake  coefficients  between (0.3 ±0.19) x 10-4 and (4.0 ±1.0) x 10-4.  NO was determined to be the principal gaseous product observed in these studies, and first-order absorbed NO2 reaction rates of (4 to 9) x  10-4 s-1 were obtained.  The large discrepancy between these measured uptake rates may be due to the difficulty of properly specifying the reactive surface area for bulk powders and the time-dependent nature of reactive uptake.

12.	NO2 + NaCl(s), NaBr(s) - Vogt and Finlayson-Pitts [170, 172] used diffuse reflectance infrared spectroscopy to study the reaction of NO2 with NaCl(s) at 298 K, and Vogt et al.[169] used the same technique to study NO2 + NaBr(s) at 298 K.  Both reactions were shown to be approximately second order in NO2.  Assuming that adsorbed N2O4 is the reactant leads to  = (1.3 ±0.6) x 10-4 for NaCl(s) and 2 (+4, -1.3) x 10-4 for NaBr(s).  Peters and Ewing [131] measured reactive uptake for single-crystal NaCl(100) surfaces and observed both NO3-(c) and ClNO products.  The value of N2O4) measured by Peters and Ewing at 298 K was only (1.3 ±0.3) x 10-6.  They noted that small amounts of water vapor (9.5 mbar) cause  to increase by two orders of magnitude.

13.	NO3 + H2O(l) - Rudich et al. [145, 146] used wetted-wall flow tube techniques to measure uptake coefficients for NO3 on pure water and aqueous NaCl, NaBr, NaI, and NaNO2 solutions.  These studies were extended to other aqueous solutions by Imamura et al.[82].  Uptake on pure water was consistent with reaction of NO3 to produce HNO3 and OH.  Uptake coefficients with solutions containing I- , Cl- , Br - , NO2-  and other anions were larger and scaled with anion concentration, indicating electon transfer reactions to produce NO3- .  The  of (2.0 ±1.0 x 10- 4) at 273 K determined for pure water by Rudich et al. is significantly lower than the lower limit of 2.5 x 10-3 quoted by Mihelcic et al. [119].  A detailed analysis of uptake coefficients for KI aqueous solutions indicated that the NO3 mass accommodation coefficient is >0.04[146].

14. 	N2O5 + H2O(s) - Leu [103] and Hanson and Ravishankara [63] have measured nearly identical values of 0.28 (±0.11) and 0.24 (±30%) near 200 K.  Hanson and Ravishankara [68] presented new and re-analyzed data as a function of ice thickness, with a value of ~0.008 for the thinnest ice sample, rising to ~0.022 for the thickest.  Quinlan et al. [134] have measured a lower limit for  on fresh ice surfaces of 0.03 at 188 K.

15. 	N2O5 + H2O(l) - Reaction on liquid water has a negative temperature dependence.  Van Doren et al. [166] measured ’s of 0.057 ±0.003 at 271 K and 0.036 ±0.004 at 282 K.  Mozurkewich and Calvert [124] studied  on NH3/H2SO4/H2O aerosols.  For their most water-rich aerosols (RH = 76%) they measured s of 0.10 ±0.02 at 274 and 0.039 ±0.012 at 293 K.  George et al. [48] use droplet train/ion chromotography techniques to measure s of (3.0 ±0.2) x 10- 2 (262 K), (2.9 ±1.2) x 10-2 (267 K), 2.0 ±0.2) x 10-2 (273 K), (1.6 ±0.8) x 10-2 (276 K), and (1.3 ±0.8) x 10-2 (277 K).  Msibi et al.[126]] measured a smaller  of 2.5 x 10-3 for water adsorbed on a denuder flow tube well under 66-96% relative humidity conditions at room temperature.

16. 	N2O5 + HNO3 • 3H2O(s) - Hanson and Ravishankara [63] have measured  = 0.0006 (±30%) at 200 K.  They presented re-analyzed and additional data as a function of ice thickness (Hanson and Ravishankara [68]), deriving a value of 3 x 10-4 for the thinnest NAT covered ice layer, with values up to three times higher for thicker NAT-covered ice layers.  This is in very poor agreement with  = 0.015 (±0.006) reported by Quinlan et al. [134].  This latter measurement may have been biased by a super-cooled nitric acid surface rather than NAT.

17.	N2O5 + H2SO4 • nH2O(l) - This reaction has been intensively studied between 195 and 296 K for a wide range of H2SO4 wt % values using four complementary experimental techniques.  Data are available from aerosol flow tube studies (Fried et al. [45], Hanson and Lovejoy [61], and Lovejoy and Hanson [108]), coated wall flow tube studies (Hanson and Ravishankara [66], Zhang et al. [186]), stirred Knudsen cell studies (Williams et al. [178], Manion et al. [111]) and droplet train studies (Van Doren et al. [166], Robinson et al. [141]).  All studies have yielded s between ~0.05 and 0.20 with modest dependence on surface H2SO4 wt % and temperature.  Aerosol flow tube studies at higher N2O5 exposure and the ternary H2SO4/HNO3/H2O studies of Zhang et al. both illustrate that significant levels of HNO3 in the H2SO4/H2O solutions will reduce  measurably; this fact explains some of the scatter in aerosol flow tube studies [45, 61, 108].  The effect of 5.0 x 10-7 torr HNO3 for  (N2O5) as a function of temperature at two water vapor concentrations are plotted in Zhang et al.; the decrease in  is greatest at low temperatures, approaching a factor of 2-5 between 200 and 195 K.

Robinson et al. have binned the data believed to be free of suspected HNO3 dilution and surface saturation effects from the studies cited above into groups with similar H2SO4 concentration, and they have fit a temperature-dependent uptake model, taking into account temperature and composition dependence of the effective Henry's Law constant, liquid phase diffusion coefficient, and the liquid phase hydrolysis rate constant.  The hydrolysis reaction was treated by modeling two reaction channels, a direct hydrolysis process dominating reaction at low H2SO4 concentrations with a reaction rate proportional to water activity, and a proton-catalyzed reaction with a rate proportional to H+ activity, which dominates at higher acid concentrations.  A parameterized fit for 30 to 80 wt % H2SO4 to the uptake model gives

 = k0 + k1/T + k2/T,  where ki = ∑ aij (wt% H2SO4)j, j = 0 to 3

i = 0, j:  	-11.548 	 0.65252 	-0.013183 	 0.000081293

i = 1, j:		 5521.6 	-316.68 	 6.4268 	-0.039527

i = 2, j:		-587410 	 34601 		-712.3 		 4.3833

18.	N2O5 + H2SO4 • H2O(s) - Zhang et al. [185] used coated flow tube techniques to measure the uptake of N2O5 on solid sulfuric acid monohydrate over a temperature range of 200 to 225 K.  The measurement values of  were significantly higher at 200 K ( ~ 1 x 10-3) than at 225 K ( ~10-4) and were well fit by log  = [4.78 - 0.0386 T(K)].  Acid rich H2SO4 • H2O surfaces had a lower  than water rich surfaces (log  = 0.162 - 0.789 x log H2O] where H2O is their experimental water vapor partial pressure.

19.	N2O5 on H2SO4 • 4H2O(s) - Hanson and Ravishankara [71] studied N2O5 uptake by frozen 57.5 and  60 wt % H2SO4 as a function of temperature and relative humidity.  The 57.5 wt % surface was not sensitive to relative humidity and was slightly more reactive ( = 0.008 vs 0.005) at 205 K than at 195 K.  Reaction probabilities on the 60 wt % surface dropped off with temperature and relative humidity.

20. 	N2O5 + HCl on H2O(s) - Leu [103] measured  = 0.028 (±0.011) at 195 K, while Tolbert et al. [162] measured a lower limit of 1 x 10-3 at 185 K.  These experiments were done at high HCl levels probably leading to a liquid water/acid surface solution (Abbatt et al. [4]).  The reaction probability may be much smaller on HCl/H2O ice surfaces characteristic of the stratosphere.

21.	N2O5 + HCl on HNO3 • 3H2O(s) - Hanson and Ravishankara [63] measured  = 0.0032 (±30%) near 200 K.

22.	N2O5 + HCl on H2SO4 • H2O(s) - Zhang et al. [185] saw no increase in N2O5 uptake on sulfuric acid monohydrate at 195 K upon exposure to HCl, setting  < 10-4.

23.	N2O5 + NaCl (s,aq) - Using FTIR analysis, Livingston and Finlayson-Pitts [107] have demonstrated that N2O5 reacts with crystalline NaCl to form NaNO3(s),  and they report   > 2.5 x 10-3 at 298 K.  However, Leu et al.[102] used flow tube/mass spectrometric  techniques to obtain  < 1 x 10-4 for dry salt at 223 and 296 K; they also noted that exposing salt surfaces to small amounts of H2O vapor increased significantly.  Fenter et al.[41] measured  = (5.0 ±0.2) x 10-4 on fused salt surfaces at room temperature, assuming the geometrical surface area is the only surface accessed.  Msibi et al. [126] measured NO3-  deposition on an annular flow reactor to determine  = 1 x 10-3 for salt surfaces between 45 and 96% relative humidity at room temperature, rising to  = 1.5 x 10-2 at 96/97% relative humidity, but they argue that most of the uptake is due to reaction with H2O.  On aqeous NaCl solutions, Zetzsch, Behnke, and co-workers [11, 12, 182] have studied the reaction of N2O5 with aqueous NaCl aerosols in an aerosol chamber.  The relative yields of ClNO2 and HNO3 rise with the NaCl concentration.  A reaction probability of ~0.03 is measured with a 50% ClNO2 yield at the deliquescence point (Zetsch and Behnke).  This picture is confirmed by droplet uptake studies on 1 M NaCl solutions reported by George et al. [48] which confirm that uptake on salt solutions in the 263 - 278 K temperature range is larger than that on pure water droplets.

24.	N2O5 + HBr on HNO3 • 3H2O(s) - This reaction, yielding  ~0.005, was investigated on NAT surfaces near 200 K by Hanson and Ravishankara [67]. Under some conditions a much higher reaction coefficient of ~0.04 was observed.

25.	N2O5 + MBr - Finlayson-Pitts et al. [43] used FTIR techniques to demonstrate that BrNO2(ads) is a major product of the N2O5(g) + NaBr(s) reaction.  However, Fenter et al. [41] failed to measure gas phase evolution of BrNO2 using Knudsen cell/mass spectrometry techniques, detecting Br2(g) instead.  They propose that BrNO2 reacts with KBr(s) to yield KNO2(s) + Br2(g).  A  of (4.0 ±2.0) x 10-3 at room temperature was determined for fused KBr surfaces with well-defined surface areas.

26.	HONO + H2O(l) - Bongartz et al. [15] present uptake measurements by two independent techniques, the liquid jet technique of Schurath and co-workers and the droplet train/flow tube technique of Mirabel and co-workers (Ponche et al. [132]).  With a surface temperature of ~245 K the droplet train techniques yielded 0.045<<0.09, while the liquid jet operating with a surface temperature of 297 K obtained 0.03<< 0.15.  Mertes and Wahner used a liquid jet technique to measure 4 x 10- 3 <  < 4 x 10-2 at 278 K.  Since HONO uptake by liquid water probably involved hydrolysis, an increase in Henry's law solubility with decreasing temperature may be offset by a decreasing hydrolysis rate constant, leaving the uptake coefficient's temperature trend uncertain.  Measured uptake coefficients will not correspond to the mass accommodation coefficient.

27.	HONO + H2SO4 • nH2O(l) - Zhang et al.[187] measured uptake coefficients for HONO on sulfuric acid that increased from (1.6 ±0.1) x 10-2 for 65.3 wt % H2SO4 (214 K) to (9.1 ±1.6) x 10-2 for 73 wt % H2SO4 (226 K).  Fenter and Rossi[42] measured uptake coefficients rising from 1.8 x 10-4 for 55 wt % H2SO4 (220 K) to 3.1 x 10-1 for 95 wt % H2SO4 (220 K and 273 K).  In general, the values measured by Zhang et al. are a factor of 2 to 5 higher than those of Fenter et al. for comparable acid concentrations.  Since the reaction probably depends on both temperature and acid concentration and since the data scatter is high in both experiments, further independent data will be required to define  as a function of acid concentration and temperature.  These data are generally consistent with the effective Henry's law constant  measurements of Becker et al. [10] who illustrate that HONO solubility decreases exponentially with H2SO4 concentration until ~53 wt %, at which point reaction to form nitrosyl sulfuric acid increases H* dramatically as H2SO4 concentration increases.

28.	HONO + HCl + H2O(s) - Knudsen cell uptake studies for HONO/HCl co-deposited on ice (180-200 K) and for HONO on 0.1 to 10 m HCl frozen solutions (~190 K) by Fenter and Rossi showed HONO uptake coefficients in the 0.02 to 0.12 range as long as surface HCl concentrations significantly exceed HONO concentrations.  ClNO was evolved quantitatively with HONO consumption.

29.	HONO + NaCl(s) - Diffuse reflectance experiments by Vogt and Finlayson-Pitt [171] on room temperature NaCl(s) and Knudsen cell uptake experiments by Fenter and Rossi on room temperature NaCl(s) and frozen 0.1 M NaCl aqueous solutions, all failed to show HONO uptake.  The latter results yield  < 1 x 10-4.

30.	HNO3 + C(s) - Knudsen cell/mass spectrometry measurements by Rogaski et al. yielded  = 3.8 (±0.8) x 10-2 on one type of amorphous carbon over a temperature range of 190-440 K.  Gas phase NO and NO2 equivalent to ~2/3 of the HNO3 uptake were observed as reaction products.

31.	HNO3 + NaX(s)/KX(s) - Vogt and Finlayson - Pitts [170, 172] used diffuse infrared reflectance spectroscopy to characterize the process.  There was absorption of HNO3, but no reaction was observed on completely dry NaCl(s); however, NaNO3 forms in the presence of very low (well below the deliquescence point) levels of H2O(g).  Using XPS spectroscopy to identify surface products and a dry HNO3 source, Laux et al. [101] (also see Vogt et al.) measured  = (4 ±2) x 10-4 at 298K.  Fenter et al. [40] measured the room temperature uptake of HNO3 on solid powders of NaCl, NaBr, KCl, KBr, and NaNO3, using Knudsen cell/mass spectrometry techniques.  They saw similar uptake for all surfaces, including unreactive NaNO3, and recommend   = (2.8 ±0.3) x 10-2 for all salts.  HCl or HBr was produced with ~100% yield from the halide surfaces.  There is some concern about the effective surface area of the powders used by Fenter et al. (see Leu et al.[102]).  Fenter et al. report new HNO3 data to support their argument that "sticky" gases such as HNO3 cannot penetrate below the top surface layer of the powders used in their experiments.  Leu et al. used flow tube/mass spectrometry techniques to measure   = (1.3 ±0.4) x 10-2 at 296 K and  > 8 x 10-3 at 223 K, both in the presence of low levels of H2O(g).  They determined that uptake at 296 K was reactive, producing HCl but that at 223 K reaction  was suppressed and uptake was largely absorptive.  Beichert and Finlayson-Pitts [13] measured  = (1.4 ±0.6) x 10-2 at 298 K with a Knudsen cell technique, and, using D2O, demonstrated that chemisorbed water, presumably retained on defect sites, was crucial for NaNO3 formation.  This suggests that low levels of defect-retained water are responsible for the small uptake values measured by Laux et al.

32.	NH3 + H2SO4 • nH2O - Robbins and Cadle [137], Huntzicker et al. [80], McMurry et al. [114], and Daumer et al. [30] all studied NH3 uptake by sulfuric acid aerosols in near room temperature flow reactors (T = 281 - 300 K).  Uptake coefficients varied between 0.1 and 0.5.  Rubel and Gentry [144] used levitated H3PO4 acid droplets to show that heterogeneous reaction does control the initial NH3 uptake on strong acid solutions.  Both Rubel and Gentry and Däumer et al. also explored the effect of organic surface coatings.

33	CH3 C(O)O2 + H2O(l) and H2SO4 • nH2O - Villalta et al. [168] used wetted-wall flow tube techniques to measure  = 4.3 (+ 2.4 /-1.5) x 10-3 for water at 274 ± 3K.  They also measured uptake for 34 wt % H2SO4 at 246 K ( = (2.7 ±1.5) x 10-3),  51 wt % at 273 K ( = (0.9 ±0.5) x 10-3), and 71 wt % at 298 K ( = (1.4 ±0.7) x 10-3).  They suggest that products subsequent to hydrolysis are HO2 and CH3C(O)OH.

34. 	Cl + H2SO4 • nH2O - Measured reaction probability (Martin et al. [113]) varies between 3 x 10-5 and 7 x 10-4 as H2O and T co-vary.  Reaction product is claimed to be HCl.

35.	Cl2+HBr + H2O(s) - Hanson and Ravishankara [67] measured a reaction probability of >0.2 on water ice near 200 K.  BrCl was not detected, presumably due to rapid reaction with excess HBr.

36.	Cl2 and BrCl + KBr(s) - Caloz et al. measured  > 0.1 for reactive uptake of Cl2 and BrCl on KBr(s) in a room temperature Knudsen cell experiment.

37.	Cl2 and Br2 + NaBr(aq) and NaI(aq) - Hu et al.,[78] measured large uptake coefficients for Cl2 on dilute aqueous droplets of NaBr and NaI solutions and Br2 on NaI solutions using a droplet train technique.  Reaction was demonstrated to proceed through both a chemisorbed surface complex and normal bulk solution second-order kinetics.  Second-order bulk reaction rate constants near the diffusion limit and consistent with bulk-phase kinetic measurements were obtained between 263 and 293 K.

38. 	ClO + H2O(s) and  HNO3 • nH2O  - Proposed reaction (Leu [103]) is 2 ClO  Cl2 + O2; reactive uptake may depend on ClO surface coverage, which in turn may depend on gas phase ClO concentrations.  Kenner et al. [93] measured reaction probabilities of (8 ±2) x 10-5 for ice at 183 K which is far lower than  the limit of >1 x 10-3 obtained by Leu et al. [103].  Abbatt [3], using nearly the same low levels of ClO as Kenner et al., obtained  < 1 x 10-5 at 213 K.  The difference  may lie in the level of ClO or other adsorbable reactive species present.  The lower value of Abbatt is probably closer to the expected reactivity under stratospheric conditions.  Kenner et al. also measured a reaction probability limit of < (8 ±4) x  10-5 for NAT at 183 K.

39.	ClO + H2SO4 • nH2O - Measured reaction probability (Martin et al. [113]) varies between 2 x 10-5 and 2 x 10-4 as H2O content is varied by changing wall temperature.  Reaction product is claimed to be HCl, not Cl2.  Abbatt[3] measured  < 1 x 10-5 for 60 and 70 wt % H2SO4 at 213 K.

40. 	HOCl + HCl + H2O(s) and HNO3 • 3H2O(s) - Hanson and Ravishankara [66] and Abbatt and Molina [5] have investigated the HOCl + HCl reaction on water ice and NAT-like surfaces, and Chu et al. [24] studied water ice.  Product yield measurements support the identification of Cl2 and H2O as the sole products.  The high reaction probabilities measured indicate that this reaction may play a significant role in release of reactive chlorine from the HCl reservoir.  The reaction probability on NAT-like surfaces falls off dramatically (a factor of 10) on water-poor (HNO3-rich) surfaces (Abbatt and Molina).  The measured yield of product Cl2 is 0.87 ±0.20 (Abbatt and Molina [5]).

41.	HOCl + HCl + H2SO4 • nH2O - This process has been studied in coated flow tubes near 200 K by Zhang et al. [184] and Hanson and Ravishankara [70].  Both studies measured large s for [HCl] > [HOCl].  Hanson and Ravishankara [70] deduced a second-order reaction rate constant of ~1 x 105 M-1 s-1 in 59.6 wt % H2SO4 at 201-205 K.  A model of this and related sulfuric acid aerosol reactions tailored to stratospheric conditions has been published by Hanson et al. [74].  Zhang et al. held the water vapor partial pressure at 3.8 x 10-4 torr and showed  increased by a factor of 50 as the temperature was lowered from 209 to 198 K, showing that the reaction rate is strongly dependent on water activity.

42.	ClNO and ClNO2 + NaCl(s) - Using a Knudsen cell technique Beichart and Finlayson-Pitts set upper limits of  < ~10-5 for reaction uptake of ClNO and ClNO2 on NaCl(s) powders at 298 K.

43. 	ClONO2 +  H2O(s) - Measurement of  = 0.3 (+0.7, -0.1) (Hanson and Ravishankara [65]) significantly exceeds previous measurements of Molina et al. [121], Tolbert et al. [163], Leu [104] and Moore et al. [123] and subsequent measurements by Chu et al. [24] and Zhang et al. [183].  Previous measurements were probably impeded by NAT formation on surface (Hanson and Ravishankara, [66], Chu et al.).  Lower levels of ClONO2(g) used by Hanson and Ravishankara [63] minimized this surface saturation problem.  Also, using lower ClONO2 concentrations, Zhang et al.  obtained a reaction probability of 0.08 ± 0.02 at 195 K, in fair agreement with the range of 0.03 to 0.13 measured by Chu et al.  More recent Knudsen cell measurements at 180 and 200 K by Oppliger et al.,[130] showed initial uptake gs in the 0.2 to 0.4 range.  Reaction products are HNO3 and HOCl.  All of the HNO3 and much of the HOCl is retained on the surface under polar stratospheric conditions (Hanson and Ravishankara).  Hanson [59] deposited ClONO2 on H218O enriched ice and detected H18OCl showing the Cl-ONO2 bond is broken during reaction on ice at 191 K.

44. 	ClONO2 + HNO3 • nH2O - Hanson and Ravishankara [63, 65] report a value of 0.006 for ClONO2 reaction with the water on NAT (HNO3 • 3H2O).  However, these authors present re-analyzed and new data with   0.001 in Hanson and Ravishankara [68].  Similar experiments (Moore et al. [123], Leu et al. [105]) report a larger value 0.02 ±0.01 which falls very rapidly as slight excesses of H2O above the 3/1 H2O/HNO3 ratio for NAT are removed.  They measure  of less than 10-6 for slightly water poor “NAT” surfaces.  The inconsistency between Hanson and Ravishankara [63, 65] and the JPL group (Moore et al. [123]; Leu et al., [105]) has not been resolved.  Hanson and Ravishankara [66] report that  for this reaction increases by a factor of 4 as the surface temperature increases from 191 to 211 K.

45. 	ClONO2 + H2SO4 • nH2O(l) - Results from wetted-wall flow tube (Hanson and Ravishankara, [72]) Knudsen cell reactor (Manion et al. [111], Williams et al., [178], aerosol flow tube (Hanson and Lovejoy  [141]), and droplet train uptake experiments (Robinson et al., 96/63) supplement older wetted-wall flow tube (Hanson and Ravishankara [66]) and Knudsen cell measurements (Rossi et al. [143], Tolbert et al. [161]).  Although earlier Knudsen cell measurements probably suffered from surface saturation, more recent results compare well with those from other techniques.  Results are now available over a temperature range of 200-265 K and a H2SO4 concentration range of 39 to 75 wt.%.  Measured  values depend strongly on H2SO4 concentration and vary modestly with temperature, with a trend to somewhat higher values for the 210 - 220 temperature range, reflecting the temperature dependence of Hkhyd1/2 and the liquid phase diffusion coefficient for ClONO2 and the rates of the direct- and proton-catalyzed hydrolysis reactions, which are proportional to the activity of H2O and the activity of H+, respectively.  (Robinson et al., [141]).

Robinson et al. have binned the data believed to be free of suspected HNO3 dilution and surface saturation effects from the studies cited above into groups with similar H2SO4 concentration and they have fit a temperature-dependent uptake model, taking into account temperature and composition dependence of the effective Henry's Law constant, liquid phase diffusion coefficient, and the liquid phase hydrolysis rate constant.  The hydrolysis reaction was treated by modeling two reaction channels, a direct hydrolysis process dominating reaction at low H2SO4 concentrations with a reaction rate proportional to water activity, and a proton-catalyzed reaction with a rate proportional to H+ activity, which dominates at higher acid concentrations.  A parameterized fit to the uptake for 30-80 wt % H2SO4 model gives:

 = k0 + k1/T + k2/T,  where ki = ∑ aij (wt% H2SO4)j, j = 0 to 3

i = 0, j:  	-10.855		-0.12764	 0.0087648	-0.00010047

i = 1, j:		 4349.6		 44.544		-3.8043		 0.043465

i = 2, j:		-454140	-3061.2		 376.53		-4.7098

46.	ClONO2 + H2SO4 • H2O(s) and H2SO4 • 4H2O(s) - Measurements by Hanson and Ravishankara [71] and Zhang et al. [183] demonstrate that the reaction probability on the tetrahydrate is a strong function of both temperature and relative humidity, both of which affect the level of adsorbed H2O.  Both groups covered the temperature range of 192-205 K.  The reaction is slowest at higher temperatures and lower relative humidities. Zhang et al. [183] have parameterized their data in the form of log  = a1 + a2 log x + a3 log2 x; for 195 K and x = water partial pressure in torr:  a1 = 10.12, a2 = 5.75 and a3 = 0.62; for a water partial pressure of 3.4 x 10-4 torr and x = T(K) between 182 and 206: a1 = 318.67, a2 =-3.13 and a3 = 0.0076.  Zhang et al.[186] have also measured a low value of   2 x 10-4 on sulfuric acid monohydrate at 195 K.

47. 	ClONO2 + HCl + H2O(s) - Reaction probabilities of 0.27 (+0.73, -0.13) (Leu [104]) and 0.05 to 0.1 (Molina et al. [121]) have been reported near 200 K.  Abbatt et al. [4], Abbatt and Molina [5], and Hanson and Ravishankara [65] report that a portion of the reaction may be due to HOCl + HCl  Cl2 + H2O, with HOCl formed from ClONO2 + H2O(s)  HOCl + HNO3(s).  Hanson and Ravishankara [63] see no enhancement of the ClONO2 reaction probability when H2O(s) is doped with HCl.  Their preferred value is  = 0.3, but this is consistent with  = 1.  Using a Knudsen cell technique and looking at initial uptake, Oppliger et al. [130] measured  = 0.7 at 180 K and 0.2 at 200 K with HCl in excess.

48. 	ClONO2 + HCl + HNO3 • 3H2O - Measurements by Hanson and Ravishankara [63, 66], Leu and co-workers (Moore et al. [123], Leu et al. [105]), and Abbatt and Molina [6]  confirm a high .  Work by Hanson and Ravishankara  indicates that reaction probabilities on nitric acid dihydrate (NAD) are similar to those on NAT.  The most recent NAT studies (Abbatt and Molina [6]) show a strong fall-off with relative humidity from  >0.2 at 90% RH to 0.002 at 20% RH, indicating the necessity of sufficient water to solvate reactants.

49. 	ClONO2 + HCl + H2SO4 • nH2O - Hanson and Ravishankara [65] estimated that low temperature solubility limits for HCl in H2SO4 • nH2O (> 60 wt.% H2SO4) would restrict the ClONO2 + HCl reaction by demonstrating that HCl vapor has a minimal effect on ClONO2 uptake on 60-75 wt.% H2SO4 surfaces.  Tolbert et al. [161] also noted no measurable enhancement of ClONO2 loss on a 65 wt.% H2SO4 surface at 210 K when the surface is exposed to HCl, but the reaction products do change to include Cl2.  However, subsequent work (Hanson and Ravishankara [72]) has led to a re-evaluation of the process as a second-order liquid phase reaction between Cl- and ClONO2, which they estimate to proceed at a diffusion limited rate of 1-3 x 107 M-1 s-1 near 200 K.  Re-analysis of H* for HCl in cold concentrated H2SO4 (see next table) may make this process important even for 60-70 wt% H2SO4.  Additional measurements by Zhang et al.[184] and Elrod et al. [37] show substantial agreement with Hanson and Ravishankara [72] and illustrate the strong dependence of  on HCl solubility, which, in turn, depends on water activity. Both Zhang et al. and Elrod et al. examined the effect of HNO3 on the reaction and found no significant change.  Hanson and Lovejoy used an aerosol flow tube method to measure a reacto-diffusive length, l, of 0.009 ± 0.005 for 60 wt % H2SO4 at 250 K.  This is a factor of 4 smaller than l for ClONO2 hydrolysis on the same aerosol, showing a significantly enhanced reaction rate for these conditions.  Sulfuric acid surfaces with less than 60 wt.% H2SO4 also have sufficient water to absorb significant levels of HCl.  Wolff and Mulvaney [179], Hofmann and Oltmans [77], and Toon et al. [164] have suggested that such water-rich H2SO4 aerosols may form under polar stratospheric conditions.

50.	ClONO2+HCl + H2SO4 • H2O(s) and H2SO4 • 4H2O(s) - This reaction has been studied by Hanson and Ravishankara [71] and Zhang et al. [183].  The reaction probability is strongly dependent on the thermodynamic state of the SAT surface, which is controlled by the temperature and the water vapor partial pressure.  At a water vapor pressure of 5.6 x 10-4 torr the measured  drops by over two orders of magnitude as the SAT surface temperature rises from 195 to 206 K.  The results from the two groups are in qualitative agreement, but sample different H2O and HCl partial pressures.  Zhang et al.  have parameterized their data as a function of water partial pressure (at 195 K) and for temperature (both at an HCl partial pressure of 4 to 8 x 10-7 torr) in the  form log  = a1 + a2 log x + a3 (log x)2. For H2O partial pressure,  a1 = 5.25, a2 = 1.91, and a3 = 0.0; for T(K), a1 = 175.74, a2 = -1.59, and a3 = 0.0035.  Care must be taken in extrapolating either data set to lower HCl concentrations.  Zhang et al. [186] measured no enhancement of ClONO2 uptake on sulfuric acid monohydrate at 195 K with (2 - 8) x 10-7 torr of HCl present, implying  < 1 x 10-4.

51.	ClONO2 + HCl + Al2O3(s) - Molina et al. [120] used flow tube techniques to measure  = 0.020 ±0.005 on alumina at 195 - 230 K with stratospheric (5 ppmV) water vapor levels.  Measured  was independent of T and was affected very little by 5 ppbv HNO3 vapor.  The same  was measured for a Pyrex surface, indicating the absorbed water and not the inorganic substrate hosted the reaction.

52. 	ClONO2 + MX(s) - Finlayson-Pitts and co-workers have shown that ClONO2 reacts with crystalline NaCl (Finlayson-Pitts et al. [43]) and NaBr (Berko et al. [14]) to produce Cl2 and BrCl, respectively.  Timonen et al. [159] have measured the reaction rate for ClONO2 with dry and slightly wet  (water vapor pressure   5 x 10-5 - 3 x 10-4 torr) NaCl at temperatures of 225 and 296 K.  Reaction probabilities were analyzed as  = 4 - 7 x   10-3 and were independent of temperature and water vapor pressure within experimental error.  The Cl2 yield on dry NaCl was 1.0 ±0.2.  Caloz et al. [20] used a room temperature Knudsen cell technique to measure  = 0.23 ±0.06 for NaCl(s) and  = 0.35 ±0.06 for KBr(s).  They argue that the surface corrections imposed by Timonen et al. were too large.  Caloz et al. measured quantitative yields of Cl2 and BrCl products.

53.	ClONO2+HBr + H2O(s) and HNO3 • nH2O(s) - This reaction was studied by Hanson and Ravishankara [67] on water ice and NAT near 200 K.  A diffusion-limited reaction probability of >0.3 was observed.

54.	ClONO2+HF + H2O(s) and HNO3 • nH2O(s) - Hanson and Ravishankara [67] were not able to observe this reaction on water ice and NAT surfaces near 200 K.

55.	CFxCl(4-x ) (x=0-3) and CF2Br2 + Al2O3(s) - Robinson et al. [139] reported dissociative uptake of CF2Cl2 and CF2Br2 on -alumina surfaces at 210 and 315 K.  Reaction probabilities of about 1 x 10-3 at 210 K were measured by monitoring the amounts of surface species bonded to the Al2O3 substrate. A re-analysis (Robinson et al. [140]) lowered this value by about a factor of 50. Moderate surface dosage with water vapor did not quench the reaction.  In addition, Dai et al. [29] and Robinson et al. [138] studied dissociative chemisorption of CF3Cl, CF2Cl2, CFCl3, and CCl4 on dehydroxylated -alumina powders.  The obtained reactive uptake probabilities ranging from 0.4 x 10-5 for CFCl3 to 1.0 x 10-5 for CFCl3 over a temperature range of 120 to 300 K.  HCl and halomethyl radicals were observed as desorption products.  Loss of these products may point to somewhat higher s, since they were measured by integrating halogen bound to Al2O3 substrates.

56.	BrO + H2O(s) + H2O(s) and H2SO4 • nH2O(l) and NaCl(aq) - Abbatt [3] used a coated flow tube technique to measure heterogeneous uptake on water ice, 60 and 70 wt % H2SO4 at 213 K, and 23 wt % aqueous NaCl at 253 K.  He obtained (ice) = (1.0 ±0.4) x 10-3,  (60 wt % H2SO4) = (7 ±2) x 10- 4,  (70 wt % H2SO4) = (5 ±2) x 10- 4 and  (23 wt % NaCl) < 3 x 10-3.  He observed product Br2, indicating BrO self-reaction on both water ice and sulfuric acid solutions.  Since reaction rate will depend on BrO concentrations, no recommendation is made for an atmospheric rate.

57.	HOBr + HCl + H2O(s) and H2SO4 • nH2O - Abbatt [1] measured  = 0.25 (+0.10/-0.05) for this reaction on ice at 228 K.  The  BrCl  product was observed by mass spectrometry.  Abbatt[2] measured s of ~ 0.1 to 0.2 for [HCl] > 1 x 1012 cm-3 over 68.8 wt % H2SO4 at 228 K; yielding an estimated kII = 1.4 x 105 M-1 s-1 with a factor of 2 uncertainty.  Hanson and Ravishankara[73] also measured  = 0.2 [+0.2, - 0.1] for 60 wt % H2SO4 at 210 K.

58.	HOBr + HBr + H2O(s) and H2SO4 • nH2O - Abbatt [1] measured  = 0.12±(0.03) on ice at 228 K.  The Br2 product was  observed  by mass  spectrometry.  Abbatt [2]  measured  = 0.25 for [HBr] = 1 x 1012 cm-3 over 68.8 wt % H2SO4 at 228 K; yielding to an estimated kII > 5 x 104 M-1 s-1.

59.	BrONO2 and BrONO2+HCl + H2O(s) - Hanson and Ravishankara [68] investigated these reactions in an ice-coated flow reactor at 200 (±10) K.  The reaction of BrONO2 with H2O(s) proceeded at a rate indistinguishable from the gas phase diffusion limit, implying that the reaction probability may be as high as one;  the product BrNO(g) was observed.  Depositing HCl and BrONO2 on ice led to rapid production of BrCl.  This may have been produced directly through reaction of BrONO2 with adsorbed HCl or, indirectly, through production of HOBr in the BrONO2/ice reaction, followed by reaction of HOBr + HCl.  No kinetic parameters for BrCl production were given.

60.	BrONO2 and BrONO2 + HCl + H2SO4 • nH2O - Hanson and co-workers ([62, 73]) used both coated flow tube and aerosol flow tube techniques to show that the reaction of BrONO2 with 45-70 wt % H2SO4 is extremely facile at temperatures from 210 to 298 K.  Hanson and Ravishankara [73] measured s of 0.5 (+ 0.5, - 0.25) (45 wt %  H2SO4, 210 K, 0.4 (+0.6, -0.2) (60 wt %, 210 K) , and  0.3 (+ 0.7, -0.1 (70 wt %, 220 K) in a coated-wall flow tube experiment.  Hanson et al. [62] measured  ~ 0.8 (20 to 40% error) for submicron aerosols at temperatures between 249 and 298 K and H2SO4 concentrations of 45 to 70 wt %; they did observe a sharp fall off in  for H2SO4 concentrations between 73 and 83 wt %.  Addition of excess  HCl to 229 K 40 and 60 wt % H2SO4 aerosols caused an increase in  to 1.0 and 0.9, respectively.

61.	CF3OH + H2O + H2O(l) and H2SO4 • nH2O(l) - Lovejoy et al. [109] used both wetted-wall and aerosol flow tube techniques to measure reactive uptake of CF3OH on water at 274 K and 39 - 60 wt % H2SO4 at various temperatures between 206 and 250 K.   s showed a strong dependence on water activity.  Aerosol uptake studies yielded reacto-diffusive lengths, l, of > 0.4 µm for 40 wt % H2SO4 and 1.0 µm for 50 wt % H2SO4, both at 250 K.  Recommended 's were estimated by averaging bulk uptake measurements at similar H2SO4 concentrations and ignoring temperature effects on water activity.

### Table 65.  Henry's Law Constants for Gas-Liquid Solubilities

T(K)		      Wt. % H2SO4		H or H*			 Notes

(M/atm)

HONO in H2SO4 • nH2O(l)

248-298		0.3 - 53	H* = (47.2 ±2.8) exp(-0.044 ±0.002) X	          1

X = (wt % H2SO4)

HNO3 in H2SO4 • nH2O

~195 - 300		0-80			See Note			          2

HCl in H2SO4 • nH2O • H2O(l) and H2SO4 • nHNO3 • mH2O(l)

~195 - 300		0 - 80			See Note			          2

HBr in H2SO4 • nH2O • H2O(l) and H2SO4 • nHNO3 • mH2O(l)

~195 - 300		0 - 80			See Note			          2

HOCl in H2SO4 • nH2O(l)

200 - 230		46 - 80			See Note			          3

HC(O)OH in H2O(l)

298			0			1.1 x 104			          4

CH3C(O)OH in H2O(l)

298			0			7 x 103				          4

CH3C(O)O2 in H2O(l)

275			0			<0.1				          5

CH3C(O)OONO2 in H2O(l)

293			0			4.1				          6

CH3CH2C(O)OONO2 in H2O(l)

293			0			2.9				          6

CCl2O in H2O(l)

278			0			< 0.2				          7

298			0			< 0.1				          7

CCl3CClO in H2O(l)

278			0			≤ 2				          8

CF2O in H2O(l)

278			0			< 1				          9

CF2O in H2SO4 • nH2O

215-230		60			< 5				        10

CF3CFO in H2O(l)

278			0			< 1				          9

Table 65.  Henry's Law Constants for Gas-Liquid Solubilities-continued

T(K)		      Wt. % H2SO4		H or H*			 Notes

(M/atm)

CF3CClO in H2O(l)

278			0			≤ 0.5				        10

CF3OH in H2SO4 • nH2O(l)

250			40			>240				        13

50			  210

CF3C(O)OH in H2O(l)

278-308		0			See Note		 	        14

NO3 in H2O(l)

273			0			0.6 ±0.3			        15

_____________________________________________________________________________________________

#### Notes to Table 65

1.	Becker et al.[10] measured H* for HONO between 248 and 298 K and 0.3 to 73.3 wt % H2SO4.  H* fell monotonically, with the expression tabulated up to 53 wt % H2SO4.  Above that, H* increased due to nitrosyl sulfuric acid formation (see previous table for reactive uptake ).

2.	Effective Henry's law coefficients, H*, for HNO3, HCl and HBr in binary H2SO4/H2O and ternary H2SO4/HNO3/H2O solutions over the temperature range 195 to 300 K are required to model the composition and heterogeneous chemistry of stratospheric and upper tropospheric aerosols.  Solubility data can be obtained from analysis of heterogeneous uptake experiments with the liquid phase diffusion coefficient estimated from acid solution viscosity (Williams and  Long [177]) or from vapor pressure data.

Recent experimental solubility data for HNO3 is provided by Van Doren et al. [167], Reihs et al. [135] and Zhang et al. [188].  Data for HCl solubility is provided by Watson et al. [174], Hanson and Ravishankara [66, 70], Zhang et al. [188], Williams and Golden [175], Abbatt [2] and Elrod et al.[37].  Data for HBr is provided by Williams et al. [176] and Abbatt [2].

These studies all show that trace species solubility in H2SO4/H2O and H2SO4/HNO3/H2O solutions is a strong function of water activity, which, in turn, depends on both temperature and acid concentrations.  Prediction of HNO3, HCl, and HBr H* values for atmospheric compositions requires a sophisticated model.  Comprehensive thermodynamic models of acid solutions for a range of atmospheric conditions have been published by Carslaw et al. [21], Tabazadeh et al. [154] and Luo et al. [110] and reviewed by Carslaw and Peter [22].  These models do an excellent job of reproducing the available experimental data, even for ternary H2SO4/HNO3/H2O solutions (Elrod et al. [37]).  These models and the Carslaw review should be consulted for plots/predictions of H* for HNO3, HCl,  and HBr in strong acid solutions over the atmospheric temperature range.

3.	Huthwelker et al.[81] have extrapolated room temperature acqueous HOCl solubility data to stratospheric temperature and acid concentrations using a thermodynamic model of acid solutions.  They obtain a Setchenow-type dependence on H2SO4 molality, mH2SO4, for HOCl activity and parameritize the physical Henry's law constant as:

ln H*  = 6.4946 - mH2SO4 (-0.04107 + 54.56/T) - 5862 (1/To - 1/T)

where 	T = T(K), To = 298.15 K and H = mHOCl/pHOCl in mol kg-1 atm-1.

4.	Johnson et al. [89] determined H* = (8.9 ±1.3) x 103 M atm-1 for formic acid and H* = (4.1 ±0.4) x 103 M atm-1 for acetic acid at 298 K in a  packed column experiment.  Earlier bubbler measurements by Servant et al. [150] measured (13.4 ±1.6) x 103 at 297 K and (9.3 ±1.1) x 103 at 296 K, respectively.  Combining the measured values, "best" experimental values of (11 ±2) x 103 and (7 ± 3) x 103 M atm-1 for 298 were recommended.

5.	Villalta et al. [168] measured an upper limit for H of 0.1 M atm-1 in coated-wall flow tube uptake experiments on aqueous sodium ascorbate solutions.

6.	Kames and Schurath[91] measured H = 4.1 ± 0.8 M atm-1 for peroxyacetylnitrate (PAN) in distilled water at 293.2 K with a bubbler apparatus; a slightly lower value of 3.6 ±0.2 was obtained for synthetic sea water of 0.61 ionic strength.  They also measured 2.9 ±0.06 (distilled water) and 2.5 ±0.5 (synthetic sea water) for peroxypropionalnitrate.  Their PAN value agrees with earlier measuremnts by Kames et al. [92] and unpublished work by Y.N. Lee.

7.	De Bruyn et al. [33] reported limits of < 0.15 at 278 K and < 0.06 at 298 K from a bubble column uptake experiment.  Uptake was controlled by H(khyd)1/2 in these experiments.  Reported limits are consistent with values from a liquid jet experiment of 0.11 at 288 K, 0.07 at 298 K, 0.05 at 308 K and 0.03 at 319 K reported by Manogue and Pigford [112].

8.	De Bruyn et al. report a limit of < 1.9 from a bubble column experiment where uptake was controlled by H(khyd)1/2.  George et al. [47] report a value of 2 for the temperature range of 274-294 K from a droplet train experiment with uptake also controlled by H(khyd)1/2, although the khyd value used to deconvolute the data was not well determined.

9.	De Bruyn et al. report a limit of < 1.0 at 278 K based on uptake controlled by H(khyd)1/2 in a bubble column experiment.  This is consistent with the limit on the uptake coefficient measured by the same group with a droplet train experiment at 300 K (De Bruyn et al. [31]).  George et al. [49] report much higher (Hkhyd)1/2 values,  implying H values > 20 for temperatures between 273 and 294 K. However, this analysis is suspect due to low signal strengths and large data scatter  at all temperatures.

10.	Hanson and Ravishankara [64] calculate an upper limit for H of CF2O based on assumed solubility limit resulting in lack of measurable uptake into 60 wt% H2SO4.

11.	De Bruyn et al. report a limit of < 0.9 at 278 K from a bubble column experiment where uptake was controlled by H(khyd)1/2.  George et al. [49] report a value of 3 at 284 K from a droplet train experiment where uptake was also controlled by H(khyd)1/2; however, deconvolution of time-dependent uptake data to yield it and khyd is suspect due to low signals and high data scatter at each temperature.

12.	De Bruyn et al. report a limit of < 0.3 at 278 K from a bubble column experiment where uptake was controlled by H(khyd)1/2.  George et al. [49] report a value of 2 at 284 K from a droplet train experiment with uptake also controlled by H(khyd)1/2; however, deconvolution of time-dependent uptake data to yield H and khyd is suspect due to low signal strength and high data scatter at each temperature.

13.	Lovejoy et al. [109] determined recto-diffusive lengths of > 0.4 µm and 1.0 µm for CF3OH uptake at  250 K on 40 and 50 wt % H2SO4 aerosols, respectively.  This leads to H* estimates of > 240 and 210 M atm-1, respectively.

14.	Bowder et al. [17] measured CF3C(O)OH vapor pressures over water at 278.15, 298.15 and 308.15 K yielding a suggested parameterization of H (mol kg-1 atm-1) = 9.009 - 9.328 x 103 (1/To - 1/T) where T = T(K) and To = 298.15 K.

15.	Wetted-wall flow tube measurements by Rudich et al. [145] yielded an H(Dl)1/2 value of (1.9 ±0.2) x 10-3 M atm-1 cm s-1/2. They assumed a liquid phase diffusion coefficient, Dl = (1.0 ±0.5) x 10-5 cm2 s-1, yielding a Henry's law constant of 0.6 ± 0.3 M atm-1 at 273 K.  This is one third of an earlier measurement of 1.8 ±1.5 M atm-1 quoted in Michelcic et al. [119].

### References for Heterogeneous Section

1.	Abbatt, J.P.D., 1994, Geophys. Res. Lett., 21, 665-668.

2.	Abbatt, J.P.D., 1995, Geophys. Res. Lett., 100, 14,009-14,017.

3.	Abbatt, J.P.D., 1996, Geophys. Res. Lett., 23, 1681-1684.

4.	Abbatt, J.P.D., K.D. Beyer, A.F. Fucaloro, J.R. McMahon, P.J. Wooldridge, R. Zhong, and M.J. Molina, 1992, J. Geophys. Res., 97, 15819-15826.

5.	Abbatt, J.P.D. and M.J. Molina, 1992, Geophys. Res. Lett., 19, 461-464.

6.	Abbatt, J.P.D. and M.J. Molina, 1992, J. Phys. Chem., 96, 7674-7679.

7.	Alebic'-Juretic', A., T. Cuitas, and L. Klasine, 1992, Ber. Bunsenges Phys. Chem., 96, 493-495.

8.	Baldwin, A.C. and D.M. Golden, 1979, Science, 206, 562.

9.	Baldwin, A.C. and D.M. Golden, 1980, J. Geophys. Res., 85, 2888-2889.

10.	Becker, K.H., J. Kleffman, R. Kurtenbach, and P. Wiesen, 1996, J. Phys. Chem., 100, 14,984-14,990.

11.	Behnke, W., H.-U. Kruger, V. Scheer, and C. Zetzsch, 1992, J. Aerosol Sci., 23, S923-S936.

12.	Behnke, W., V. Scheer, and C. Zetzsch, 1993, J. Aerosol Sci., 24, S115-S116.

13.	Beichert, P. and B.J. Finlayson-Pitts, 1996, J. Phys. Chem., 100, 15,218-15,228.

14.	Berko, H.N., P.C. McCaslin, and B.J. Finlayson-Pitts, 1991, J. Phys. Chem., 95, 6951-6958.

15.	Bongartz, A., J. Kames, U. Schurath, C. George, P. Mirabel, and J.L. Ponche, 1994, J. Atm. Chem., 18, 149-160.

16.	Bongartz, A., S. Schweighoefer, C. Roose, and U. Schurath, 1995, J. Atmos. Chem., 20, 35-58.

17.	Bowder, D.J., S.L. Clegg, and P. Brimblecombe, 1996, Chemosphere, 32, 405-420.

18.	Brown, D.E., S.M. George, C. Huang, E.K.L. Wong, K.B. Rider, R.S. Smith, and B.D. Kay, 1996, J. Phys. Chem., 100, 4988-4995.

19.	Brown, L.A., V. Vaida, D.R. Hanson, J.D. Graham, and J.T. Roberts, 1996, J. Phys. Chem., 100, 3121-3125.

20.	Caloz, F., F.F. Fentner, and M.J. Rossi, 1996, J. Phys. Chem., 100, 7494-7501.

21.	Carslaw, K.S., S.L. Clegg, and P. Brimblecombe, 1995, J. Phys. Chem., 99, 11,557-11,574.

22.	Carslaw, K.S. and T. Peter, 1996, Rev. Geophys., submitted.

23.	Chu, L.T. and J.W. Heron, 1995, Geophys. Res. Lett., 22, 3211-3214.

24.	Chu, L.T., M.-T. Leu, and L.F. Keyser, 1993, J. Phys. Chem., 97, 12798-12804.

25.	Chu, L.T., M.-T. Leu, and L.F. Keyser, 1993, J. Phys. Chem., 97, 7779-7785.

26.	Clegg, S.L. and P. Brimblecombe, 1986, Atmos. Environ., 20, 2483.

27.	Cooper, P.L. and J.P.D. Abbatt, 1996, J. Phys. Chem., 100, 2249-2254.

28.	Dai, D.J., S.J. Peters, and G.E. Ewing, 1995, J. Phys. Chem., 99, 10,299-10,304.

29.	Dai, Q., G.N. Robinson, and A. Freedman, 1996, J. Phys. Chem., submitted.

30.	Daumer, R. Nissner, and D. Klockow, J. Aerosol Sci., 23, 315-325.

31.	De Bruyn, W.J., S.X. Duan, X.Q. Shi, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1992, Geophys. Res. Lett., 19, 1939-1942.

32.	De Bruyn, W.J., J.A. Shorter, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1994, J. Geophys. Res., 99, 16927-16932.

33.	DeBruyn, W.J., J.A. Shorter, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1995, Environ. Sci Technol., 29, 1179-1185.

34.	Dlugokencky, E.J. and A.R. Ravishankara, 1992, Geophys. Res. Lett., 19, 41-44.

35.	Donaldson, D.J., J.A. Guest, and M.C. Goh, 1995, J. Phys. Chem., 99, 9313-9315.

36.	Duan, S.X., J.T. Jayne, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1993, J. Phys. Chem., 97, 2284-2288.

37.	Elrod, M.J., R.E. Koch, J.E. Kim, and M.S. Molina, 1995, Faraday Discuss, 100, 269-278.

38.	Fendel, W., D. Matter, H. Burtscher, and A. Schimdt - Ott, 1995, Atmos. Environ, 29, 967-973.

39.	Fendel, W. and A.S. Ott, 1993, J. Aerosol Sci., 24, S317-S318.

40.	Fenter, F.F., F. Caloz, and M.J. Rossi, 1994, J. Phys. Chem., 98, 9801-9810.

41.	Fenter, F.F., F. Caloz, and M.J. Rossi, 1996, J. Phys. Chem., 100, 1008-1019.

42.	Fenter, F.F. and M.J. Rossi, 1996, J. Phys. Chem., 100, 13765-13775.

43.	Finlayson-Pitts, B.J., M.J. Ezell, and J.N. Pitts Jr., 1989, Nature, 337, 241-244.

44.	Fox, L.E., D.R. Worsnop, M.S. Zahniser, and S.C. Wofsy, 1994, Science, 267, 351-355.

45.	Fried, A., B.E. Henry, J.G. Calvert, and M. Mozukewich, 1994, J. Geophys. Res., 99, 3517-3532.

46.	Fung, K.N., I.N. Tang, and H.R. Munkelwitz, 1987, Appl. Optics, 26, 1282-1287.

47.	George, C., J. Lagrange, P. Lagrange, P. Mirabel, C. Pallares, and J.L. Ponche, 1994, J. Geophys. Res., 99, 1255-1262.

48.	George, C., J.L. Ponche, P. Mirabel, W. Behnke, V. Sheer, and C. Zetzsch, 1994, J. Phys. Chem., 98, 8780-8784.

49.	George, C., J.Y. Saison, J.L. Ponche, and P. Mirabel, 1994, J. Phys. Chem., 98, 10857-10862.

50.	Gershenzon, Y.M., A.V. Ivanov, S.I. Kucheryavyi, and V.B. Rozenshtein, 1986, Kinet. Katal., 27, 1069-1074.

51.	Gershenzon, Y.M. and A.P. Purmal, 1990, Russ. Chem. Rev., 59, 1007-1023.

52.	Gersherzon, V.M., V.M. Grigorieva, A.V. Ivanov, and R.G. Remorov, 1995, Faraday Discuss, 100, 83-100.

53.	Gertner, B.J. and J.T. Hynes, 1996, Science, 271, 1563-1566.

54.	Graham, J.D. and J.T. Roberts, 1994, J. Phys. Chem., 98, 5974-5983.

55.	Graham, J.D. and J.T. Roberts, 1995, Geophys. Res. Lett., 22, 251-254.

56.	Graham, J.D., J.T. Roberts, L.A. Brown, and V. Vaida, 1996, J. Phys. Chem., 100, 3115-3120.

57.	Hanning-Lee, M.A., B.B. Brady, L.R. Martin, and J.A. Syage, 1996, Geophys. Res. Lett., 23, 1961-1964.

58.	Hanson, D.R., 1992, Geophys. Res. Lett., 19, 2063-2066.

59.	Hanson, D.R., 1995, J. Phys. Chem., 99, 13,059-13,061.

60.	Hanson, D.R., J.B. Burkholder, C.J. Howard, and A.R. Ravishankara, 1992, J. Phys. Chem., 96, 4979-4985.

61.	Hanson, D.R. and E.R. Lovejoy, 1994, Geophys. Res. Lett., 21, 2401-2404.

62.	Hanson, D.R. and E.R. Lovejoy, 1995, Science, 267, 1326-1329.

63.	Hanson, D.R. and A.R. Ravishankara, 1991, J. Geophys. Res., 96, 5081-5090.

64.	Hanson, D.R. and A.R. Ravishankara, 1991, Geophys. Res. Lett., 18, 1699-1701.

65.	Hanson, D.R. and A.R. Ravishankara, 1991, J. Geophys. Res., 96, 17307-17314.

66.	Hanson, D.R. and A.R. Ravishankara, 1992, J. Phys. Chem., 96, 2682-2691.

67.	Hanson, D.R. and A.R. Ravishankara, 1992, J. Phys. Chem., 96, 9441-9446.

68.	Hanson, D.R. and A.R. Ravishankara, 1993, J. Phys. Chem., 97, 2802-2803.

69.	Hanson, D.R. and A.R. Ravishankara, 1993, The Tropospheric Chemistry of Ozone in the Polar Regions, H. Niki and K.H. Becker, Editors,  NATO, pp. 17281-17290.

70.	Hanson, D.R. and A.R. Ravishankara, 1993, J. Phys. Chem., 97, 12309-12319.

71.	Hanson, D.R. and A.R. Ravishankara, 1993, J. Geophys. Res., 98, 22931-22936.

72.	Hanson, D.R. and A.R. Ravishankara, 1994, J. Phys. Chem., 98, 5728-5735.

73.	Hanson, D.R. and A.R. Ravishankara, 1995, Geophys. Res. Lett., 22, 385-388.

74.	Hanson, D.R., A.R. Ravishankara, and S. Solomon, 1994, J. Geophys. Res., 99, 3615-3629.

75.	Harker, A.B. and W.W. Ho, 1979, Atmos. Environ., 13, 1005-1010.

76.	Haynes, D.R., N.J. Tro, and S.M. George, 1992, J. Phys. Chem., 96, 8502-8509.

77.	Hofmann, D.J. and S.J. Oltmans, 1992, Geophys. Res. Lett., 22, 2211-2214.

78.	Hu, J.H., Q. Shi, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1995, J. Phys. Chem., 99, 8768-8776.

79.	Hu, J.H., J.A. Shorter, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1993, J. Phys. Chem., 97, 11037-11042.

80.	Huntzicker, J.J., R.A. Cary, and C.-S. Ling, 1980, Environ. Sci. Technol., 14, 819-824.

81.	Huthwelker, T., T. Peter, B.P. Juo, S.L. Clegg, K.S. Carshlaw, and P. Brimblecombe, 1995, J. Atmos. Chem., 21, 81-95.

82.	Imamura, T., Y. Rudich, R.K. Talukdar, R.W. Fox, and A.R. Ravishankara, 1996, J. Phys. Chem., submitted.

83.	Iraci, L.T., A.M. Middlebrook, M.A. Wilson, and M.A. Tolbert, 1994, Geophys. Res. Lett., 21, 867-870.

84.	Ivanov, A.V., Y.M. Gersherzon, F. Gratpanche, P. Devolder, and J.-P. Saverysyn, 1996, Am. Geophys., 14, 659-664.

85.	Jayne, J.T., P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1990, J. Phys. Chem., 94, 6041-6048.

86.	Jayne, J.T., S.X. Duan, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1991, J. Phys. Chem., 95, 6329-6336.

87.	Jayne, J.T., S.X. Duan, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1992, J. Phys. Chem., 96, 5452-5460.

88.	Jayne, J.T., D.R. Worsnop, C.E. Kolb, E. Swartz, and P. Davidovits, 1996, J. Phys. Chem., 100, 8015-8022.

89.	Johnson, B.J., E.A. Betterton, and D. Craig, 1996, J. Atmos. Chem., 24, 113-119.

90.	Kalberer, M., K. Tubor, M. Ammann, Y. Parrat, E. Weingartner, D. Piguet, E. Rossler, D.T. Just, A. Jurles, H.W. Gaaggeler, and V. Baltersperger, 1996, J. Phys. Chem., 100, 15,487-45,493.

91.	Kames, J. and U. Schurath, 1995, J. Atmos. Chem., 21, 151-164.

92.	Kames, J., S. Schweighoefer, and U. Schurath, 1991, J. Atmos. Chem., 12, 169-180.

93.	Kenner, R.D., I.C. Plumb, and K.R. Ryan, 1993, Geophys. Res. Lett., 20, 193-196.

94.	Keyser, L.F. and M.-T. Leu, 1993, J. Colloid Interface Sci., 155, 137-145.

95.	Keyser, L.F. and M.-T. Leu, 1993, Micros. Res. Technol., 25, 434-438.

96.	Keyser, L.F., M.-T. Leu, and S.B. Moore, 1993, J. Phys. Chem., 97, 2800-2801.

97.	Keyser, L.F., S.B. Moore, and M.T. Leu, 1991, J. Phys. Chem., 95, 5496-5502.

98.	Koehler, B.G., L.S. McNeill, A.M. Middlebrook, and M.A. Tolbert, 1993, J. Geophys. Res., 98, 10563-10571.

99.	Kolb, C.E., D.R. Worsnop, M.S. Zahniser, P. Davidovits, L.F. Keyser, M.-T. Leu, M.J. Molina, D.R. Hanson, A.R. Ravishankara, L.R. Williams, and M.A. Tolbert, 1994, "Progress and Problems in Atmospheric Chemistry," Adv. Phys. Chem. Series, 3, J.R. Barker, Editor,   , pp. 771-875.

100.	Kroes, G.-J. and D.C. Clary, 1992, J. Phys. Chem., 96, 7079-7088.

101.	Laux, J.M., J.C. Hemminger, and B.J. Finlayson-Pitts, 1994, Geophys. Res. Lett., 21, 1623-1626.

102.	Leu, M.-T., R.S. Timonen, L.F. Keyser, and Y.L. Yung, 1995, J. Phys. Chem., 99, 13,203-13,212.

103.	Leu, M.T., 1988, Geophys. Res. Lett., 15, 851-854.

104.	Leu, M.T., 1988, Geophys. Res. Lett., 15, 17-20.

105.	Leu, M.T., S.B. Moore, and L.F. Keyser, 1991, J. Phys. Chem., 95, 7763-7771.

106.	Li, Z., R.R. Friedl, S.B. Moore, and S.P. Sander, 1996, J. Geophys. Res., 101, 6795-6802.

107.	Livingston, F.E. and B.J. Finlayson-Pitts, 1991, Geophys. Res. Lett., 18, 17-20.

108.	Lovejoy, E.R. and D.R. Hanson, 1995, J. Phys. Chem., 99, 2080-2087.

109.	Lovejoy, E.R., L.G. Huey, and D.R. Hanson, 1995, J. Geophys. Res., 100, 18,775-18,780.

110.	Luo, B., K.S. Carslaw, T. Peter, and S.L. Clegg, 1995, Geophys. Res. Lett., 22, 247-250.

111.	Manion, J.A., C.M. Fittschen, D.M. Golden, L.R. Williams, and M.A. Tolbert, 1994, Israel J. Chem., 34, 355-363.

112.	Manogue, W.H. and R.L. Pigford, 1960, A.I.Ch.E.J., 6, 494-500.

113.	Martin, L.R., H.S. Judeikis, and M. Wun, 1980, J. Geophys. Res., 85, 5511-5518.

114.	McMurry, P.H., H. Takano, and G.R. Anderson, 1983, Environ. Sci. Technol., 17, 347-357.

115.	Mertes, S. and A. Wahner, 1995, J. Phys. Chem., 99, 14,000-14,006.

116.	Michelangeli, D.V., M. Allen, and Y.L. Yung, 1991, Geophys. Res. Lett., 18, 673-676.

117.	Middlebrook, A.M., L.T. Iraci, L.S. McNeil, B.G. Koehler, M.A. Wilson, O.W. Saastad, and M.A. Tolbert, 1993, J. Geophys. Res., 98, 20473-20481.

118.	Middlebrook, A.M., B.G. Koehler, L.S. McNeill, and M.A. Tolbert, 1992, Geophys. Res. Lett., 19, 2417-2420.

119.	Mihelcic, D., D. Klemp, P. Msgen, H.W. Ptz, and A. Volz-Thomas, 1993, J. Atmos. Chem., 16, 313-335.

120.	Molina, M.J., R.F. Meads, D.D. Spencer, and L.T. Molina, 1996, Geophys. Res. Lett., submitted.

121.	Molina, M.J., T.L. Tso, L.T. Molina, and F.C. Wang, 1987, Science, 238, 1253-1259.

122.	Molina, M.J., R. Zhang, P.J. Woolridge, J.R. McMahon, J.E. Kim, H.Y. Chang, and K.D. Beyer, 1993, Science, 261, 1418-1423.

123.	Moore, S.B., L.F. Keyser, M.T. Leu, R.P. Turco, and R.H. Smith, 1990, Nature, 345, 333-335.

124.	Mozurkewich, M. and J. Calvert, 1988, J. Geophys. Res., 93, 889-896.

125.	Mozurkewich, M., P.H. McMurray, A. Gupta, and J.G. Calvert, 1987, J. Geophys. Res., 92, 4163-4170.

126.	Msibi, I.M., Y. Li, J.P. Shi, and R.M. Harrison, 1994, J. Phys. Chem., 18, 291-300.

127.	Msibi, I.M., J.P. Shi, and R.M. Harrison, 1993, J. Atmos. Chem., 17,339-17,351.

128.	Noyes, R.M., M.B. Rubin, and P.G. Bowers, 1996, J. Phys. Chem., 100, 4167-4172.

129.	Olszyna, K., R.D. Cadle, and R.G. dePena, 1979, J. Geophys. Res., 84, 1771-1775.

130.	Oppliger, R., A. Allanic, and M.J. Rossi, 1996, J. Phys. Chem., submitted.

131.	Peters, S.J. and G.E. Ewing, 1996, J. Phys. Chem., 100, 14,093-14,102.

132.	Ponche, J.L., C. George, and P. Mirabel, 1993, J. Atmos. Chem., 16, 1-21.

133.	Pueschel, R.F., D.F. Blake, A.G. Suetsinger, A.D.A. Hansen, S. Verma, and K. Kato, 1992, Geophys. Res. Lett., 19, 1659-1662.

134.	Quinlan, M.A., C.M. Reihs, D.M. Golden, and M.A. Tolbert, 1990, J. Phys. Chem., 94, 3255-3260.

135.	Reihs, C.M., D.M. Golden, and M.A. Tolbert, 1990, J. Geophys. Res., 95, 16,545-16,550.

136.	Rieley, H., H.D. Aslin, and S. Haq, 1995, J. Chem. Soc. Faraday Trans., 91, 2349-2351.

137.	Robbins, R.C. and R.D. Cadle, 1958, J. Phys. Chem., 62, 469-471.

138.	Robinson, G.N., Q. Dai, and A. Freedman, 1996, J. Phys. Chem., submitted.

139.	Robinson, G.N., A. Freedman, C.E. Kolb, and D.R. Worsnop, 1994, Geophys. Res. Lett., 21, 377-380.

140.	Robinson, G.N., A. Freedman, C.E. Kolb, and D.R. Worsnop, 1996, Geophys. Res. Lett., 23, 317.

141.	Robinson, G.N., D.R. Worsnop, J.T. Jayne, C.E. Kolb, and P. Davidovits, 1996, J. Geophys. Res., 102, 3583-3601.

142.	Rogaski, C.A., D.M. Golden, and L.R. Williams, 1996, Geophys. Res. Lett., 24, 381-384.

143.	Rossi, M.J., R. Malhotra, and D.M. Golden, 1987, Geophys. Res. Lett., 14, 127-130.

144.	Rubel, G.O. and J.W. Gentry, 1984, J. Aerosol Sci., 15, 661-671.

145.	Rudich, Y., R.K. Talukdar, R.W. Fox, and A.R. Ravishankara, 1996, J. Geophys. Res., 101, 21,023-21,031.

146.	Rudich, Y., R.K. Talukdar, T. Imamura, R.W. Fox, and A.R. Ravishankara, 1996, Chem. Phys. Lett., 261, 467-473.

147.	Rudolf, R. and P.E. Wagner, 1994, J. AerosolSci, 25, 597-598.

148.	Saastad, O.W., T. Ellerman, and C.J. Nielson, 1993, Geophys. Res. Lett., 20, 1191-1193.

149.	Schwartz, S.E., 1988, Atmos. Environ., 22, 2331.

150.	Servant, J., G. Koundio, B. Cross, and R. Delmas, 1991, J. Atmos. Chem., 12, 367-380.

151.	Shimono, A. and S. Koda, 1996, J. Phys. Chem., 100, 10,269-10,276.

152.	Smith, D.M., W.F. Welch, J.A. Jassim, A.R. Chughtai, and D.H. Stedman, 1988, Appl. Spectros., 42, 1473-1482.

153.	Stephens, S., M.J. Rossi, and D.M. Golden, 1986, Int. J. Chem. Kinetics, 18, 1133-1149.

154.	Tabazadeh, A., R.P. Turco, and M.Z. Jacobson, 1994, J. Geophys. Res., 99, 12,897-12,914.

155.	Tabor, K., L. Gutzwiller, and M.J. Rossi, 1993, Geophys. Res. Lett., 20, 1431-1434.

156.	Tabor, K., L. Gutzwiller, and M.J. Rossi, 1994, J. Phys. Chem., 98, 6172-7186.

157.	Tang, I.N. and J.H. Lee, 1987, The Chemistry of Acid Rain, G.E. Gordon and R.W. Johnson, Editors,  Am. Chem. Soc. Symp. Series, pp. 109-117.

158.	Tang, I.N. and H.R. Munkelwitz, 1989, J. Colloid Interface Sci., 128, 289-295.

159.	Timonen, R.S., L.T. Chu, M.-T. Leu, and L.F. Keyser, 1994, J. Phys. Chem., 98, 9509-9517.

160.	Tolbert, M.A., J. Praff, I. Jayaweera, and M.J. Prather, 1993, J. Geophys. Res., 98, 2957-2962.

161.	Tolbert, M.A., M.J. Rossi, and D.M. Golden, 1988, Geophys. Res. Lett., 15, 847-850.

162.	Tolbert, M.A., M.J. Rossi, and D.M. Golden, 1988, Science, 240, 1018-1021.

163.	Tolbert, M.A., M.J. Rossi, R. Malhotra, and D.M. Golden, 1987, Science, 238, 1258-1260.

164.	Toon, O., et al., 1993, Science, 261, 1136-1140.

165.	Utter, R.G., J.B. Burkholder, C.J. Howard, and A.R. Ravishankara, 1992, J. Phys. Chem., 96, 4973-4978.

166.	Van Doren, J.M., L.R. Watson, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1990, J. Phys. Chem., 94, 3265-3269.

167.	Van Doren, J.M., L.R. Watson, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1991, J. Phys. Chem., 95, 1684-1689.

168.	Villalta, P.W., E.R. Lovejoy, and D.R. Hanson, 1996, Geophys. Res. Lett., 23, 1765-1768.

169.	Vogt, R., Elliott, C., Allen, H.C., Laux, J.M., J.C. Hemminger, and B.J. Finlayson-Pitts, 1996, Atmos. Environ, 30, 1729-1737.

170.	Vogt, R. and B. Finlayson-Pitts, 1994, J. Phys. Chem., 98, 3747-3755.

171.	Vogt, R. and B.F. Finlayson-Pitts, 1994, Geophys. Res. Lett., 21, 2291-2294.

172.	Vogt, R. and B.J. Finlayson-Pitts, 1995, J. Phys. Chem., 99, 13,052.

173.	Wang, L. and D.C. Clary, 1996, J. Chem. Phys., 104, 5663-5673.

174.	Watson, L.R., J.M.V. Doren, P. Davidovits, D.R. Worsnop, M.S. Zahniser, and C.E. Kolb, 1990, J. Geophys. Res., 95, 5631-5638.

175.	Williams, L.R. and D.M. Golden, 1993, Geophys. Res. Lett., 20, 2227-2230.

176.	Williams, L.R., D.M. Golden, and D.L. Huestis, 1995, J. Geophys. Res., 100, 7329-7335.

177.	Williams, L.R. and F.S. Long, 1995, J. Phys. Chem., 99, 3748-3751.

178.	Williams, L.R., J.A. Manion, D.M. Golden, and M.A. Tolbert, 1994, J. Appl. Meteor., 33, 785-790.

179.	Wolff, E.W. and R. Mulvaney, 1991, Geophys. Res. Lett., 18, 1007-1010.

180.	Worsnop, D.R., L.E. Fox, M.S. Zahniser, and S.C. Wofsy, 1993, Science, 259, 71-74.

181.	Worsnop, D.R., M.S. Zahniser, C.E. Kolb, J.A. Gardner, L.R. Watson, J.M.V. Doren, J.T. Jayne, and P. Davidovits, 1989, J. Phys. Chem., 93, 1159-1172.

182.	Zetzsch, C. and W. Behnke, 1992, Ber. Bunsenges. Phys. Chem., 96, 488-493.

183.	Zhang, R., J.T. Jayne, and M.J. Molina, 1994, J. Phys. Chem., 98, 867-874.

184.	Zhang, R., M.-T. Leu, and L.F. Keyser, 1994, J. Phys. Chem., 98, 13,563-13,574.

185.	Zhang, R., M.-T. Leu, and L.F. Keyser, 1995, Geophys. Res. Lett., 22, 1493-1496.

186.	Zhang, R., M.-T. Leu, and L.F. Keyser, 1995, J. Geophys. Res., 100, 18,845-18,854.

187.	Zhang, R., M.-T. Leu, and L.F. Keyser, 1996, J. Phys. Chem., 100, 339-345.

188.	Zhang, R., P.J. Wooldridge, and M.J. Molina, 1993, J. Phys. Chem., 97, 8541-8548.

189.	Zolensky, M.E., D.S. McKay, and L.A. Kaczor, 1989, J. Geophys. Res., 94, 1047-1056.

## APPENDIX 1:  GAS PHASE ENTHALPY DATA

SPECIES 	 ∆Hf(298)		SPECIES 	 ∆Hf(298)	SPECIES	 ∆Hf(298)	SPECIES	 ∆Hf(298)

(Kcal/mol)			(Kcal/mol)		(Kcal/mol)		(Kcal/mol)

H	52.1

H2	0.00

O	59.57

O(1D)	104.9

O2	0.00

O2 (1)	22.5

O2 (1∑)	37.5

O3	34.1

HO	9.3

HO2	2.8±0.5

H2O	-57.81

H2O2	-32.60

N	113.00

N2	0.00

NH	85.3

NH2	45.3±0.3

NH3	-10.98

NO	21.57

NO2	7.9

NO3	17.6±1

N2O	19.61

N2O3	19.8

N2O4	2.2

N2O5	2.7±1

HNO	25.6±1

HONO	-19.0

HNO3	-32.3

HO2NO2	-12.5±2

C	170.9

CH	142.0

CH2	93±1

CH3	35±0.2

CH4	-17.88

CN	104±3

HCN	32.3

CH3NH2	-5.5

NCO	38±3

HNCO	-25±3

CO	-26.42

CO2	-94.07

HCO	10±1

CH2O	-26.0

COOH	-53±2

HCOOH	-90.5

CH3O	4±1

CH3O2	4±2

CH2OH	-3.6±1

CH3OH	-48.2

CH3OOH	-31.3

CH3ONO	-15.6

CH3ONO2	-28.6

CH3O2NO2	-10.6±2

C2H	135±1

C2H2	54.35

C2H2OH	30±3

C2H3	71±1

C2H4	12.45

C2H5	28.4±0.5

C2H6	-20.0

CH2CN	58.5±3

CH3CN	18±3

CH2CO	-11±3

CH3CO	-2.4±0.5

CH3CHO	-39.7

C2H5O	-4.1±1

CH2CH2OH	-8±2

C2H5OH	-56.2

CH3CO2	-49.6

CH3COOH	-103.3

C2H5O2	-6±2

CH3COO2	-41±5

CH3OOCH3	-30.0

C3H5	39.4±2

C3H6	4.8

n-C3H7	22.6±2

i-C3H7	19±3

C3H8	-24.8

C2H5CHO	-44.8

CH3COCH3	-51.9

CH3COO2NO2	-62±5

F	19.0±0.1

F2	0.00

HF	-65.14±0.2

HOF	-23.4±1

FO	26±3

F2O	5.9±.4

FO2	6±1

F2O2	5±2

FONO	13±7

FNO	-16±2

FNO2	-26±2

FONO2	3.1±2

CF	61±2

CF2	-44±2

CF3	-112±1

CF4	-223.0

CHF3	-166.8

CHF2	-58±2

CH2F2	-108.2

CH2F	-8±2

CH3F	-56±1

FCO	-41±15

F2CO	-145±2

CF3O	-150±2

CF3O2	-148±2

CF3OH	-218±3

CF3OOCF3	-343±5

CF3OOH	-191±5

CF3OF	-173±5

CH3CHF	-17±2

CH3CH2F	-63±2

CH2FCH2F	-107±1

CH2FCHF2	-159±2

CHF2CHF2	-210±1

CH2CF3	-124±2

CH3CF3	-179±2

CH3CF2	-71±2

CH3CHF2	-120±1

CHFCF3	-163±2

CH2FCF3	-214±1

CF2CF3	-213±2

CHF2CF3	-264±2

Cl	28.9

Cl2	0.00

HCl	-22.06

ClO	24.4

ClOO	23.3±1

OClO	22.6±1

ClOO2	>16.7

ClO3	52±4

Cl2O	19.5±1

Cl2O2	31±3

Cl2O3	37±3

HOCl	-18±3

ClNO	12.4

ClNO2	3.0

ClONO	13

ClONO2	5.5

FCl	-12.1

CCl2	57±5

CCl3	17±1

CCl3O2	-2.7±1

CCl4	-22.9

CHCl3	-24.6

CHCl2	23±2

CH2Cl	29±2

CH2Cl2	-22.8

CH3Cl	-19.6

ClCO	-5±1

COCl2	-52.6

CHFCl	-15±2

CH2FCl	-63±2

CFCl	7±6

CFCl2	-22±2

CFCl3	-68.1

CF2Cl2	-117.9

CF3Cl	-169.2

CHFCl2	-68.1

CHF2Cl	-115.6

CF2Cl	-67±3

COFCl	-102±2

CH3CF2Cl	-127±2

CH2CF2Cl	-75±2

C2Cl4	-3.0

C2HCl3	-1.9

CH2CCl3	17±2

CH3CCl3	-34.0

CH3CH2Cl	-26.8

CH2CH2Cl	22±2

CH3CHCl	17.6±1

Br	26.7

Br2	7.39

HBr	-8.67

HOBr	-14±2

BrO	30±2

BrNO	19.7

BrONO	25±7

BrNO2	17±2

BrONO2	11

BrCl	3.5

CH2Br	40±2

CHBr3	6±2

CHBr2	45±2

CBr3	48±2

CH2Br2	-2.6±2

CH3Br	-8.5

CH3CH2Br	-14.8

CH2CH2Br	32±2

CH3CHBr	30±2

I	25.52

I2	14.92

HI	6.3

CH3I	3.5

CH2I	52±2

IO	30.5±2

INO	29.0

INO2	14.4

S	66.22

S2	30.72

HS	34.2±1

H2S	-4.9

SO	1.3

SO2	-70.96

SO3	-94.6

HSO	-1±2

HSO3	-92±2

H2SO4	-176

CS	67±2

CS2	28.0

CS2OH	26.4

CH3S	29.8±1

CH3SOO	18±2

CH3SO2	-57

CH3SH	-5.5

CH2SCH3	32.7±1

CH3SCH3	-8.9

CH3SSCH3	-5.8

OCS	-34

## APPENDIX 1:  GAS PHASE ENTHALPY DATA

SPECIES 	 ∆Hf(298)		SPECIES 	 ∆Hf(298)	SPECIES	 ∆Hf(298)	SPECIES	 ∆Hf(298)

(Kcal/mol)			(Kcal/mol)		(Kcal/mol)		(Kcal/mol)

H	52.1

H2	0.00

O	59.57

O(1D)	104.9

O2	0.00

O2 (1)	22.5

O2 (1∑)	37.5

O3	34.1

HO	9.3

HO2	2.8±0.5

H2O	-57.81

H2O2	-32.60

N	113.00

N2	0.00

NH	85.3

NH2	45.3±0.3

NH3	-10.98

NO	21.57

NO2	7.9

NO3	17.6±1

N2O	19.61

N2O3	19.8

N2O4	2.2

N2O5	2.7±1

HNO	25.6±1

HONO	-19.0

HNO3	-32.3

HO2NO2	-12.5±2

C	170.9

CH	142.0

CH2	93±1

CH3	35±0.2

CH4	-17.88

CN	104±3

HCN	32.3

CH3NH2	-5.5

NCO	38±3

HNCO	-25±3

CO	-26.42

CO2	-94.07

HCO	10±1

CH2O	-26.0

COOH	-53±2

HCOOH	-90.5

CH3O	4±1

CH3O2	4±2

CH2OH	-3.6±1

CH3OH	-48.2

CH3OOH	-31.3

CH3ONO	-15.6

CH3ONO2	-28.6

CH3O2NO2	-10.6±2

C2H	135±1

C2H2	54.35

C2H2OH	30±3

C2H3	71±1

C2H4	12.45

C2H5	28.4±0.5

C2H6	-20.0

CH2CN	58.5±3

CH3CN	18±3

CH2CO	-11±3

CH3CO	-2.4±0.5

CH3CHO	-39.7

C2H5O	-4.1±1

CH2CH2OH	-8±2

C2H5OH	-56.2

CH3CO2	-49.6

CH3COOH	-103.3

C2H5O2	-6±2

CH3COO2	-41±5

CH3OOCH3	-30.0

C3H5	39.4±2

C3H6	4.8

n-C3H7	22.6±2

i-C3H7	19±3

C3H8	-24.8

C2H5CHO	-44.8

CH3COCH3	-51.9

CH3COO2NO2	-62±5

F	19.0±0.1

F2	0.00

HF	-65.14±0.2

HOF	-23.4±1

FO	26±3

F2O	5.9±.4

FO2	6±1

F2O2	5±2

FONO	13±7

FNO	-16±2

FNO2	-26±2

FONO2	3.1±2

CF	61±2

CF2	-44±2

CF3	-112±1

CF4	-223.0

CHF3	-166.8

CHF2	-58±2

CH2F2	-108.2

CH2F	-8±2

CH3F	-56±1

FCO	-41±15

F2CO	-145±2

CF3O	-150±2

CF3O2	-148±2

CF3OH	-218±3

CF3OOCF3	-343±5

CF3OOH	-191±5

CF3OF	-173±5

CH3CHF	-17±2

CH3CH2F	-63±2

CH2FCH2F	-107±1

CH2FCHF2	-159±2

CHF2CHF2	-210±1

CH2CF3	-124±2

CH3CF3	-179±2

CH3CF2	-71±2

CH3CHF2	-120±1

CHFCF3	-163±2

CH2FCF3	-214±1

CF2CF3	-213±2

CHF2CF3	-264±2

Cl	28.9

Cl2	0.00

HCl	-22.06

ClO	24.4

ClOO	23.3±1

OClO	22.6±1

ClOO2	>16.7

ClO3	52±4

Cl2O	19.5±1

Cl2O2	31±3

Cl2O3	37±3

HOCl	-18±3

ClNO	12.4

ClNO2	3.0

ClONO	13

ClONO2	5.5

FCl	-12.1

CCl2	57±5

CCl3	17±1

CCl3O2	-2.7±1

CCl4	-22.9

CHCl3	-24.6

CHCl2	23±2

CH2Cl	29±2

CH2Cl2	-22.8

CH3Cl	-19.6

ClCO	-5±1

COCl2	-52.6

CHFCl	-15±2

CH2FCl	-63±2

CFCl	7±6

CFCl2	-22±2

CFCl3	-68.1

CF2Cl2	-117.9

CF3Cl	-169.2

CHFCl2	-68.1

CHF2Cl	-115.6

CF2Cl	-67±3

COFCl	-102±2

CH3CF2Cl	-127±2

CH2CF2Cl	-75±2

C2Cl4	-3.0

C2HCl3	-1.9

CH2CCl3	17±2

CH3CCl3	-34.0

CH3CH2Cl	-26.8

CH2CH2Cl	22±2

CH3CHCl	17.6±1

Br	26.7

Br2	7.39

HBr	-8.67

HOBr	-14±2

BrO	30±2

BrNO	19.7

BrONO	25±7

BrNO2	17±2

BrONO2	11

BrCl	3.5

CH2Br	40±2

CHBr3	6±2

CHBr2	45±2

CBr3	48±2

CH2Br2	-2.6±2

CH3Br	-8.5

CH3CH2Br	-14.8

CH2CH2Br	32±2

CH3CHBr	30±2

I	25.52

I2	14.92

HI	6.3

CH3I	3.5

CH2I	52±2

IO	30.5±2

INO	29.0

INO2	14.4

S	66.22

S2	30.72

HS	34.2±1

H2S	-4.9

SO	1.3

SO2	-70.96

SO3	-94.6

HSO	-1±2

HSO3	-92±2

H2SO4	-176

CS	67±2

CS2	28.0

CS2OH	26.4

CH3S	29.8±1

CH3SOO	18±2

CH3SO2	-57

CH3SH	-5.5

CH2SCH3	32.7±1

CH3SCH3	-8.9

CH3SSCH3	-5.8

OCS	-34

## APPENDIX 2:  GAS PHASE ENTROPY DATA

SPECIES 	So(298)	SPECIES 	So(298)	SPECIES	 So(298)	SPECIES	 So(298)

(cal/mol/deg)	(cal/mol/deg)	(cal/mol/deg)                                  (cal/mol/deg)

H	27.4

H2	31.2

O	38.5

O2	49.0

O3	57.0

HO	43.9

HO2	54.4

H2O	45.1

H2O2	55.6

N	36.6

N2	45.8

NH	43.3

NH2	46.5

NH3	46.0

NO	50.3

NO2	57.3

NO3	60.3

N2O	52.6

N2O3	73.9

N2O4	72.7

N2O5	82.8

HNO	52.7

HONO	59.6

HNO3	63.7

HO2NO2	(72)

C	37.8

CH	43.7

CH2	46.3

CH3	46.4

CH4	44.5

CN	48.4

HCN	48.2

CH3NH2	58.0

HNCO	56.9

NCO	55.5

CO	47.3

CO2	51.1

HCO	53.7

CH2O	52.3

COOH	61.0

HCOOH	59.4

CH3O	55.0

CH3O2	65.3

CH2OH	58.8

CH3OH	57.3

CH3OOH	67.5

CH3ONO	68.0

CH3ONO2	72.1

CH3O2NO2	(82)

C2H	49.6

C2H2	48.0

C2H3	56.3

C2H4	52.5

C2H5	58.0

C2H6	54.9

CH2CN	58.0

CH3CN	58.2

CH2CO	57.8

CH3CO	64.5

CH3CHO	63.2

C2H5O	65.3

C2H5OH	67.5

CH3CO2	(68)

CH3COOH	67.5

C2H5O2	75.0

CH3COO2	(80)

CH3OOCH3	74.1

C3H5	62.1

C3H6	63.8

n-C3H7	68.5

i-C3H7	66.7

C3H8	64.5

C2H5CHO	72.8

CH3COCH3	70.5

CH3COO2NO2	(95)

F	37.9

F2	48.5

HF	41.5

HOF	54.2

FO	51.8

F2O	59.1

FO2	61.9

F2O2	66.3

FONO	62.2

FNO	59.3

FNO2	62.3

FONO2	70.0

CF	50.9

CF2	57.5

CF3	63.3

CF4	62.4

CH3F	53.3

CH2F	55.9

CH2F2	58.9

CHF2	61.7

CHF3	62.0

FCO	59.4

COF2	61.9

CF3O	67.7

CF3O2	75.0

CF3OH	69.3

CF3OOH	75.2

CF3OF	77.1

CH3CH2F	63.3

CH3CHF	(64)

CH3CHF2	67.6

CH3CF2	69.9

CH3CF3	68.6

CH2CF3	71.8

CH2FCF3	75.8

CHF2CF3	(80)

CF2CF3	81.6

FCl	52.1

CH2FCl	63.3

CHFCl	(63)

CFCl	62.0

CFCl3	74.0

CF2Cl2	71.8

CF3Cl	68.3

CHFCl2	70.1

CFCl2	71.5

CHF2Cl	67.2

CF2Cl	68.7

COFCl	66.2

CH3CF2Cl	68.7

CH2CF2Cl	(69)

Cl	39.5

Cl2	53.3

HCl	44.6

ClO	54.1

ClOO	64.0

OClO	61.5

ClOO2	73

Cl2O	64.0

Cl2O2	72.2

HOCl	56.5

ClNO	62.6

ClNO2	65.1

ClONO	(70)

ClONO2	(74)

FCl	52.1

CCl2	63.4

CH3Cl	56.1

CH2Cl	58.2

CH2Cl2	64.6

CHCl2	66.5

CHCl3	70.7

CCl3	71.0

CCl4	74.0

ClCO	63.5

COCl2	67.8

C2Cl4	81.4

C2HCl3	77.5

CH2CCl3	80.6

CH3CCl3	76.4

CH3CH2Cl	65.9

CH2CH2Cl	(66)

CH3CHCl	(66)

CHCl2CF3	84.0

Br	41.8

Br2	58.6

HBr	47.4

HOBr	59.2

BrO	56.8

BrNO	65.3

BrONO	(72)

BrNO2	(67)

BrONO2	(77)

BrCl	57.3

CH3Br	58.7

CH2Br	(61)

CH2Br2	70.1

CHBr2	(72)

CHBr3	79.1

CBr3	80.0

CH3CH2Br	68.6

CH2CH2Br	(70)

CH3CHBr	(70)

I	43.2

I2	62.3

HI	49.3

CH3I	60.6

CH2I	(61)

IO	58.8

INO	67.6

INO2	70.3

S	40.1

S2	54.5

H2S	49.2

HS	46.7

SO	53.0

SO2	59.3

SO3	61.3

H2SO4	69.1

CS	50.3

CS2	56.9

CH3SH	61.0

CH3S	57.6

CH3SO2	(62)

CH3SCH3	68.4

CH2SCH3	(69)

CH3SSCH3	80.5

OCS	55.3

## APPENDIX 3:   SOLAR FLUXES AND SPECIES  PROFILES

Figures 6 and 7 show data for solar irradiances and fluxes.  These were  provided by Kenneth Minschwaner. The solar irradiances are from measurements by the Solar Ultraviolet Spectral Irradiance Monitor (SUSIM) for ≤ 400 nm (VanHoosier et al. [6]), and by Neckel and Labs [5] for 400 <  ≤ 600 nm.  The SUSIM measurements are spectrally degraded to 2 nm full width half-maximum to correspond to the resolution of the Neckel and Labs data.  Additionally, a normalization factor that varies linearly from 1.17 at 400 nm to 1.0 at 440 nm has been applied to the Neckel and Labs irradiances in order to match SUSIM values at 400 nm.  Irradiances from 110 to 120 nm are based on measurements by Mount and Rottman [4] and Woods and Rottman [8].  Values below 110 nm are not plotted.

The solar fluxes are computed from the sum of the direct, attenuated solar beam plus angularly integrated scattered radiation.  Fluxes at 0, 20, 30, 40, and 50 km are based on the solar irradiances, assuming a solar zenith angle of 30° and the U.S. Standard Atmosphere (1976).  Molecular and aerosol scattering are taken into account; the latter process is appropriate for "moderate volcanic" conditions (Fenn et al. [2]).  The surface albedo is 0.3.  Ozone cross sections follow the recommendations herein; oxygen cross sections in the Herzberg continuum are taken from Yoshino et al. [9]; Schumann-Runge band absorption is determined using the high-resolution treatment of Minschwaner et al. [3], with fluxes spectrally degraded to 1.0 nm resolution.

The species and "J" value profiles presented in Figures  8-16 were provided by Peter Connell.  They were generated by the LLNL 2-D model of the troposphere and stratosphere.  The temperature profile is an interpolation to climatological values.  Surface source gas boundary conditions are those for the year 1990, as reported in chapter 6 of the WMO/UNEP report [7].  The equatorial tropopause source gas mixing ratios are: total chlorine 3.4 ppb, total fluorine 1.6 ppb, total bromine 18 ppt, methane 1.67 ppm, and nitrous oxide 309 ppb.  The kinetic parameters used were consistent, to the extent possible, with the current recommendations.  Representations of sulfate aerosol and polar stratospheric heterogeneous processes which were included are hydrolysis of nitrogen pentoxide and chlorine and bromine nitrate and reaction of hydrogen chloride with chlorine nitrate and hypochlorous acid.  The model run represents a periodic steady-state atmosphere with 1990 surface abundances of source gases.

The "J" values were calculated with a clear sky, two-stream radiative transfer model with wavelength binning of 5 nm above 310 nm and 500 cm-1 below.  Surface reflectance includes the effect of average cloudiness on the albedo.  Oxygen cross sections in the Schumann-Runge region were calculated by the method of Allen and Frederick [1], corrected for the Herzberg continuum values of Yoshino et al. [9].

The fluxes and profiles are given to provide "order of magnitude" values of important photochemical parameters.  They are not intended to be standards or recommended values.

References

1.	Allen, M. and J.E. Frederick, 1982, J. Atmos. Sci., 39, 2066-2075.

2.	Fenn, W.R., S.A. Clough, W.O. Gallery, R.E. Good, F.X. Kneizys, J.D. Mill, L.S. Rothman, E.P. Shettle, and F.E. Volz, 1985, "Optical and Infrared Properties of the Atmosphere," Handbook of Geophysics and the Space Environment, Chapter 18, A.S. Jursa, Editor,   Air Force Geophysics Laboratory,  Bedford, MA.

3.	Minschwaner, K., G.P. Anderson, L.A. Hall, and K. Yoshino, 1992, J. Geophys. Res., 97, 10103-10108.

4.	Mount, G.H. and G.J. Rottman, 1985, J. Geophys. Res., 90, 13031-13036.

5.	Neckel, H. and D. Labs, 1984, Solar Physics, 90, 205-258.

6.	VanHoosier, M.E., J.-D.F. Bartoe, G.E. Brueckner, and D.K. Prinz, 1988, Astro. Lett. and Communications, 27, 163-168.

7.	WMO, Scientific Assessment of Ozone Depletion: 1994,  World Meteorological Organization Global Ozone Research and Monitoring Project, Report No. 37, 1994, Geneva: National Aeronautics and Space Administration.

8.	Woods, T.N. and G.J. Rottman, 1990, J. Geophys. Res., 95, 6227-6236.

9.	Yoshino, K., A.S.C. Cheung, J.R. Esmond, W.H. Parkinson, D.E. Freeman, S.L. Guberman, A. Jenouvrier, B. Coquart, and M.F. Merienne, 1988, Planet. Space Sci., 36, 1469-1475.

Figure 6.  Solar Irradiance

Figure 7.  Actinic Flux at Several Altitudes

Figure 8.  Temperature and Density

Figure 9.  Number Densities of Oxygen and Hydrogen Species

Figure 10.  Number Densities of Nitrogen Species

Figure 11.  Number Densities of Chlorine Species

Figure 12.  Number Densities of CFCl3, CF2Cl2, and CO

Figure 13.  J-Values for O2 and H2O

Figure 14.  Selected J-Values

Figure 15.  Selected J-Values

Figure 16.  Selected J-Values